## Slide 1: rfc6326bis
Donald E. Eastlake, 3rd
d3e3e3@gmail.com
+1-508-333-2270

## Slide 2: rfc6326bis
draft-eastlake-isis-rfc6326bis-08.txt
RFC 6326 “TRILL use of IS-IS” is based on the TRILL protocol in RFC 6325, which was passed up to the IESG in September 2009, almost 3 years ago.

## Slide 3: Changes
Categories of Changes
  Multicast Group sub-TLVs
  Clarifications
  Robustness
  Capabilities Announcement
  Other Extensions
  IANA Considerations

## Slide 4: Multicast Group sub-TLVs
Existing: VLAN scoped MAC addresses
Added:
  VLAN scoped
    IPv4, IPv6
  Fine Grained label scoped
    MAC, IPv4, IPv6

## Slide 5: Clarifications
Handling of invalid VLAN IDs in two sub-TLVs
Zero sources implies (*,G) multicast listener
Fix Errata: Type for Group Address TLV was wrongly given as 10 in one place (it’s 142).

## Slide 6: Robustness
Require that LSP number zero be no larger than 1470 bytes and contain any originatingLSPBufferSize TLV.

## Slide 7: Capability Announcement
Expand Existing TRILL-VER sub-TLV value with 32 flag bits
Add PORT-TRILL-VER sub-TLV with TRILL version and 32 flags bits
RBridge Channel Protocols supported sub-TLV

## Slide 8: Other Extensions
Tree Affinity sub-TLV: Ability for an RBridge to specify a child node in listed trees
Ability to express SNPA size other than 6 bytes in TRILL Neighbor TLV
Size of Source ID fields in MTU PDUs specified as ID length from IS-IS PDU Header rather than the fixed value 6

## Slide 9: Other Extensions (cont.)
For two existing sub-TLVs, add fine grained label versions :
  Interested Labels and Spanning Tree Roots
  Label Group

## Slide 10: IANA Considerations
Add sub-registries for
  Capability bits in TRILL VER sub-TLVs
  TRILL Neighbor TLV Neighbor RECORD flag bits

## Slide 11: END
Donald E. Eastlake, 3rd
d3e3e3@gmail.com
+1-508-333-2270