## Slide 1: Fine Grained Labeling draft-ietf-trill-fine labeling-01.txt
Donald E. Eastlake 3rd
Huawei Technologies
d3e3e3@gmail.com

## Slide 2: Fine Grained Labeling
Current protocol data frame:
Link Header
TRILL Header
VLAN Label
Dest Addr
Src Addr
Link Trailer
Payload
E T
E T
C-VLAN 8100
12-bit VLAN ID
Pri DEI

## Slide 3: Fine Grained Labeling
Multi-tenant applications require substantially more than the 2**12 – 2 isolatable data labels provided by VLANs
Current fine grained labeling draft can provide approaching 2**24 labels

## Slide 4: Fine Grained Labeling
Current fine grained label draft:
Link Header
TRILL Header
Initial Tag
Dest Addr
Src Addr
Link Trailer
Payload
E T
E T
8100
FGL Upper Part
Pri DEI
Ext Tag
E T
Backwards compatible for transit TRILL switches
893B
FGL Lower Part
Pri DEI
Priority/DEI in TRILL campus
Ingress priority/DEI, restored on egress

## Slide 5: Fine Grained Labeling
The current fine grained labeling frame format was brought up at the IETF and IEEE 802 Leadership meeting last week with the objection that it uses 0x8100 with a different semantic than the 0x8100 Ethertype.
People seemed to be indicating that the use of a 16-bit quantity other than 0x8100 would solve this problem.

## Slide 6: Fine Grained Labeling
Example solution 1:
Link Header
TRILL Header
Initial Tag
Dest Addr
Src Addr
Link Trailer
Payload
E T
E T
893B
FGL Upper Part
Pri DEI
Ext Tag
E T
893B
FGL Lower Part
Pri DEI
Priority/DEI in TRILL campus
Ingress priority/DEI, restored on egress
More compatible with existing hardware

## Slide 7: Fine Grained Labeling
Example solution 2:
Link Header
TRILL Header
TRILL Label
Dest Addr
Src Addr
Link Trailer
Payload
E T
E T
893B
24-bit Label
P r i
P r i
Ingress priority/DEI, restored on egress
Priority/DEI in TRILL campus
More compact