## Slide 1: RSVP App-ID Profiles at IETF84
draft-polk-tsvwg-rsvp-app-id-vv-profiles-04
1 August 2012
James Polk
Subha Dhesikan

## Slide 2: Scope of ID
Purpose – differentiate what traffic type is carried in each reservation
Create registered profiles using RFC 2872 RSVP Application-ID Object for each real-time traffic class defined within RFC 4594 (which is being updated now)

## Slide 3: RSVP APP-ID Object Template
The template from RFC 2872 is as follows:
0 1 2 3
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PE Length (8) | P-type = AUTH_APP |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Attribute Length | A-type = | Sub-type = |
| | POLICY_LOCATOR| ASCII_DN |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Application policy locator attribute data in X.500 DN format |
| (see below) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Creates a profile that includes the following pieces of information:
“P-type = , A-type = , Sub-type = , GUID= , APP= , VER= “
The Broadcast Video Surveillance Profile
APP_TC, POLICY_LOCATOR, ASCII_DN,
"GUID=http://www.ietf.org/internet-drafts/
draft-ietf-mmusic-traffic-class-for-sdp-01.txt,
APP=broadcast.video.surveillance, VER="

## Slide 4: Profiles in the Draft
Broadcast Profiles
Broadcast IPTV for audio and video
Broadcast Live-events for audio and video
Broadcast Surveillance for audio and video
Realtime-Interactive Profiles
Realtime-Interactive Gaming
Realtime-Interactive Remote-Desktop
Realtime-Interactive Virtualized-Desktop
Multimedia-Conferencing Profiles
Multimedia-Conferencing presentation-data
Multimedia-Conferencing application-sharing
Multimedia-Conferencing whiteboarding

## Slide 5: Profiles in the Draft
Multimedia-Streaming Profiles
Multimedia-Streaming multiplex
Multimedia-Streaming webcast
Conversational Profiles
Conversational Audio
Conversational Audio Admitted
Conversational Video
Conversational Video Admitted
Conversational Audio Avconf
Conversational Audio Avconf Admitted
Conversational Video Avconf
Conversational Video Avconf Admitted
Conversational Audio Immersive
Conversational Audio Immersive Admitted
Conversational Video Immersive
Conversational Video Immersive Admitted

## Slide 6: Fixed Open issues in this Version
clarified security considerations section to mean RSVP cannot police the type of traffic within a reservation to know if a traffic flow should be using a different profile, as defined in this document.
changed existing informative language regarding "... other Sub-types ..." from 'can' to normative 'MAY'.
editorial changes to clear up minor mistakes.

## Slide 7: New Open issues
  Addressed all issues pointed out by two recent reviews
  No other known open issues
  MMUSIC is waiting on this WG to progress this draft before moving forward with
    draft-ietf-mmusic-traffic-class-for-sdp

## Slide 8: Next steps
Chairs said get two full reviews to the list and would consider for WG item.
  DONE
Can there be another hum to adopt this draft?
  First in Beijing, with no one against