## Slide 1: DiffServ Standards Problem Statement
draft-polk-tsvwg-diffserv-stds-problem-statement-00
1 August 2012
James Polk

## Slide 2: Purpose of Draft
Create discussion to resolve various issues wrt perception of DiffServ usage and guidance.
Scope of this effort is wide, so some things to remember:
The IETF is only for SPs (not true).
The only considerations to be contemplated at IETF are expressed live, and about ‘their’ network (again, not true).
New things that require interoperability and “do no harm” (true).

## Slide 3: Why This and Why Now
Migrate towards consistency on many common traffic types over time.
  Certainly not for all traffic types
  Certainly not against internal policies for internal traffic
Applications becoming more and more involved in QoS/CoS, and there are more and more of them behave slightly differently.
  More vendors building applications and/or endpoints *without* this in mind.
While flexibility from RFC 2474/5 is great, reality is difficult to manage.

## Slide 4: DiffServ Standards (by DSCP)
RFC 2474 - CS0, CS1, CS2, CS3, CS4, CS5, CS6, CS7
RFC 2597 - AF1x, AF2x, AF3x, and AF4x
RFC 3246 - EF (101110)
RFC 5865 - VOICE-ADMIT (101100)
EF and VOICE-ADMIT have defined forwarding behavior per hop (called a Per Hop Behavior (PHB))
AF has defined behavior only wrt adjacent other 2 in group per hop (i.e., AF4x only affecting other AF4x, etc)
No other defined behaviors…. Until RFC 4594.

## Slide 5: Confusion about DiffServ (1/2)
confusion between RFC 4594 and RFC 5127, the latter of which is for aggregating many 6-bit DSCP values into a 3-bit (8 value) field used specifically by service provider (SP) networks.
some believe both RFCs are for SPs, while others ignore RFC 5127 and use RFC 4594 as if it were standards track or BCP.
some believe RFC 5127 is for SPs only, and want RFC 4594 to reduce the number of DSCPs within its guidelines to recommend using only 3 or 4 DSCPs. This seems to stem from a manageability and operational perspective.

## Slide 6: Confusion about DiffServ (2/2)
some know RFC 4594 is informational and do not follow its guidelines specifically because it is informational.
some use DSCP values that are not defined within RFC 4594, making mapping between different networks using similar or identical application flows difficult.
some believe enterprise networks should not use either RFC except at the edge of their networks, where they directly connect to SP networks.
some argue that the services class guidance per class is too broad and are therefore not sure in which service class a particular application is to reside.

## Slide 7: Service Classes defined in RFC 4594
12 service classes utilizing one or more DSCPs:
Network Control Broadcast Video
Telephony Low-Latency Data
Signaling OAM
Multimedia Conferencing High-throughput Data
Realtime Interactive Standard
Multimedia Streaming Low-priority Data

## Slide 8: Service Classes defined in RFC 4594-Update
14 service classes utilizing one or more DSCPs:
Network Control Broadcast
Audio Low-Latency Data
Video Convo. Signaling
Hi-Res OAM
Multimedia Conferencing High-throughput Data
Realtime Interactive Standard
Multimedia Streaming Low-priority Data

## Slide 9: Service Class vs. Treatment Aggregate
RFC 4594 defines “Service Class”
RFC 5127 defines “Treatment Aggregate”
Per RFC 5127: one or more Service classes are placed into a Treatment Aggregate

## Slide 10: RFC 5127 Treatment Aggregate Behavior
------------------------------------------------------------
|Treatment |Treatment || DSCP |
|Aggregate |Aggregate || |
| |Behavior || |
|==========+==========++=====================================|
| Network | CS || CS6 |
| Control |(RFC 2474)|| |
|==========+==========++=====================================|
| Real- | EF || EF, CS5, AF41, AF42, AF43, CS4, CS3 |
| Time |(RFC 3246)|| |
|==========+==========++=====================================|
| Assured | AF || CS2, AF31, AF21, AF11 |
| Elastic |(RFC 2597)||-------------------------------------|
| | || AF32, AF22, AF12 |
| | ||-------------------------------------|
| | || AF33, AF23, AF13 |
|==========+==========++=====================================|
| Elastic | Default || Default, (CS0) |
| |(RFC 2474)||-------------------------------------|
| | || CS1 |
------------------------------------------------------------

## Slide 11: RFC 5127 Treatment Aggregate Behavior
------------------------------------------------------------
|Treatment |Treatment || DSCP |
|Aggregate |Aggregate || |
| |Behavior || |
|==========+==========++=====================================|
| Network | CS || CS6 |
| Control |(RFC 2474)|| |
|==========+==========++=====================================|
| Real- | EF || EF, CS5, AF41, AF42, AF43, CS4, CS3 |
| Time |(RFC 3246)|| |
|==========+==========++=====================================|
| Assured | AF || CS2, AF31, AF21, AF11 |
| Elastic |(RFC 2597)||-------------------------------------|
| | || AF32, AF22, AF12 |
| | ||-------------------------------------|
| | || AF33, AF23, AF13 |
|==========+==========++=====================================|
| Elastic | Default || Default, (CS0) |
| |(RFC 2474)||-------------------------------------|
| | || CS1 |
------------------------------------------------------------
- So, where does RFC 5865 defined VOICE-ADMIT go?
- Can all proposed capacity-admitted service classes go into the same treatment aggregate?

## Slide 12: Next Steps
If RFC 4594 update is an acceptable effort (at least the direction of it), need to update RFC 5127 to make both consistent.

## Slide 13: Open Issues
React to comments and questions about the update draft…