## Slide 1: Standard Configuration of DiffServ Service Classes at IETF84
draft-polk-tsvwg-rfc4594-update-01.txt
draft-polk-tsvwg-new-dscp-assignments-00.txt
1 August 2012
James Polk (editor)

## Slide 2: Purpose of the drafts
To specify DiffServ service class traffic characteristics, with associated DSCP name and value
First draft proposes to obsolete RFC 4594
Also proposed currently as standards track
Second draft merely creates the new DiffServ values needed by the update draft
NOTE: RFC 5127 is for Aggregating Service Classes

## Slide 3: Particulars within RFC 4594 update
Built on text from RFC 4594 (from this WG)
Updates to included Voice-Admit from RFC 5865
Adds several more Capacity Admitted Service classes for
  (newly modified) Realtime-Interactive
  Broadcast
  (new) Hi-Res service class
  (newly modified) Multimedia-Conferencing
Also adds non-capacity-admitted service classes:
  (newly modified) Multimedia-Conferencing
  (newly modified) Conversational Signaling

## Slide 4: Particulars within RFC 4594 update
Differences of traffic characteristics between service classes requires too much time for this preso…
  … but I’ll try
  Please read the draft for these details
  If you don’t fall asleep, send mail to the list if you have comments.

## Slide 5: List of Service Classes Unchanged
Multimedia-Streaming
  Remains the same
High-Throughput Data
  Remains the same
Low-Priority Data
  Remains the same
Default Forwarding
  Remains the same
Network Routing
  Remains the same
OAM
  Remains the same

## Slide 6: List of Service Classes Modified or New
Realtime-Interactive
  Moved to (near) realtime TCP-based apps
Audio
  Same as Telephony (which is now gone), adds Voice-Admit for capacity-admitted traffic
Video
  NEW for video and audio/video conferencing, was in Multimedia-Conferencing
Hi-Res
  NEW for video and audio/video conferencing
Multimedia-Conferencing
  Now without audio or human video
Broadcast
  Remains the same, added CS3-Admit for capacity-admitted
Low-Latency Data
  Remains the same, adds IM & Presence traffic explicitly
Conversational Signaling
  Was ‘Signaling’
Now “Conversational” traffic classes

## Slide 7: New Figure 1. User/Subscriber Service Classes Grouping
+-----------------------------------------------------------------+
| Application | Service | Signaled | Flow | G.1010 |
| Categories | Class | | Behavior | Rating |
|-------------+---------------+----------+-----------+------------|
| Application | A/V Sig | Not | Inelastic | Responsive |
| Control | |applicable| | |
|-------------+---------------+----------+-----------+------------|
| | Real-Time | Yes | Inelastic | Interactive|
| | Interactive | | | |
| |---------------+----------+-----------+------------|
| | Audio | Yes | Inelastic | Interactive|
| |---------------+----------+-----------+------------|
| | Video | Yes | Inelastic | Interactive|
| |---------------+----------+-----------+------------|
| | Hi-Res | Yes | Inelastic | Interactive|
| |---------------+----------+-----------+------------|
| Media- | Multimedia | Yes | Rate | Moderately |
| Oriented | Conferencing| | Adaptive | Interactive|
| |---------------+----------+-----------+------------|
| | Broadcast | Yes | Inelastic | Responsive |
| |---------------+----------+-----------+------------|
| | Multimedia | Yes | Elastic | Timely |
| | Streaming | | | |
|-------------+---------------+----------+-----------+------------|
| | Low-Latency | No | Elastic | Responsive |
| | Data | | | |
| |---------------+----------+-----------+------------|
| Data | High- | No | Elastic | Timely |
| |Throughput Data| | | |
| |---------------+----------+-----------+------------|
| | Low- | No | Elastic |Non-critical|
| | Priority Data | | | |
|-------------+---------------+----------+-----------+------------|
| Best Effort | Standard | Not Specified |Non-critical|
+-----------------------------------------------------------------+

## Slide 8: New Figure 2. Service Class Characteristics (1/2)
+-------------------------------------------------------------------+
|Service Class | | Tolerance to |
| Name | Traffic Characteristics | Loss |Delay |Jitter|
|===============+==============================+======+======+======|
| Network |Variable size packets, mostly | | | |
| Control |inelastic short messages, but | Low | Low | Yes |
| |traffic can also burst (BGP) | | | |
|---------------+------------------------------+------+------+------|
| Real-Time | Inelastic, mostly variable | Low | Very | Low |
| Interactive | rate | | Low | |
+---------------+------------------------------+------+------+------+
| | Variable-size small packets, | Very | Very | Very |
| Audio | inelastic | Low | Low | Low |
| | | | | |
+---------------+------------------------------+------+------+------+
| | Bursty, small-large packets | Very | Very | Very |
| Video | inelastic | Low | Low | Low |
| | | | | |
+---------------+------------------------------+------+------+------+
| | Bursty, small-large packets | Very | Very | Very |
| Hi-Res A/V | inelastic | Low | Low | Low |
| | | | | |
+---------------+------------------------------+------+------+------+

## Slide 9: New Figure 2. Service Class Characteristics (2/2)
+-------------------------------------------------------------------+
|Service Class | | Tolerance to |
| Name | Traffic Characteristics | Loss |Delay |Jitter|
|===============+==============================+======+======+======|
| Multimedia | Variable size packets, | Low | Low | Low |
| Conferencing | constant transmit interval, | - | - | - |
| | rate adaptive, reacts to loss|Medium|Medium|Medium|
+---------------+------------------------------+------+------+------+
| Multimedia | Variable size packets, |Low - |Medium| High |
| Streaming | elastic with variable rate |Medium| | |
+---------------+------------------------------+------+------+------+
| Broadcast | Constant and variable rate, | Very |Medium| Low |
| | inelastic, non-bursty flows | Low | | |
+---------------+------------------------------+------+------+------+
| Low-Latency | Variable rate, bursty short- | Low |Low - | Yes |
| Data | lived elastic flows | |Medium| |
|---------------+------------------------------+------+------+------+
|Conversational | Variable size packets, some | Low | Low | Yes |
| Signaling | what bursty short-lived flows| | | |
|---------------+------------------------------+------+------+------+
| OAM | Variable size packets, | Low |Medium| Yes |
| | elastic & inelastic flows | | | |
|---------------+------------------------------+------+------+------+
| High- | Variable rate, bursty long- | Low |Medium| Yes |
|Throughput Data| lived elastic flows | |- High| |
|---------------+------------------------------+------+------+------+
| Standard | A bit of everything | Not Specified |
|---------------+------------------------------+------+------+------+
| Low-Priority | Non-real-time and elastic | High | High | Yes |
| Data | | | | |
+-------------------------------------------------------------------+

## Slide 10: New Figure 3. DSCP to Service Class Mapping (1/2)
+------------------------------------------------------------------+
| Service | DSCP | DSCP | Application |
| Class Name | Name | Value | Examples |
|===============+=========+=============+==========================|
|Network Control| CS6&CS7 | 11xxxx | Network routing |
|---------------+---------+-------------+--------------------------|
| Real-Time | CS5, | 101000, | Remote/Virtual Desktop |
| Interactive |CS5-Admit| 101001 | and Interactive gaming |
|---------------+---------+-------------+--------------------------|
| Audio | EF | 101110 | Voice bearer |
| |Voice-Admit| 101100 | |
|---------------+---------+-------------+--------------------------|
| Hi-Res A/V | CS4, | 100000, | Conversational Hi-Res |
| |CS4-Admit| 100001 | Audio/Video bearer |
|---------------+---------+-------------+--------------------------|
| Video |AF41,AF42|100010,100100| Audio/Video conferencing |
| | AF43 | 100110 | bearer |
|---------------+---------+-------------+--------------------------|
| Multimedia | MC, | 011101, | Presentation Data and |
| Conferencing | MC-Admit| 100101 | App Sharing/Whiteboarding|
|---------------+---------+-------------+--------------------------|

## Slide 11: New Figure 3. DSCP to Service Class Mapping (2/2)
+------------------------------------------------------------------+
| Service | DSCP | DSCP | Application |
| Class Name | Name | Value | Examples |
|===============+=========+=============+==========================|
| Multimedia |AF31,AF32|011010,011100| Streaming video and |
| Streaming | AF33 | 011110 | audio on demand |
|---------------+---------+-------------+--------------------------|
| Broadcast | CS3, | 011000, | Broadcast TV, live events|
| |CS3-Admit| 011001 | & video surveillance |
|---------------+---------+-------------+--------------------------|
| Low-Latency |AF21,AF22|010010,010100|Client/server trans., Web-|
| Data | AF23 | 010110 |based ordering, IM/Pres |
|---------------+---------+-------------+--------------------------|
|Conversational | A/V-Sig | 010001 | Conversational signaling |
| Signaling | | | |
|---------------+---------+-------------+--------------------------|
| OAM | CS2 | 010000 | OAM&P |
|---------------+---------+-------------+--------------------------|
|High-Throughput|AF11,AF12|001010,001100| Store and forward |
| Data | AF13 | 001110 | applications |
|---------------+---------+-------------+--------------------------|
| Low-Priority | CS1 | 001000 | Any flow that has no BW |
| Data | | | assurance |
|------------------------------------------------------------------|
| Best Effort | CS0 | 000000 | Undifferentiated |
| | | | applications |
+---------------+---------+-------------+--------------------------+

## Slide 12: New Figure 4. Summary of CoS Mechanisms Used for Each Service Class (1/2)
+-----------------------------------------------------------------+
| Service | DSCP | Conditioning at | PHB | Queuing| AQM|
| Class | | DS Edge | Used | | |
|===============+=======+===================+=======+========+====|
|Network Control|CS6/CS7| See Section 3.1 |RFC2474| Rate | Yes|
|---------------+-------+-------------------+-------+--------+----|
| Real-Time | CS5, |Police using sr+bs |RFC2474| Rate | No |
| Interactive | CS5- | | | | |
| | Admit*| |[ID-DSCP]| | |
|---------------+-------+-------------------+-------+--------+----|
| | EF, |Police using sr+bs |RFC3246|Priority| No |
| Audio |Voice- | | | | |
| | Admit*| |RFC5865| | |
|---------------+-------+-------------------+-------+--------+----|
| | CS4, |Police using sr+bs |RFC2474|Priority| No |
| Hi-Res A/V | CS4- | | | | |
| | Admit*| |[ID-DSCP]| | |
|---------------+-------+-------------------+-------+--------+----|
| | AF41*,| Using two-rate, | | | Yes|
| Video | AF42 |three-color marker |RFC2597| Rate | per|
| | AF43 | (such as RFC 2698)| | |DSCP|
|---------------+-------+-------------------+-------+--------+----|
| Multimedia | MC, |Police using sr+bs|[ID-DSCP]| Rate | No |
| Conferencing | MC- | | | | |
| | Admit*| |[ID-DSCP]| | |
|---------------+-------+-------------------+-------+--------+----|

## Slide 13: New Figure 4. Summary of CoS Mechanisms Used for Each Service Class (2/2)
+-----------------------------------------------------------------+
| Service | DSCP | Conditioning at | PHB | Queuing| AQM|
| Class | | DS Edge | Used | | |
|===============+=======+===================+=======+========+====|
| Multimedia | AF31*,| Using two-rate, | | | Yes|
| Streaming | AF32 |three-color marker |RFC2597| Rate | per|
| | AF33 | (such as RFC 2698)| | |DSCP|
|---------------+-------+-------------------+-------+--------+----|
| Broadcast | CS3, |Police using sr+bs |RFC2474| Rate | No |
| | CS3- | | | | |
| | Admit*| |[ID-DSCP]| | |
|---------------+-------+-------------------+-------+--------+----|
| Low- | AF21 | Using single-rate,| | | Yes|
| Latency | AF22 |three-color marker |RFC2597| Rate | per|
| Data | AF23 | (such as RFC 2697)| | |DSCP|
|---------------+-------+-------------------+-------+--------+----|
|Conversational |AV-Sig |Police using sr+bs|[ID-DSCP]| Rate | No |
| Signaling | | | | | |
|---------------+-------+-------------------+-------+--------+----|
| OAM | CS2 |Police using sr+bs |RFC2474| Rate | Yes|
|---------------+-------+-------------------+-------+--------+----|
| High- | AF11 | Using two-rate, | | | Yes|
| Throughput | AF12 |three-color marker |RFC2597| Rate | per|
| Data | AF13 | (such as RFC 2698)| | |DSCP|
|---------------+-------+-------------------+-------+--------+----|
| Standard | DF | Not applicable |RFC2474| Rate | Yes|
|---------------+-------+-------------------+-------+--------+----|
| Low-Priority | CS1 | Not applicable |RFC3662| Rate | Yes|
| Data | | | | | |
|---------------+-------+-------------------+-------+--------+----|

## Slide 14: Open Issues
Incorporated “service class vs. treatment aggregate” into doc (section 2.4), but didn’t mention that in the intro section, which is needed.
Need to solidify on the ‘audio’, ‘video’ and ‘Hi-Res’ service class names.
Other minor edits to make clearer…

## Slide 15: What’s Next?
Need more reviewers and comments
If Problem Statement draft is valid, need to incorporate some of it into Section 1 of this draft.
Solid enough to become a WG item?