## Slide 1: Liaison to Transport Area WG: “Development of Informative Codepoint mapping in ITU-T Study Group 12”
Al Morton, Rapporteur of Question 17 on Performance of packet-based networks
https://datatracker.ietf.org/liaison/1165/
Notes: 16.04.2009
<number>
Autor / Thema der Präsentation

## Slide 2: What’s all this about? Q17’s work to improve interconnection between Service Providers now in a Recommendation
<number>
Y.1566 “QoS mapping and interconnection between Ethernet, IP and MPLS Networks”
  formerly Y.QoSMap, informal name still appears in places
  Describes Classes: qualitative performance char. & apps
    4 Ordinary (~every SP has them) and 4 Auxiliary (3-bit code space)
    Similar to Treatment Agg. in RFC 5127 or Per-Domain Behaviors
  NO normative codepoint to Class assignment inside SP
    Informative mapping between classes and code-points in an Appendix – this is for tsvwg’s info and comment
  Concept: Interconnecting Link between SPs
    Mark to standard Link Class & 3-bit CP, Re-mark on Egress
    Each SP can configure to the Link once for all interconnections
    Incentive to evolve to Link markings within SP over time

## Slide 3: What Happens Next?
<number>
tsvwg decides to
  Prepare a consensus response as reply
  Share a set of individual comments from tsvwg-list
  Consider the information shared in the Liaison
  Do nothing

## Slide 4: Background – Y.1566 Interconnecting Link
<number>

## Slide 5: Information and Example Mapping
<number>

## Slide 6: Standardised packet network QoS class and codepoint schemes at interconnection points.
<number>
Streaming
Background
(no subclass)
Conversational
Interactive
  High Prority
  Medium Priority
  Low Priority
First item
3GPP Classes &
GSMA IP PHB
MPLS TC
Ethernet Priority
IP Precedence
3
4
5
0
3
4
5
0
AF41
EF
Best Effort 0
AF31
AF32
AF33
Medium
  Comitted
  Excess
Low
  Comitted
  Excess
High
MEF IP PHB‘s & Classes
3
4
5
0
AF31
AF32, AF33
N/A
AF11
BE 0, AF12, AF13
EF
The table below is proposing classes and codepoints for interconnection interfaces and interworking between IP/MPLS and Ethernet layers. Please note that the table proposes changing GSMA PHBs (AF32 replaces AF21 and AF33 replaces AF 11). This change also solves a compatibility issue between GSMA IR.34 and MEF 23.1 on application of PHB AF1.
N/A
Notes: 16.04.2009
<number>
Autor / Thema der Präsentation