## Slide 1: Flow-based Performance Measurement (FPM) draft-sun-tsvwg-flowbased-pm-00
Lishun Sun
Wendong Wang
Fang Yu

## Slide 2: Requirements Overview
IP Performance Monitoring based on flow/applications is needed in many cases.
For mobile operator’s backhaul network, the applications are devided into multiple bearers with proper mobile QoS parameters (e.g. QCI). If the mobile network would manage bearers as QoS and applications, then the performance of backhaul is more like to be based on applications or QoS.
Currently there is no appropriate approach to monitor/test IP performance for separate applications.
In addition, in some cases, it needs to monitor the various time-varying performance indexes of the IP network, the performance measurement should be based on real service stream and reflect the real performance of the network. The average performance indexes measured by the active measurement method may not be suitable in these cases.
Page <number>

## Slide 3: Protocol Overview
This is an end-to-end flow-based IP performance monitoring method:
  It can support on-the-spot measurement.
  OAM packets are injects to the network to carry some parameters related to service flow and some statistic information.
  The OAM packets are processed using the same method as its corresponding service flow.
  The measurement statistics are Delay, Jitter, Loss rate and Bandwidth.
It involves three steps:
  Connection Activation
    Establish a connection between PM Initiator and PM Responder
    Define flow according to a certain method
    Configure parameters (e.g. period of measurement packets, Flow ID)
  Measurement Process
  Connection Deactivation
Page <number>

## Slide 4: Connection Activation-Definition of Flow
In the IPPM connection activation process, a unique Flow ID is assigned to a connection between the PM Initiator and the PM Responder for a defined flow.
Flow can be defined by different combinations of SIP, DIP, PT, DSCP, sPort and dPort：
  Flow can be defined by:
    (SIP, DIP, PT)
    (SIP, DIP, PT, DSCP)
    (SIP, DIP, PT, sPort, dPort)
  The more the combinational dimensions are, the more fine-grained can be the monitoring of data flow.
Page <number>

## Slide 5: Measurement Process-Typical process
PM
Responder
ACT
ACT-ACK
FM
BR
BR
DEA
DEA-ACK
FM
BR
.
.
.
FM
PM
Initiator
ACT:
FM:
BR:
Notes: Firstly the PM Initiator sends a request to the PM Responder to set up the PM connection activation. The PM Responder responds with an ACK packet including some parameters based on the request. When the PM Initiator receives the ACK, it will prepare for starting the measurement process.
During the measurement process, the PM Initiator periodically generates Forward Monitor (FM) packets with the source and destination IP addresses, and other classification information (for example DSCP class) , which are sent to the PM Responder. The generation and transmission of FM packets can be periodical with a specific time interval, or a certain number of traffic packets should be sent between two contiguous FM packets.
The PM Responder receives the FM packets and sends Backward Reporting(BR)packets which is constructed according to the FM packets.
The path performance such as the delay, jitter and loss rate etc. are calculates by the PM Initiator according to the information in the BR packets.
<number>

## Slide 6: Statistics
Delay ,
Jitter ,
Loss
  Lost Packet = (SPN(M) - SPN(M - 1) ) - (RPN(M) - RPN(M - 1) )
  Lost Packet Rate = ((SPN(M) - SPN(M - 1) ) - (RPN(i) - RPN(M - 1) ))/ (SPN(M) - SPN(M - 1) )

## Slide 7: Exception Handling
FM/BR Packet Loss
  In some cases the FM or BR packet may be lost in transit, no statistics can be obtained from this round of measurement, then loss rate of the mth measurement can be calculated as:
    Lost Packet Rate = ((SPN(M) - SPN(M - 1) ) - (RPN(i) - RPN(M - 1) ))/ (SPN(M) - SPN(M - 1) ) (note: M is the SN of the BR packet currently received and N is the SN of the latest BR received.)
Packets Mis-ordering
  Reasons for packets mis-ordering:
    the extra time spent on the IP fragment reassembly.
    Some load sharing schemes for network (e.g. ECMP, ML-PPP) may create multipath for packets.
    Multi-core CPU processing and multi-threading of packets in the sender and receiver.
  Solutions
    In the simplest case that data transmits along a single path, DSCP can be used to classify the flow in order to avoid the packet reordering.
    The packet loss calculation is based on sample statistic, by increasing the monitoring period, the error caused by the occasional packet reordering can be smoothed.
Page <number>

## Slide 8: Thank you