## Slide 1: Semantic IPv6 Prefix draft-jiang-semantic-prefix IETF 84 v6ops WG August 3, 2012
Sheng Jiang
Page <number>/10
Notes: <number>

## Slide 2: Motivation
This is a bad idea
  It waste a lot IPv6 addresses
But, we (as IETF) cannot stop people to use it LOCALLY
  It has many operational benefits from network operator perspective
But, it is dangerous
  The more semantics embedded into prefix, the more complicated management could be. Also there are technical gaps to fill
  It tries to push the problem to host OS and applications, but they are not ready to take it
The purpose of this document is to discuss how to use it well
  it could be manageable if the semantics have been carefully restricted
Page <number>/10
Notes: We already cannot get the host OS to choose IPv6 addresses properly, and forcing multi-function devices to have multiple IPv6 prefixes (one for each "special" application running on the device) will only make matters worse.
if we do not get the semantics straight and untangled, the routing scalability will be much worse in IPv6.
<number>

## Slide 3: Overview
Network operators (both ISPs and enterprises) desire to be aware of more information about each packet
  so that packets can be treated differently and efficiently
  Packet-level differentiating can enable flow-level and user-level differentiating
IPv6, with a large address space, allows semantics to be embedded into addresses
  Routers can easily apply relevant operations accordingly
This document provides analysis on how to use semantic prefix well, and identifies the technical gaps
It is recommended to use 4~12 bits in prefix for embedded semantics
Page <number>/10

## Slide 4: Why Prefix
Many information is not expressed explicitly. Hence, it is difficult for network operators to identify
Untrusted choices: interface identifier, extension header, diffServ field, etc.
Prefix is almost the only thing a network operator can trust in an IP packet
  it is delegated by the network and the network can detect any undesired modifications, then filter the packet
  if one get the destination addr wrong, the packet would not reach; it it get the source addr wrong, the return packet would not arrive
  It surely allows enterprise semantics to be able to traverse ISP networks
Page <number>/10
Notes: DPI is expensive and inefficiency. Overlay network, tunnel or label forwarding may operate the traffic path, they introduce extra overhead while they depend on indirect information sources
Although interface identifier of IPv6 address has arbitrary bits and extension header can carry much more information, they are not trustable by network operators
<number>

## Slide 5: Semantic Prefix Domain
A domain in which a consistent set of semantic prefix policies are administered in a coordinated fashion
  An enterprise Semantic Prefix Domain may span several physical networks, traversing ISP networks
A Semantic Prefix domain has a set of pre-defined semantic definitions, which is only meaningful locally
Standardizing a general semantic is almost an impossible job
Unless there are semantics agreements between two domains
  Sharing semantic definition among Semantic Prefix domains enables more semantic based network operations
Page <number>/10

## Slide 6: The Embedded Semantics
The prefix bits that can be used for embedded semantics are very limited
only the selected, most useful semantics can be embedded in the prefix
  Note, DiffServ provides a very rich QoS semantic with only 6 bits
  When used, all of semantic should be restricted in a highly abstracted way
In a given Semantic Prefix Domain, multiple semantics can be used combinatorially
Page <number>/10
Notes: A standard binding that would meet everyone's needs would require way to many bits
any attempt to standardize the semantics is doomed to failure
<number>

## Slide 7: How to use it well
Principle: avoid semantic overlap for packet
  though semantic overlap for devices/hosts is fine
Recommend: network operator only use necessary semantics
  Too many semantics make management for prefix delegation become very complicated. And hosts would not be able to handle
Recommend: assign in low granularity, such as bit by bit
Recommend: use less than 12 bits in prefix for semantics
The locator function of IP address should be ensured first for ISPs
  Recommend: use the most left bits of prefix for locator function and lower bits for semantics
Page <number>/10
Notes: recommended using the most left bits of prefix for locator function and lower bits for semantics. This would minimize the impact on routing aggregation. Actually, if considering the policy-based routing, the embedded semantics may provide better aggregation. It allows many policies to be aggregated according to the same semantics.
<number>

## Slide 8: Benefits
Depending on embedded semantics, various beneficial scenarios can be expected
Easy measurement and statistic
Easy flow control
Policy aggregation
Application-aware routing
The listed are not all
Page <number>/10

## Slide 9: Technical Gaps
The simplest model without any technical gaps: Only embedded abstracted user type semantic into the prefix
  It can be supported with the current network architecture
  because each subscriber is still assigned one prefix, while they are not notified the semantic within it
The more semantics embedded into prefix, the more complicated functions are needed for prefix delegation, host notification and address selections
  Associate semantics with prefix delegation
  Notify prefix semantics to hosts
  Address selection according to semantics on hosts. This may involve application interaction through socket API
It may take time for hosts to ready (enterprise may be quick)
Page <number>/10

## Slide 10
Page 10/<number>
Questions, clarifications?
Thanks!
Notes: Declaration again: this is an Informational document.
<number>