## Slide 1: Design Guidelines for IPv6 Networks draft-matthews-v6ops-design-guidelines
Philip Matthews
Alcatel-Lucent

## Slide 2: What?
Advice to designers of IPv6 networks.
Discusses questions that often arise in IPv6 or dual-stack network design.
  Ex: “Use LLAs or GUAs for eBGP sessions?”
For each question:
  List all the options
  Discuss pros and cons
  Describe current practice or make recommendation
Lower-level than existing docs on “Deploying IPv6 in <foo>-type networks”.
-00 version very preliminary

## Slide 3: Scope
No Addressing Plan section
  See RFC 5375 (Time to revise?)
Unicast only, for now
No DNS etc, for now
  Separate doc?
MPLS currently in

## Slide 4: Next-hop address in static route?
In a static route:
(a) Use far-end’s LLA addresses as next-hop, OR
(b) Use far-end’s GUA/ULA?
RFC 4861 (“ND for IPv6”) section 8 specifies (a):
“A router MUST be able to determine the link-local address for each of its neighboring routers in order to ensure that the target address in a Redirect message identifies the neighbor router by its link-local address. For static routing, this requirement implies that the next-hop router's address should be specified using the link-local address of the router.”
This implies (b) will prevent a router from sending redirects. Typically only a problem when 2+ routers and 1+ hosts are connected to same LAN, and where one router might redirect to the other (e.g., not running VRRP).
When redirects are not a concern, either (a) or (b) can be used.
Q for WG: Any other pros/cons?
My sense is that most operators do (b).
Suggest 6MAN update 4861?

## Slide 5: Mix or separate v4 and v6?
On a point-to-point router link:
(a) Mix v4 and v6, OR
 One L3 interface at each end
(b) Separate v4 and v6 onto separate (logical) links?
 Two L3 interfaces at each end
Pros for Option (a):
  Better scaling. Also lower cost if physical, rather than logical, links are used for option (b).
Pros for Option (b):
  Easier to measure traffic levels of each individual protocol. This is difficult today with option (a).
Most operators do (a) today, but (b) is also used.
Q for WG: Any other pros/cons? Recommend (a)?

## Slide 6: LLA or GUA/ULA addressing ?
On a point-to-point router link:
(a) Use LLA addresses only (“unnumbered”), OR
(b) Also use GUA/ULA addresses?
Pros for unnumbered links:
  Ease of configuration (less so if using manual LLA assignment).
  Security: interfaces cannot be attacked off-link
Cons for unnumbered links:
  Cannot ping interfaces from an off-link device.
  Traceroute returns loopback/system address rather than interface address.
  On some routers, LLA will change after line card swap unless hard-coded.
  Cannot identify interface or link by just LLA (in database, email, etc.)
Because of the cons, operators do (b) today.
Q for WG: Any other pros/cons? Recommend (b)?

## Slide 7: eBGP with LLA or GUA endpoints?
For an eBGP session:
(a) Use LLA addresses as endpoints, OR
(b) Use GUA addresses as endpoints ?
Note: This is about the eBGP endpoints, and not whether the link has GUAs.
Pros for option (a):
  Security against off-link attacks
Cons for option (a):
  Need “next-hop-self” at both endpoints (some routers do this automatically)
  Cannot refer to BGP session using just addresses, something operators are used to doing
  Inconsistency between v4 and v6 when doing dual-stack
  On some routers, eBGP with LLAs is more complex to configure.
  Strict interpretation of RFC 2545 (“MP-BGP for IPv6”) can be seen as forbidding eBGP sessions with LLA endpoints, as it requires the next-hop field to contain a GUA.
Most operators today use (b).
Q for WG: Any other pros/cons? Recommend (b)?