## Slide 1: RTCP XR Block for TS Decodability Statistics Metric
Draft-ietf-xrblock-rtcp-xr-decodability-00
Rachel Huang ( rachel.huang@huawei.com )
Hitoshi Asaeda (asaeda@wide.ad.jp)
Qin Wu ( bill.wu@huawei.com )
Glen Zorn (glenzorn@gmail.com)

## Slide 2: Overview
This draft (version 03) adopted in July 6 and associated milestones updated in July 9.
The draft is based on TS101.290, used with Transport Stream
and report the number of errors happens in the TS header.
00 WG draft was submitted in July 30.
Changes from previous version.
  Adding some clarifications on why only chooses 8 parameters from ETSI TR 101 290 in main body.
  Deleting acronyms part, subsection 2.2.
  Other editorial changes.

## Slide 3: Issue# Length of Each Metric
It was proposed to use 16bit for each metric field
However 16bit metric can not be used to report 2^16*7 TSs or 2^16*7 header errors.
  One RTP packet could contain at most 7 MPEG2 TS packets.
  One report block could report 65535(2^16) error event or the total number of TS.
Do we really need 32-bit for each metrics?
  Using 32-bit. It’s the simplest solution. Bandwidth is not a problem.
  Using 16-bit. 0xFFFF could indicate an over-range measurement.

## Slide 4: Issue# Normative or Informative?
ETSI TR 101 290 is a Technical Report, which contains mainly informative elements. Should it be referenced as a normative reference or informative reference?
It was argued that a normative reference is one which must be read and understood in order to read and understand the document citing it.
Propose to use ETSI TR 101 290 as normative reference.

## Slide 5: Next Step
Questions and comments?
Document will be updated based on feedback we received so far, thanks.