## Slide 1: RTCP XR Report Block for QoE metric Reporting draft-ietf-xrblock-rtcp-xr-qoe-02
26/7/30
XRBLOCK IETF 84 Vancouver
Geoff Hunt
Alan Clark
Roland Scott
Qin Wu
Glen Zorn
<number>

## Slide 2: Document Status
26/7/30
XRBLOCK IETF 84 Vancouver
This draft deals with two use cases
  each media sent in separate RTP stream
  Multi-channel audios sent in the same RTP stream
Two open issues were raised in the Paris meeting
  channel mapping in the multi-channel audio case
  how to identify layers for layered codecs
01 version was submitted after Paris meeting to address these two issues.
02 version is submitted with some editorial changes
Focus on introducing how the proposed change fix those two issues.
<number>

## Slide 3: Issue # channel mapping in multi-channel audio case
There are some payload formats that use different channel mappings
Magnus note that QoE for a single stream will also depend on the payload format in use
  Signal the details of what payload format was in use using out band schemes in case multiple payload formats are supported.
Changes to be done:
  Change 1: Update monitoring architecture document to point out some metric block may depend on payload format;
  Change 2: Include payload type of reported media in the metric block;
  Change 3: Update Channel Identifier definition and point out using Payload Type to determine the appropriate channel mapping;
26/7/30
XRBLOCK IETF 84 Vancouver
<number>

## Slide 4: Issue# identify each layer of video
In Paris meeting, we proposed to assign each layer with the integer value from 0 to n using the following mapping:
  SSID SSID description 0 base layer 1 enhancement layer 1 2 enhancement layer 2 ............... n enhancement layer n
However it is difficult to identify each layer for layered SVC.
  Static mapping is not sufficient
  The mapping may be tied to payload format
Magnus noted that it’s not sufficient to support only SSRC- and session-multiplexing
  SVC is used with multilayered video within a single stream, using 23 bit layer identifiers
Open question to report QoE for a layered stream
  report on the complete stream received, then a standard QoE report should be sufficient
    why is it useful to report per layer QoE ?
    Why does it matter to calculate and report QoE for each view?
Changes to be done.
  Remove layered support from the QoE metric draft
    Seems there is no work in ITU-T to evaluate the layered video quality
  If QoE for layered stream is needed, we will submit a new draft.
26/7/30
XRBLOCK IETF 84 Vancouver
<number>

## Slide 5: Follow Up
26/7/30
XRBLOCK IETF 84 Vancouver
Question?
WGLC?
<number>