## Slide 1: RTCP XR Blocks for Synchronization Delay and Offset Metrics Reporting
Hitoshi Asaeda (asaeda@wide.ad.jp)
Rachel Huang (rachel.huang@huawei.com)
Qin Wu (sunseawq@huawei.com)
draft-ietf-xrblock-rtcp-xr-synchronization-00
84th IETF, Vancouver, Canada

## Slide 2: Overview
The XR Blocks report initial Synchronization Delay for all medias to join multimedia session and synchronization Offset between RTP streams belonging to the same multimedia session.
Milestone updated on July 9
-00 WG draft submitted on July 30
Several changes made from -04 version
  Change back to only report one single value of general synchronization offset
  Enlarge the size of synchronization offset value to 64 bit NTP timestamp format
  Add definition of Initial Synchronization Delay
  Editorial changes

## Slide 3: Discussion on the Size of Synchronization Offset
Using millisecond as the unit (32-bit size)
  Con: Insufficient for some scenarios requiring high accuracy. (e.g., networked stereo loudspeakers, video walls, etc.)
Using 1/65535 second as the unit (32-bit size)
  Con: the 15 microsecond accuracy of a 1/65536 timestamp is marginal for measuring presentation time for some audio applications and could be insufficient for future applications in other fields
Using NTP timestamp (64-bit size)
  Pro: Sufficient for all the scenarios. No concern.
  Suggested on the list and Adopted.

## Slide 4: Next Step
Address all the remaining issues we receive
Comments?