## Slide 1: Mutually Exclusive Link Group (MELG)
draft-beeram-ccamp-melg-00.txt
Vishnu Pavan Beeram (Ed), John Drake, Gert Grammel
[Juniper Networks]
Igor Bryskin (Ed), Wes Doonan
[Adva Optical Networking]
Manuel Paul, Ruediger Kunze
[Deutsche Telekom]
Friedrich Armbruster, Cyril Margaria
[NSN] Oscar González de Dios
[Telefonica]
Daniele Ceccarelli
[Ericsson]
draft-beeram-ccamp-melg-00.txt

## Slide 2: MELG
Discussed earlier in GMPLS-ENNI draft
MELG-00 Content
  Definition
    Virtual TE Links and their “mutual exclusivity” attribute
  Usage
  Protocol Formats
    OSPF/ISIS
draft-beeram-ccamp-melg-00.txt

## Slide 3: MELG: Example 1
B
A
C
D
E
F
G
H
I
J
A
B
E
F
J
I
C
D
Client TE Info
MELG 33/192000
MELG 33/192000
draft-beeram-ccamp-melg-00.txt
Virtual “TE Links” E-I and F-J are mutually exclusive (Underlying server-paths require usage of the same resource – lambda channel 192000)
Same MELG is assigned to both the “TE-Links”

## Slide 4: MELG: Example 2
B
A
C
D
E
F
G
H
I
J
A
B
E
F
J
I
C
D
Client TE Info
MELG 19191901/bcde4f10
MELG 19191901/bcde4f10
draft-beeram-ccamp-melg-00.txt
Virtual “TE Links” F-J and F-I are mutually exclusive (Underlying server-paths require usage of the same resource – source transponder [ID bcde4f10])
Same MELG is assigned to both the “TE-Links”

## Slide 5: MELG: Construct Usage
Indicate via separate network unique number(s) that the advertised Virtual TE Link belongs to one or more Mutually Exclusive Link Groups
Indicate whether the advertised Virtual TE Link is committed or not at the time of advertising.
draft-beeram-ccamp-melg-00.txt

## Slide 6: MELG: Construct Format
draft-beeram-ccamp-melg-00.txt

## Slide 7: MELG: U-Bit Semantics
VTE Link advertisement
  MAY include MELGs sub-TLV with zero MELGs
  Withdrawn, when there is no potential path
  with (BW=0), (MELG U-Bit=0)
    Resources used by some other VTE Link with common MELG
    Candidate for MBB Computation, provided original path is known to PCE
  with (BW=0), (MELG U-Bit=1)
    VTE Link is fully loaded
    Candidate for MBB computation, provided the original path is known to PCE and this link is present in the original path
  with (BW≠0), (MELG U-Bit=0,1)
    Candidate for normal and MBB computation

## Slide 8: Questions
Separate document for extensions to each protocol ?
Working Group status ?
draft-beeram-ccamp-melg-00.txt

## Slide 9: Thank you
draft-beeram-ccamp-melg-00.txt