## Slide 1: draft-pfister-bier-mld-02 BIER Ingress Multicast Flow Overlay using Multicast Listener Discovery Protocols
Pierre Pfister, pierre.pfister@darou.fr
IJsbrand Wijnands, ice@cisco.com
Markus Stenberg, markus.stenberg@iki.fi
Stig Venaas, stig@cisco.com

## Slide 2: Overview
MLDv2/IGMPv3 overlay is used to inform ingress BIER routers which egress BIER routers should receive which flows
Routers receiving multicast from outside the BIER domain, or that have directly connected sources must be BMLD queriers
Routers desiring to receive multicast are BMLD listeners and send BMLD reports
  They also need to be configured with the BFR-ids of the queriers, or alternatively sending to all BFRs (all bits set)
Multicast sources
Receivers
querier
Elected querier
Query
Reports

## Slide 3: Details
Only routers that may be forwarding multicast into the BIER domain need to be queriers
  Only these routers need to receive reports and maintain state
  They will do explicit tracking to know each receiver for each flow
  As usual, one is elected to be the querier
All routers that may be forwarding multicast out of the BIER domain need to be listeners
  Listeners need to be configured with the BFR-ids of the queriers, or alternatively sending to all BFRs (all bits set)
Queries must be sent to all listeners and queriers
  The latter for querier election
  Queriers need to be configured need to be configured with the BFR-ids of the listeners and queriers, or alternatively sending to all BFRs (all bits set)
BMLD messages sent to “All BMLD queriers” and all “All BMLD nodes” addresses
  Addresses are configurable, and there can be multiple instances with different addresses

## Slide 4: Open issues
Duplicate traffic entering the BIER domain
  If multiple queriers can receive from the same source, only one should forward into the BIER domain
Duplicate traffic leaving the BIER domain
  This depends on the topology of the network outside the BIER domain and may be handled there
If BIER used end-to-end, then draft-wijnands-bier-mld-lan-election may be a solution