## Slide 1
Distributed Mobility Management (DMM) WG Forwarding Path & Signaling Management (FPSM) draft-ietf-dmm-fpc-cpdp-05.txt L. Bertz, S. Matsushima, M. Liebsch, S. Gundavelli, D. Moses, IETF97, Seoul
2016-11-14

## Slide 2: FPC Version 04/05
IETF 97
November 2016

## Slide 3: What is this work about..?
Enable the separation of a mobility network‘s Control-Plane function from its Data-Plane function
Enable distributed deployment of Control- and Data-Plane functions by abstracted Data-plane model and protocol messages
Support multi-tenancy on a single real deployed D-plane network and multiple domains within a tanant
Mobility Control-Plane
FPC Client
DPN(s) Configuration API
FPC Agent
D-plane model
Protocol messages

## Slide 4: Progress since last IETF96 meeting
New data model adopted
  Configuration of Data-Plane Topology
  Configuration of Forwarding Policy (e.g. filters, QoS and traffic steering, etc)
  Port collects Policies and instantiated by Context that represents mobility session (e.g. tunnel endpoints of DPN, meters)
Commands and Operations aligned with new data model
  Create Mobile Node session context
  Re-use pre-configured data (Topology, Policy and existing mobilie sessions)
  Select Data-Plane nodes based on topology view
Multi-DPN Agent
Single-DPN Agent

## Slide 5: Information Model of FPC Data-Plane
Policy-group
~v03
v04~
Port
Context
Property
Descriptor
Property
Descriptor
Attribute
Attribute
Attribute
Property
Descriptor
Model-1
Model-2
Port
Topology
Context
Context
Context
Multi-DPN attr
Single DPN attr
Policy-group
Policy
Policy
Action(s)
Descriptor(s)
Rule
Action(s)
Descriptor(s)
Rule
Anchor DPN
DPN-Group
Access DPN
DPN-Group

## Slide 6: FPC D-Plane Abstraction (v04~)
Domain 1a
Domain 2a
Domain Na
DPN-Group(MAG)
DPN-Group(SGW)
DPN-Group(SGSN)
DPN-Group(LMA)
DPN-Group(PGW)
DPN-Group(GGSN)
Domain 1x
Domain 2x
Domain Nx
DPN-Group(MAG)
DPN-Group(SGW)
DPN-Group(SGSN)
DPN-Group(LMA)
DPN-Group(PGW)
DPN-Group(GGSN)
Abstracted D-Plane on a FPC-Agent
Tenant A
Tenant X
・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・・
DPN1
DPN2
Real Deployed D-plane NW of an Operator

## Slide 7: Abstracted DPN and Real Deployed DPN
Two kind of DPNs coexist
  Abstracted DPN(s) on a FPC-Agent
  Real deployed DPN(s) in an operator’s networks
Do we need to clearly distinguish them using appropriate terms? for example:
  A-DPN (Abstracted DPN)
  R-DPN (Real-deployed DPN)

## Slide 8: Domain vs. Network Slice
Network Slice
  NGMN Whitepaper
  3GPP TR23.799 (Work in progress)
“Domain” in FPC
  Quite similar concept with Slice
Do we use term Slice instead of Domain?
Do we need to liaise to 3GPP to align what Slice is?
  Not only at Slice, but FPC as a D-plane interface for 5G that also be liaised

## Slide 9: Protocol Overview

## Slide 10: Remote Procedure Calls (Client => Agent)
Version 03 had > 3 RPC Calls for Model 1 and > 24 for Model 2
Versions 04/05 define 2 calls
  Configure (CONF)
    Can perform Create, Update, Query & Delete on Contexts and Ports
    A single CONF body is referred to as an ‘Operation’ or ‘Op’
  Configure Bundles (CONF_BUNDLES) – A Grouping of CONF messages
    Each Operation is given an order to be executed in.
    All Operations are executed according to the order
    All Operations of lower order value MUST be completed prior to starting the current Operation
    2 Types of Transaction execution strategies defined
      Default – If operation N fails
        All prior operations remain (no rollback)
        An error is returned indicating the failure of Operation N
        No subsequent messages (operation N+1) or higher will be executed
      All or Nothing – Like the default strategy but
        All prior operations are rolled back
  RPC responses include status of OK, FAIL & OK-NOTIFY-FOLLOWS (ACK + Update via Notification)

## Slide 11: CONF Basic Flow Example
Client
Agent
DPN
CONF
OK_NOTIFY_FOLLOWS
CONFIG_RESULT_NOTIFY
Any Agent Assignment work is done here
Client
Agent
DPN
CONF
OK
Synchronous Style
Ack/Update and Aynchronous Style

## Slide 12: Notifications (Agent to Client)
CONFIG_RESULT_NOTIFICATION – Final Result of a CONF or CONF_BUNDLE request IF the Agent initially responded to a client with an OK_NOTIFY_FOLLOWS.
NOTIFY – Can represent
  Agent Events
  MONITOR related events

## Slide 13: Monitors (Largely Unchanged since v03)
Watches for items
  Single values
  Events
Each Monitor has a configuration
  Threshold
  Periodic
  Event based
All values are returned as part of a Notification
RPCs are provided for
  Probe – Get a Monitor Notification ‘right now’
  Register – Set up a Monitor
  De-register – Remove a Monitor

## Slide 14: CONF and CONF_BUNDLES Options
Option | Description | Benefit | Downside
Op-Ref | The scope the Agent needs to search to find a reference made inside the operation: none intra-operation Inter-operation (bundles) Storage (in agent) Unknown (treated as Storage) | Let’s the Agent know when to stop searching for a reference. Can be used to build stateless Agents (only support ‘none’ or intra-operation’ | An extra parameter but in the case of invalid configuration the Agent can quickly determine the error rather than trying to find data not present in the cache
Command Set | Bit format (technology specific) that tells the Agent EXACTLY what the Client needs. | Allows for quick error detection. Permits Agent to be built more as a transaction manager / adapter | Very explicit command/control may preclude development of smart agents.
Policy Configuration | Ability to send policy information model in CONF and CONF_BUNDLES | Supports realtime provision of all FPC Information elements | Requires more work in the Agent and inflates the over the wire messages.

## Slide 15: FPCv04 Implementation
IETF DMM Working Group
IETF 97

## Slide 16: FPC Implementations
V04 adds an Implementation Status from Sprint
Two projects
fpcagent (v03 Model 1 Implementation – RETIRED, will NOT be made available)
  Objectives
    Study v03 Model 1
    Performance Characteristics
    Complexity
fpc (v04 implementation)
  Objectives
    Full Implementation / Open Source
    Performance Characteristics – Can we use RESTConf for call processing?
    Complexity

## Slide 17: fpc Project
Overview
  Java based
  Opendaylight ODL
    Beryllium release
    Plugin (maven startup archetype)
  Intended Release: Open Source (ODL licensing)
  Intended to be IPR Free (implements FPC and a proprietary DPN API)
Features
  Multi-DPN Agent
  CONF message
  CONF_BUNDLES (not thoroughly tested)
  Client binding – bind Client/Tenant relationships (not in spec)
  HTTP and ZeroMQ (ZMQ - SCTP influenced) transport
  Proprietary ZMQ DPN API
  Auto-assignment of DPN, IP Address and Tunnel Info

## Slide 18: HTTP RESTConf Performance
Client
Agent
DPN
CONF
OK_NOTIFY_FOLLOWS
CONFIG_RESULT_NOTIFY
4-6ms
3-5 ms is JSON parsing!
1-6 ms* (based on transaction)
Benchmark
8700 tps via HTTP RESTConf when using a client with same threadpool startup, e.g. jmeter
  Eventually Garbage Collection becomes an issue
  Required 8-12 cores of a CPU
Currently working through burst on start / re-start where we can lose packets or jam the system under high load
* - Made heavy use of OpRef and CommandSet options in version 04. Cache write and persistence is done by another process.
Takeaway – RESTConf can sustain loads but the JSON parsing is the bulk of the processing for the first message.

## Slide 19: Takeaways
Performance
    Is 8700 TPS enough? (Depends upon your call models; we can’t really answer this for the generic 5G operator until the mobility and call models are understood)
    We will ALWAYS find a need for more devices per Controller
  Do you want a single SDN Controller dedicated to just FPC work? (Shouldn’t it be doing other SDN related work?)
  8-12 cores is too much but this was first pass on the code (un-optimized)
  Latency - RESTConf appears to be okay for this but it is 75-80% of the time spent processing => there is room for improvement
Complexity
  We had system close to feature complete in September but removed persistence and monitors to study the main RPC calls. This code started on September 1. We’re happy with v04’s progress.

## Slide 20: Appendix

## Slide 21: fpc TODOs
Resolve Burst Issue in HTTP Threadpool
Openflow 1.3.1+ DPN Support with specific TPP (pipelines)
Move to a standard ODL in memory cache which allow us to complete
  Persistence
  Rollbacks
  Full Deletion support (it is not always consistent right now)
Finish CONF_BUNDLES testing
Monitors
Multi Agent Clustering
Open Sourcing (under internal Legal Review)
Migrate to v05

## Slide 22: Current Interfaces
Assignment Phase
Activation Phase
ZeroMQ
RestCONF
(Router/Dealer)
- EXPERIMENTAL
HTTP
RestCONF
ZeroMQ
DPN API
(Pub Sub)
ZeroMQ Pub/Sub
OpenDaylight
Cache Mgt / Notification
HTTP
RestCONF-like
Notification
DPNs
Queues
Queues
Queues