## Slide 1: Neighbor discovery to support direct communication in ITS
draft-yan-its-nd-01.txt
Zhiwei Yan & Jong-Hyouk Lee

## Slide 2: Neighbor discovery in ITS
Discover the neighbor vehicle and the nearby service
Learn the link-layer address of the selected neighbor vehicle
In the dynamic and fragmentation-possible environment--VANET
Assumptions:
Name: vehicle SHOULD have a temporary name which is related to location
Address: vehicle SHOULD have a global IP address which is more stable

## Slide 3: ITS Network Architecture
May be out the scope of this draft
Router
Internet
RSU1
RSU2
Vehicle1
Vehicle1
Vehicle1
Local name1
Local name2
IP Prefix
Address: IP Prefix
Name: local name1
Address: IP Prefix
Name: local name2
Address: IP Prefix
Name: local name1
Name: local name2
Logically:
*WSA: IP prefix+name+…

## Slide 4: Why mDNS (Multicast DNS)?
Suitable for the infrastructure-less environment
  VANET
For service discovery
  Discovery the named service and named vehicle
Standardized protocol
  ST-RFC6762, based on DNS
  Neighbor vehicles with the same prefix are ON THE SAME LINK

## Slide 5: ND based on mDNS---- Ad-hoc based
Different modes can be used in different scenarios:
  One-shot Multicast DNS Query
    E.g., Locate the specific service
  Continuous Multicast DNS Query
    E.g., Locate the nearby vehicles which are moving
  Multiple Questions per Query: Locate multiple services/vehicles simultaneously
  Multiple Questions Multicast Responses: update the caches of receivers
  Multiple Questions Unicast Responses: new vehicle joins

## Slide 6: ND based on mDNS----RSU based
Vehicles MAY have direct connection with RSU
RSU is a local DNS server
RSU maintains the registered vehicle/services
or acts as a relay/proxy:
  Direct Unicast Queries to Port 5353
  or
  Legacy Unicast DNS

## Slide 7: ND based on mDNS
Probing and Announcing on Startup
A vehicle starts up, wakes up from stalls, topology changes (after configuration of the name and address):
  Probe the availability of the service it announced
  Then, announce the service and its existence
    Unsolicited multicast DNS response containing, in the Answer Section, all of its service and name and address……
    Update the information actively if there is any change

## Slide 8: ND based on mDNS
Goodbay~
A vehicle will arrive at its destination, stall temporarily or shut down its camera…
  Announce the service suspending and its inexistence
    Unsolicited multicast DNS response packet, giving the same RRs (containing its name and address), but TTL of zero

## Slide 9: Signaling messages
TBD:
To piggyback link-layer address
To include Geo-information
….
OR:
mDNS service discovery + NDP
mDNS service discovery + Others
Extension of mDNS RR

## Slide 10: Security considerations
DNS traffic reduction and flooding avoidance
  With mDNS schemes
    Known-Answer Suppression
    Multipacket Known-Answer Suppression
    Duplicate Question Suppression
    Duplicate Answer Suppression
Origination: DNS message Source Address Check
DNS message tampering avoidance
  With DNSSEC, IPsec
  ……

## Slide 11
Thank you for your attention~