## Slide 1: On-demand Continuity Check (CC) and Connectivity Verification(CV) for OverlayNetworks draft-ooamdt-rtgwg-demand-cc-cv-01
Greg Mirsky
Erik Nordmark
Nagendra Kumar
Deepak Kumar
Mach Chen
IETF-97, Seoul. November, 2016
Yizhou Li
David Mozes
David Dolson
Ignas Bagdonas

## Slide 2: Update
Terminology:
  switched from ping to “Echo Request” and “Echo Reply”
Overlay Echo Request Transmission:
  MUST use the appropriate encapsulation of the monitored overlay network;
  Overlay network's header MUST be immediately followed by the Overlay OAM Header;
  Message Type field in the Overlay OAM Header MUST be set to Overlay Echo Request value

## Slide 3: Security Considerations
Overlay EchoRequest/Replay operates within the domain of the overlay network and thus inherits any security considerations that apply to the use of that overlay technology and, consequently, underlay data plane.
Possible approaches of attacking an overlay node using Overlay Echo Request/Reply:
  send Overlay Echo Requests to overload the node, i.e. DoS;
  tampering with Echo Request/Reply to misrepresent state of the overlay network;
  unauthorized use of Echo Request/Reply to obtain information about overlay/underlay network.
To mitigate risks:
  throttle control packets to the control plane;
  use Sendler’s Handle, Sequence Number and, possible, Timestamp block;
  source address validation

## Slide 4: Traceroute in Overlay
What is traceroute in an Overlay Network?
Does any overlay have TTL?
Or is traceroute expected to trace the underlay?

## Slide 5: Next steps
Welcome comments from the WG
Asking WG to consider adoption of the draft
Thank you