## Slide 1: Optimizing DTLS for use in IoT
draft-mavrogiannopoulos-dtls-cid-00
draft-fossati-tls-iot-optimizations-00
IETF 97 Seoul

## Slide 2: Overview
RFC 7925 was written to provide guidance for use with TLS/DTLS in the IoT environment.
  Goal was to use TLS/DTLS as is.
There are, however, cases where extensions would help.
draft-fossati-tls-iot-optimizations-00 talks about those. Popular is
  Transport Agnostic Security Associations
  Reducing the DTLS Record Layer Header Overhead

## Slide 3: Use Cases
Long lasting CoAP/DTLS sessions with very little data sent will fail due to aggressive NAT timeouts
Keep-alive traffic is not an option for sleepy/constrained devices, and neither is negotiating a new security association every time a new application protocol transaction is needed

## Slide 4: Use Cases, cont.
Same as use case (1), but in the context of DTLS-based VPNs
Aggressive NAT UDP timeouts break the underlying security association
Using Heartbeat [RFC 6520] is not an option when client is a phone or a tablet

## Slide 5: Use Cases, cont.
IoT device with radio technologies offering limited bandwidth, such as GSM, and low power WANs
Handshaking over those is painful and basically limited to PSK

## Slide 6: Requirements
Work with DTLS 1.2 and later
Optional behaviour
Privacy-friendly whenever possible

## Slide 7: Proposed Solution
DTLS context de-muxing based on Transport independent identifier (CID)
  CID is negotiated using a new DTLS extension (ts_sa)
  CID is added to each DTLS record header
Two ways to allocate the CID:
  Server decides unilaterally a value that is fixed for the duration of the session (SecAssocType.fixed)
  Server and Client agree on a sequence of values generated using HOTP [RFC 4226] seeded by the session shared secret (SecAssocType.hotp); Client shifts to the next value when needed (e.g. on transport handover)

## Slide 8: Open Issues
How to signal the other party that the wire format has changed
  Creative use of the version field?
Are 32-bits enough to make HOTP usable for high load servers? Probability of CID collisions is already quite high with ~100 concurrent sessions
  Bigger cid (e.g., 5-6 bytes) when SecAssocType.hotp is negotiated

## Slide 9: Implementation
Three stacks have already showed their interest in implementing:
  mbedTLS, gnuTLS, and Scandium