## Slide 1: ECN Experimentation
draft-black-ecn-experimentation
TSVWG – IETF 97 (Seoul)
David L. Black (as draft author)

## Slide 2: Proposed ECN Experiments
Proposed areas of ECN experimentation:
  Non-drop-equivalent response to Congestion Experienced (CE) marks [new name: Congestion Response Differences]
    draft-khademi-tcpm-alternativebackoff-ecn
    draft-briscoe-tsvwg-l4s-id
  Treat ECT(1)-marked traffic differently from ECT(0)-marked traffic.
    draft-briscoe-tsvwg-l4s-id
  Use ECN on control packets e.g., TCP SYN, etc.
    draft-bagnulo-tcpm-generalized-ecn
Experimental RFCs seem plausible for all 3, but:
  ECN RFC modifications required, e.g., to RFC 3168
  ECT(1) for L4S also requires changing the ECN Nonce (Experimental RFC 3540) to Historic.

## Slide 3: draft-black-tsvwg-ecn-experimentation
One standards-track draft to modify RFC 3168 and friends to enable ECN experimentation:
  Experimental or better RFC required to use modifications
    IESG retains control over ECN behavior on the Internet
  Inform the IETF community (& the IESG) about this activity
  Avoid multiple process exceptions for Experimental RFCs
  This is NOT a 3168bis draft.
Also declares ECN Nonce experiment to be over
  And reclassifies RFC 3540 as Historic
Most issues resolved in -03 version of draft:
  Many thanks to Bob Briscoe for detailed review
Major open issue: ECT(1) requirements
  Background and proposed direction: Next 2 slides

## Slide 4: ECT(1): Background
RFC 3168 says:
  SHOULD use ECT(0) if only one codepoint needed
L4S uses ECT(1) codepoint to identify traffic for higher probability CE marking
  Much more frequent CE marking than drop equivalence
  Protocols that use ECT(1) and assume drop equivalence of CE marks will have problems
    E.g., Tunnel Congestion Feedback: MUST NOT use ECT(1)
If L4S is successful, IETF may designate ECT(1) codepoint for L4S use only:
  ECN Nonce: Primary known existing use of ECT(1)
  RTP allows ECT(1), deployment unclear
  There may be other not-yet-known existing uses.

## Slide 5: ECT(1): Proposed Direction
ECT Usage (Open Issue: SHOULD vs. MUST):
  ECT(0) SHOULD be used unless otherwise specified by an Experimental RFC.
  ECT(1) SHOULD NOT be used unless otherwise specified by an Experimental RFC.
Document main points from previous slide:
  Warn that ECT(1) use by L4S is likely to result in more network marking of CE than drop equivalence.
  Note that ECT(1) may become L4S-only in future, hence use by new non-L4S RFCs is not appropriate.
Remove RFC 3168 and RFC 6679 text that could allow ECT(1) usage if both ECT codepoints used.

## Slide 6: Request & Plan
Request: TSVWG WG Adoption of draft-black-ecn-experimentation
Plan: Updated draft and WG Last Call by end of year, submit to IESG shortly thereafter