## Slide 1: Trusted Execution Environments (TEE) and the Open Trust Protocol (OTrP)
Hannes Tschofenig and Mingliang Pei
16th July 2017 -- IETF 99th, Prague

## Slide 2
What do we mean by security?

## Slide 3: Communication Security
Aims
Prevent eavesdropping on communication
  Solution: Encryption
Prevent spoofing of end point/server
  Solution: Authentication
Components Required
Standards based encryption/decryption & authentication algorithms
True random number generator
Strong key provisioning, management, and storage
Strong identity provisioning, management, and storage

## Slide 4: Software Security
Aims
Protect device/system from rogue software
  Downloaded software
  Remote software
Prevent access to certain assets & data
  Reading data
  Alteration of data
Allow recovery from attack
Note: access can be remote or via local connector
Components Required
Isolation of and restricted access to certain data, resources and code
Secure storage
Trusted boot
Immutable device identity
Separation of monitoring & recovery functionality

## Slide 5: Physical Security
Aims
Protecting against hardware attacks.
  Intrusive attacks
  Semi Intrusive attacks
  Side Channel attacks
Examples include:
  Differential power analysis
  Cutting internal chip tracks
  Fault injection
  Voltage variation
  etc
Components Required
Specialised anti-tampering technology. E.g.
  Deducing power and timing traces
  Randomization of the pipeline
Encrypted memory interfaces

## Slide 6
Security Principles

## Slide 7: Security Principles: Isolation and Least Privilege
Isolation
Isolate trusted resources from non-trusted
Access to trusted software only through APIs
Non-trusted software run at lowest privilege possible
Reduce attack surface of key components
non-trusted
trusted

## Slide 8: Security Principles: Isolation and Least Privilege
non-trusted
trusted
Non-Trusted
Majority of software
Operating system
Graphics
Applications
Data processing
etc
Trusted Software
Crypto functions
Key management
Attack detection
Sensitive data
Trusted Software
Provision of security services
Small, well reviewed code
Notes: The fundamental security principles of isolation and least privilege are reinforced within a root of trust. This gives us a set of essential features every secure system needs such as:
Root keys
Secure Boot into a known state
Validating a secure clock and counters
Using a Chain of Trust, from secure kernel to boot a TEE and bring in trusted device drivers signed with certificates in secure key store
Secure memory partitions
Once a root of trust is established only then is it safe to start the applications themselves

## Slide 9: Security Profiles
Invasive HW Attacks
Well resourced and funded
Unlimited time, money & equipment.
Non-invasive HW Attacks
Physical access to device: JTAG, Bus Probing, IO Pins, Side Channels etc.
Value to attacker
Software Attacks
Malware, Viruses, Root Kits
Social engineering
Cost/Effort
To Attack
Cost/Effort
to Secure

## Slide 10
TEE Solutions

## Slide 11: Trusted Execution Environment: Why?
Internet protocols today all rely on security protection
  Use security protocols requiring cryptographic keys
  Utilize cryptographic algorithms
Operating systems (OSs), such as Android/Linux, are complex and sophisticated.
Solution is to augment the OS with a more restrictive, and environment
And extract the security components from applications / OS into this environment
Trusted Execution Environments provide such an environment

## Slide 12: Trusted Execution Environment: What is needed?
Lightweight OS that can support mutually distrusting Trusted Apps
Isolated environment for the execution of trusted code
Private memory spaces for code and data
        Cannot be snooped or modified by other system agents
Well defined entry and exit interfaces
  Designed to retain secrets when clients are fully compromised
Trusted Boot ROM*
Trusted boot process*
Cryptographic services
  Symmetric Private Key
  Asymmetric Public Key
  Random Number Generator
Cryptographic key store
  Unique and shared keys
Secure storage
  For persistent data, such as keys
(*) Needed for ARM TrustZone but not for other TEEs (e.g., Intel SGX)

## Slide 13: Security Profiles
Invasive HW Attacks
Well resourced and funded
Unlimited time, money & equipment.
Non-invasive HW Attacks
Physical access to device: JTAG, Bus Probing, IO Pins, Side Channels etc.
Value to attacker
Software Attacks
Malware, Viruses, Root Kits
Social engineering
Cost/Effort
To Attack
Cost/Effort
to Secure
TrustZone based TEE
Secure Elements / HSMs

## Slide 14: ARM Architecture Profiles
Application Profile ARMv8-A
32-bit and 64-bit
A32, T32 and A64 instruction sets
Virtual memory system
Supporting rich operating systems
Real-time Profile
ARMv8-R
32-bit
A32 and T32 instruction sets
Protected memory system
(optional virtual memory)
Optimized for real-time systems
Microcontroller Profile
ARMv8-M
32-bit
T32 / Thumb® instruction set only
Protected memory system
Optimized for microcontroller applications
Notes: With the launch of ARMv8-M, ARM has now completed all three profiles for the 8th generation of the ARM architecure.
Just to remind you, these are the application profile with architecure ARMv8-A, like the Cortex-A57, A72 and A35 processors used in mobile devices and servers.
Then there is the Real-time profile with the ARMv8-R architecture that is targetted at real-time applications, for example in cars, but also in hard disk controllers.
Finally, the microcontroller profile with the ARMv8-M architecure is designed for resource constrained microcontroller applications.

## Slide 15: TrustZone for ARMv8-A TrustZone for ARMv8-M
SECURE STATES
NON-SECURE STATES
SECURE STATES
NON-SECURE STATES
TrustZone for ARMv8-M
Secure transitions handled by the processor to maintain embedded class latency
Secure App/Libs
Secure OS
Non-secure OS
Non-secure App
Secure App/Libs
Secure OS
Rich OS, e.g.Linux
Secure Monitor
Notes: About TZ-M
Just like TZ, there’s a safety barrier between software domains
You have Secure and Non-Secure code running on the same processor
Unlike TZ, there’s no SM, improving interrupt latency as NS apps can call S apps directly
Secure Monitor is an execution level only in TZ. Makes transition between SC and NS state. Downside is this makes interrupt latency high. With TZ-M, non-secure app can call secure app directly.
Part of new ARMv8-M architecture
  Security architecture for deeply embedded processors
  Enables containerisation of software
  Simplifies security assessment of embedded devices
Conceptually similar to ARM TrustZone technology, but...
  New architecture tailored for embedded devices
  Preserves low interrupt latencies
  Better cross-domain calling performance
Foundation for high-level security features
  Secure remote firmware update
  Secure manufacturing
  Safe crypto implementations
Secure Thread – Trusted code/data
Secure Handler – Trusted device drivers,

## Slide 16: Secure Memory Map
I2C
Boot ROM
SRAM
DRAM
Code
&
Data
UART
I2C
Normal physical memory map contains
  DRAM for code and data
  I/O peripherals
  On chip ROM and SRAM
The Secure state acts like “33rd address bit”
  Doubling size of physical address map
Key resources become secure only
  Boot ROM and internal SRAM
I/O devices are segregated
  Secure only, Non-Secure or shared access
DRAM can be partitioned
  Using address space controller
DRAM
Code
&
Data
0xFFFFFFFF
0x00000000
0x80000000
Boot ROM
0x20000000
0x10000000
0x50000000
0x60000000
0x40000000
SRAM
UART
I2C
Boot ROM
SRAM
I2C
Secure
NS=0
Non-Secure
NS=1
FUSES
0xFFFFFFFF
0x00000000
0x80000000
0x20000000
0x10000000
0x50000000
0x60000000
0x40000000
0x90000000
Secure DRAM

## Slide 17: Example System on Chip (SoC)
CPU 0
L1I$
L1D$
MMU
L2$
DRAM
System Bus
L2$
GPU
CPU 1
L1I$
L1D$
MMU
SRAM
Memory Controller
ROM
GIC
Peripheral Bus
RTC
UART
Timer
Flash
MMU
Display
Controller
MMU
Flash
Memory
I2C
CPU cluster
  MMUs and caches
Bus mastering devices
  GPU and Display controller
Boot ROM and SRAM
Memory Controller to DRAM
Peripheral bus
  Standard peripherals
Debug

## Slide 18: Example SoC with TrustZone
Secure state added to CPU
  MMU and Caches
NS tags in buses
Boot ROM and SRAM secured
Debug and profiling secured
Secure only peripherals added
Shared peripherals modified
DRAM partitioned for Secure
Crypto HW accelerator
External Secure Peripherals
Existing Non-Secure HW remains unchanged
  Never able to generate NS=0 transactions
Note: Secure resources not to scale
CPU 0
L1I$
L1D$
MMU
L2$
DRAM
System Bus
L2$
GPU
CPU 1
L1I$
L1D$
MMU
SRAM
ROM
GIC
Peripheral Bus
RTC
UART
Timer
Flash
MMU
Display
Controller
MMU
Flash
Memory
I2C
Memory Controller
Debug
NS
CPU 1
L1I$
L1D$
MMU
NS
NS
NS
CPU 0
L1I$
L1D$
MMU
NS
NS
NS
NS
SRAM
ROM
Debug
Peripheral Bus
Timer
Fuses
RNG
GIC
I2C
Secure Partition
TZASC
Crypto
Finger
Print
KEY:
Trusted
Normal
NS

## Slide 19: TrustZone Software Stack
Trusted Execution Environment
  Light-weight operating system offering security services:
    Key Store, Crypto,
    Random Numbers
    Secure Store
    Secure Device Drivers
  Enables Trusted Apps, which can be installed, updated and deleted
EL3 Monitor provides Secure / Non-Secure switching
OS integration requires TEE driver issues SMCs to TEE
Rich OS
TEE
TA 2
Monitor . .
TA 1
Non-Secure
Secure
Hypervisor
EL0
EL1
EL2
EL3
S-EL0
S-EL1
TEE Driver
Media
Player
Web
Browser
SMC
Dispatch
Crypto
Keys
Finger
Print Reader
Event
Handler
Finger Print Driver
Crypto Driver
Hardware

## Slide 20: FIDO Use Case
FIDO is an attempt to replace username/password-based authentication with something strong.
Process:
  Web service challenges device
  Challenge passed onto FIDO authenticator
  Performs user verification (e.g., fingerprint)
  Cryptographically sign the challenge
  Send response to web service
  User now securely logged in
  For transaction confirmation, trusted display is used.
Software and hardware stack needed for operation
  Networking, Rich OS, Secure OS, HW
  FIDO Authenticator functionality in TEE; FIDO private key and fingerprint never leaves the TEE
Rich OS
FIDO plugin
TEE
FIDO
TA
Monitor
Non-Secure
Hypervisor
EL0
EL1
EL2
EL3
S-EL0
S-EL1
TEE Driver
Web
Browser
SMC
Dispatch
Crypto
Keys
Finger
Print
Event
Handler
Finger Print
Driver
Crypto
Driver
Secure
Hardware
Trusted Display
Trusted Display

## Slide 21
Running Code

## Slide 22: Open Source Software Available
Many developers of TEE technology
  Chip companies, OEMs, OS platform owners, Independent Software Vendors, OSS
ARM Trusted Firmware:
  Link: https://github.com/ARM-software/arm-trusted-firmware
  AArch64 reference implementation containing trusted boot, monitor and runtime firmware
OP-TEE
  Link: https://github.com/OP-TEE/
  Reference implementation of secure world OS.
GlobalPlatform provides common set of API’s and services

## Slide 23: Trying TrustZone @ Home
TrustZone on Raspberry Pi3
Sequitur Labs port of Linaro’s OP-TEE environment to the Raspberry Pi 3
Press release:
http://linuxgizmos.com/trustzone-tee-tech-ported-to-raspberry-pi-3/
Code:
https://github.com/OP-TEE/build/blob/master/docs/rpi3.md
Video: https://www.youtube.com/watch?v=3MnLrHoQcyI
USB Armory
Hardware: http://inversepath.com/usbarmory.html
~100 EUR
The USB armory from Inverse Path is an open source hardware design, implementing a flash drive sized computer with TrustZone.
Example apps available: https://github.com/inversepath/usbarmory/wiki/Applications

## Slide 24: Summary
Isolation helps to improve security for software.
TrustZone provides the CPU and system isolation.
Open source code available for you to play with.

## Slide 25
Open Trust Protocol (OTrP):
Problem Statement

## Slide 26: Demand of hardware based security with TEE and TA
Secure World
SD
Device with TEE
SP
TAM
OTA Provisioning and Management
Trusted
Applications
(TA)
Create
Hardware Platform
TEE
Normal World
Rich OS
Client
Applications
TA
SD
TA
Payment App
Providers
Security App
Providers
Game App Providers
Enterprise App Providers

## Slide 27: The Challenge
Adoption gap for service providers
  Gap between devices with hardware security and a wish to push Trusted Apps to devices with different TEEs and vendors
Fragmentation is growing - IoT accelerated that fragmentation
Lack of standards to manage TAs
  Devices have hardware based Trusted Execution Environments (TEE) but they do not have a standard way of managing those security domains and TAs

## Slide 28: Gaps to utilize hardware based security
Payment App
Providers
Security App
Providers
Game App Providers
Multiple OSs
Firmware X, Y, Z
Many
Service
Providers
Device Hardware
Trusted Applications
Client Applications
Device
Manufactures
TEE
Providers
Chip/Firmware
Providers
Key
Management
?
What protocol to install, update, and delete TAs? (with attestation feature)
Trusted
Applications
Devices with TEE
Enterprise App Providers

## Slide 29
Open Trust Protocol (OTrP)

## Slide 30: Open Trust Protocol (OTrP)
An interoperable Trust Application Management protocol across broad application providers and diverse TEE OS providers
Designed to work with any hardware security based TEE that aims to support a multi-vendor environment
Focus on re-use of existing schemes (CA and PKI) and ease of implementation (keeping message protocol high level)

## Slide 31
CAs issue certificates to OTrP actors (TEE, TAM, SP)
TAM and TEE exchange messages
An OTrP Agent relays the OTrP message between TAM and TEE
Secure World
Normal World
Client App
Trusted App
Secure World
OS
Hardware
OTrP Agent
Normal World OS
Device
Overview
Certification Authorities for Devices
Certification Authorities for TAM and SP
Open Trust Protocol
TAM
Service Providers (SP)

## Slide 32: Design Choices
Uses asymmetric keys and PKI
  Manufacturer-provided keys and trust anchors
  Enables attestation between TAM and TEE-device
JSON-based messaging between TAM and TEE
  Messages for attestation
  Messages for security domain management and TA management
  Use JOSE (JSON signing and encryption specifications) – CBOR alternative spec available.
OTrP Agent in REE relays message exchanges between a TAM and TEE
Device has a single TEE only

## Slide 33: Envisioned User Experience
App developer builds two components:
Android App &
Trusted App
Developer includes a TAM library to handle the OTrP transport
App developer uploads their Android app to a suitable app store and securely sends their trusted app to their TAM provider
End user downloads Android app from an app store
App on first start communicates to TAM provider and installs trusted app into the TEE using OTrP
End user enjoys a rich Android experience and the security of a TEE backed trusted component
TAM

## Slide 34: OTrP Agent
Responsible for routing OTrP messages to the appropriate TEE
Most commonly developed and distributed by TEE vendor
Implements an interface as a service, SDK, etc.
TAM

## Slide 35
PKI
Device
Software
OTrP
Device
Certification Authority
TEE
Hardware Platform
TAM
OTrP
Agent
Certificate Enrollment API
Implementation Specific API
OTrP Message
OTrP Agent API
Scope
Certification Authority
Client App
Service Provider

## Slide 36
Command | Descriptions
GetDeviceState | Retrieve information of TEE device state including SD and TA associated to a TAM
Command | Descriptions
CreateSD | Create SD in the TEE associated to a TAM
UpdateSD | Update sub-SD within SD or SP related information
DeleteSD | Delete SD or SD related information in the TEE associated to a TAM
Command | Descriptions
InstallTA | Install TA in the SD associated to a TAM
UpdateTA | Update TA in the SD associated to a TAM
DeleteTA | Delete TA in the SD associated to a TAM
Remote Device Attestation
Security Domain Management
Trusted Application Management
Operations and Messages

## Slide 37
* AIK: Attestation Identity Key, TFW: Trusted Firmware
Certificate Authority
TAM
Service Provider
SP Key pair
and Certificate
TAM Key pair
and Certificate
TEE Key pair
and Certificate
TFW Key pair
and Certificate (optional)
Device TEE
* Key pair and Certificate:
evidence of secure boot
and trustworthy firmware
* Key pair and Certificate:
used to sign a TA
* Key pair and Certificate:
device attestation
to remote TAM and SP.
* SP AIK in runtime
for use by SP (encrypt TA data / verify)
* Key pair and Certificate:
used to issue certificate
CA Certificate
Trust Anchors: trusted Root CA list of TEE certificates
Keys
* Key pair and Certificate:
sign OTrP requests to be verified by TEE
Trust Anchors: trusted Root CA list of TAM & TFW
Keys
Trust Anchors
Usage

## Slide 38: Entity Relationships

## Slide 39
Security of the Operation Protocol is enhanced by applying the following three Measures:
  Verifies validity of Message Sender’s Certificate
  Verifies signature of Message Sender to check immutability
  Encrypted to guard against exposure of Sensitive data
Request to TSM for TA installation
Send [GetDeviceState] to TEE
Return DSI as a response to [GetDeviceState]
Send [CreateSD]to create SD where the TA will be installed
Send other prerequisite commands (if necessary)
Send [installTA] with encrypted TA binary and its data
Decrypt TA binary and its
personal data.
Install TA into target SD.
Store personal data in
TA’s private storage.
Phase#1
“Device Attestation”
Operation request triggered and verify Device state information
Phase#2
Prerequisite operation
(if Security domain doesn’t exist where the TA should be installed)
Phase#3
Perform Operation requested by SP or Client Application
TAM
Client App
TEE
Create new SD
Sample Protocol Usage Flow

## Slide 40: Summary
Some TEEs, such as TrustZone, are open to companies to install their favorite secure world OS.
Vendors want to have a choice regarding Trusted Application Managers.
This creates an interoperability challenge for managing (installing, updating, deleting) Trusted Applications on a TEE.
OTrP provides a protocol for such a TA management (offering attestation capabilities).