## Slide 1: BIER-Ethernet draft-wang-bier-ethernet Linda Wang (Presenting) Sandy. Zhang

## Slide 2: Background
BIER-Ethernet: implements BIER forwarding in Ethernet network.

## Slide 3: DATA Plane Solution
Because there requires directions to identify the BIFT table, there should allocate the BSL, sub-domain and SI fields in the updated BIER header, as well as TTL and TOS field. As follow:
Additionally, mostly, this updated BIER header is immediately after Ethernet header, so there may need a new Ether Type to encode this kind of updated BIER header.

## Slide 4: Control Plane Solution
The Main Idea:
    Define a new sub-sub-TLV to carry BSL information;
    Then advertise this BSL sub-sub-TLV together with BIER Info sub-TLV in IGP extension/BGP extension.
    Already updated and defined in ISIS extension draft

## Slide 5: Some updates
Why using BIER-Ethernet? --- For more clean cut design
and just let MPLS as an independent layer protocol to help BIER forwarding as it does for IPv4/IPv6/IPmcast traffic. Additionally, the BIER forwarding capability will be also introduced in enterprise/data center, such feature may be newly implemented in switch ASICs, with clean cut design using BIER-ethernet, the implementation will be more clean as well.
2. BIER Ethernet Considerations for NVO3 network
There may be requirements for current switch ASICs in datacenter to implement BIER- Ethernet forwarding. And then, there will be a more efficient way to forward BUM traffic, rather than ingress replication and multicast tree.

## Slide 6: Some updates
3. BIER Ethernet Considerations for BIER Traffic Engineering
BIER-TE encapsulation format may be the same as BIER encapsulation. However, how to interpret the BitString is totally different. Hence, BIER-Ethernet encapsulation MUST need one identifier to be assigned to identify the BIER header is for BIER forwarding or BIER-TE forwarding. For example, one bit in Reserved field can be reserved for this purpose.
4. BIER Ethernet Considerations for MVPN
In MVPN, the P-tunnels are used for carrying multicast traffic across backbone. BIER tunnel Type is newly defined in [I-D.ietf-bier-mvpn]. The BIER Encapsulation used for multicast tunnel is independant of the MPLS label. Hence, BIER-Ethernet can also be used as P-Tunnel. In other words, there may need a new Tunnel Type to identify BIER-Ethernet Tunnel type, or a new flag to distinguish BIER-MPLS tunnel and BIER-Ethernet Tunnel.

## Slide 7: Next Steps
DISCUSSION…….