## Slide 1: BIER Use Case in NVO3 draft-wang-bier-vxlan-use-case-02 Linda Wang (Presenting) Sandy. Zhang

## Slide 2: Background
Motivated by draft-ietf-bier-use-cases, in section 3.6, it proposes there are many advantages introducing BIER in Data Center Virtualization.
proposes solutions how to extend protocol to take advantage of BIER in Data Center Virtualization.
Until now, received several precious comments.

## Slide 3: The Problem
In data center virtualization, there are two most common solutions to forward BUM traffic on the overlay network:
  Ingress Replication: However, it doesn’t provide the optimal forwarding of multicast packets.
  Enable the multicast capability in the underlay, such as PIM-SM or PIM-BIDIR and so on. However, it requires data centers to run multicast protocol and maintain multicast state in all the edge nodes and intermediate nodes.
Proposed EVPN solution
  Mapping the VXLAN VNI or NVGRE VSID to an EVI
  Advertising inclusive Multicast Ethernet Tag routes to carry the VNI/VSID field through EVPN control plane
  Advertising BGP Encapsulation extended community to carry the specific data plane encapsulation for the BUM traffic, such as VXLAN/NVGRE/MPLS/MPLS in GRE/VXLAN GPE and so on.
  However, it requires NVE/VTEP to run EVPN

## Slide 4: The Solution
Introducing BIER at the transport layer in Data Center Virtualization
Furthermore, introducing MLD as control plane to construct the overlay mapping.
  Providing the optimal forwarding of multicast packets
  Doesn’t require the data centers to run multicast protocol and maintain multicast state in the intermediate nodes
  Doesn’t require the data centers to run EVPN

## Slide 5: The Sketch of this Solution
  Specifically, using MLD as an overlay control plane to collect the VTEP/NVE belonging to the same VNI/VSID (like constructing I-PMSI tunnel), through carrying VNI/VSID information in the MLD extension.
BIER Domain
MLD
BIER info + VNI info
NVE-A:00001
NVE-C:00100
NVE-D:01000
NVE-E:10000
MLD
BIER info + VXLAN info
MLD
BIER info + VNI info
MLD
BIER info + VXLAN info
VM20
VM30
VM30
VM20
I-BIFT:
VNI | Bitmask | …
20 | 01110 | …
30 | 10000 | …
VM20
VNI 20
VNI 30
MLD
BIER info + VNI info
NVE-B:00010
VM20

## Slide 6: The Sketch of this Solution
  Then, using MLD as an overlay control plane as well to collect the VTEP/NVE attaching to the same tenant who join the same multicast group(like constructing S-PMSI tunnel), through carrying <S,G>information in the MLD extension.
BIER Domain
MLD
BIER info +VNI info+ <S,G> info
NVE-A:00001
NVE-C:00100
NVE-D:01000
NVE-E:10000
MLD
BIER info +VNI info+ <S,G> info
VM20
VM30
VM30
VM20
S-BIFT:
<S,G> | VNI | Bitmask | …
<S,G> | 20 | 00110 | …
VM20
NVE-B:00010
VM20
(S,G)Join
(S,G)Join

## Slide 7: The Sketch of this Solution
  Using the <S,G> information in the multicast traffic to lookup S-BIFT, encapsulating the multicast traffic with the Bitmask in the table, and forwarding the multicast traffic using BIER forwarding.
BIER Domain
NVE-A:00001
NVE-C:00100
NVE-D:01000
NVE-E:10000
VM20
VM30
VM20
S-BIFT:
<S,G> | VNI | Bitmask | …
<S,G> | 20 | 00110 | …
VM20
NVE-B:00010
VM20

## Slide 8: MLD extension
The main idea:
  Each NVE advertises Virtual Network Identifier information with BIER information to other NVEs through MLD, including VXLAN network identifer, VSID and so on.
BIER Info sub-TLV
VNI Info sub-sub-TLV
Virtual Network Identifier Info sub-sub-TLV

## Slide 9
Discussion