## Slide 1: Updates to Draft Specification for DTN TCPCLv4
Brian Sipos
RKF Engineering Solutions

## Slide 2: Overview
Background and current draft
Review comments and initial responses
Path forward for TCPCL

## Slide 3: Motivations for Updates to TCPCL
During implementation of TCPCLv3, Scott Burleigh found an ambiguity in bundle acknowledgment and refusal.
For use in a terrestrial WAN, I have a need for TLS-based authentication and integrity. TCPCLv3 mentions TLS but does not specify its use.
Contact negotiation in TCPCLv3 is limited and relatively hard-coded.
Allow an endpoint to positively reject a message (rather than simply ignoring it).

## Slide 4: Goals for TCPCLv4
Do not change scope or workflow of TCPCL!
  As much as possible, keep existing requirements and behaviors. The baseline spec was a copy-paste of TCPCLv3.
  Still using single-phase contact negotiation, re-using existing headers and message type codes.
  Allow existing implementations to be adapted for TCPCLv4.
Re-use existing encoding, type and reason codes.
  Avoid duplication of IANA assignments.
  Since workflow is preserved, majority of message types are retained.
  This inherits limitations from TCPCLv3 for the sake of simplified implementation changes.

## Slide 5: Reviews To-Date
Original TCPCL(v3) authors asked to review
  Michael Demmer no longer in field, declined review
  Simon Perreault reviewed with no comments
  Joerg Ott provided comments to WG mailing list

## Slide 6: Comment Areas
Front matter and editorial
Interoperation with TCPCLv3
Combined BPv6 and BPv7 operation
Multiple underlying transport?
Contact Header Option List
Bundle Exchange messages (Bundle IDs)
Security requirements

## Slide 7: General Comments
Section 1 front matter
  Will update text for DTN WG, etc.
Keyword capitalization
  Can scour document and replace
Interoperation with TCPCLv3
  Currently allow backward compatibility, but not stated earlier than Contact Header
  SHUTDOWN code for v3?
Combined BPv6 and BPv7 operation
  Is this a necessary mode?
  Would require per-bundle version identifier
Multiple underlying transport?
  My feeling is defer this until really needed, many “what if” options
Need to bump the protocol version number?
  Yes, the TCPCLv3 concepts are kept but not the mechanisms

## Slide 8: Contact Header Comments
Option ordering
  Would add a canonical order by Type Code
Reduce use of SDNV
  I don’t have strong opinion on this
How to handle unknown Types
  Add flag to indicate mandatory interpretation (similar to CMS “CRITICAL” flag or BP block flags)
Repeated options not allowed
  This just simplifies logic
  What would be an example of repeated option?
Replacement for IGNORE mnemonic
  Any recommendations?
Acknowledge Bundle negotiation
  This was purely for backwards compatibility, can leave out
  If both LENGTH and ACK_BUNDLE are protocol-mandatory then logic is simplified… thoughts?
Bundle/fragment maximum size negotiation?
  Sure, with default no-limit

## Slide 9: Bundle Exchange Comments
LENGTH message size vs. actual received size difference
  Agree with comment, LENGTH is indicative only
REJECT message add field to indicate troublesome location within message
  This seems fine to add but I’m not sure how much value it adds
Nomenclature byte vs octet
  Will replace with octet throughout
Tighter requirements on generation of Bundle IDs needed
  I was hoping to avoid this, but I do agree that lack of required behavior can lead to bad behavior
  Maybe specify sequentially increasing values..?
  Maybe specify contact negotiation of maximum ID..?
  Any thoughts?
SDNV really needed for Bundle ID?
  I think this is too use-case dependent to be otherwise

## Slide 10: Bundle Exchange cont.
Rephrase requirement which depends on bundle structure
  I believe that this was in TCPCLv3 and left as-is
  I agree that this should simply be removed and existing requirement left as: each segment corresponds to distinct bundle
LENGTH needs to contain Bundle ID?
  Yes, the Bundle ID is needed so that it can be present in a possible corresponding REFUSE message

## Slide 11: STARTTLS Comments
How to handle received messages on insecure link when secure link is required?
  I agree with a rejection reason AWAITING_TLS or similar
  Could use current UNEXPECTED
Comment about requirements on TLS exchange itself
  Current draft follows lead of RFC2595 (STARTTLS for mail)
  Any TLS-specific parameters or negotiation are deferred to application, can plainly state this in TCPCL spec
Question whether additional info is needed in Security section
  I believe only explicit lack of requirement is needed

## Slide 12: Revised Protocol Status
Editorial comments need to be incorporated into existing draft
Further discussion on open questions
  DTN mailing list suitable for discussions
Joerg has recommended review but current TCPCL implementers
  Would this be a side-effect of WG adoption of TCPCLv4?
WG adoption of TCPCPv4 for BPbis use
  Would anything in I-D need to change to allow this?