## Slide 1
Chairs:
Pascal Thubert
Thomas Watteyne
Etherpad for Minutes: https://etherpad.tools.ietf.org/p/6tisch
IPv6 over the TSCH mode of IEEE 802.15.4
6 October 2017 Webex

## Slide 2: Note Well
Any submission to the IETF intended by the Contributor for publication as all or part of an IETF Internet-Draft or RFC and any statement made within the context of an IETF activity is considered an "IETF Contribution". Such statements include oral statements in IETF sessions, as well as written and electronic communications made at any time or place, which are addressed to:
  The IETF plenary session
  The IESG, or any member thereof on behalf of the IESG
  Any IETF mailing list, including the IETF list itself, any working group or design team list, or any other list functioning under IETF auspices
  Any IETF working group or portion thereof
  Any Birds of a Feather (BOF) session
  The IAB or any member thereof on behalf of the IAB
  The RFC Editor or the Internet-Drafts function
All IETF Contributions are subject to the rules of RFC 5378 and RFC 8179.
Statements made outside of an IETF session, mailing list or other function, that are clearly not intended to be input to an IETF activity, group or function, are not IETF Contributions in the context of this notice. Please consult RFC 5378 and RFC 8179 for details.
A participant in any IETF activity is deemed to accept all IETF rules of process, as documented in Best Current Practices RFCs and IESG Statements.
A participant in any IETF activity acknowledges that written, audio and video records of meetings may be made and may be available to the public.

## Slide 3
Reminder: Minutes are taken * This meeting is recorded ** Presence is logged ***
* Scribe; please contribute online to the minutes at: https://etherpad.tools.ietf.org/p/6tisch
** Recordings and Minutes are public and may be subject to discovery in the event of litigation.
*** From the Webex login

## Slide 4: Agenda bashing
7:05 | Opening, agenda bashing (Chairs) Note-Well, Scribes, Agenda Bashing, Approval minutes from last meeting Status of drafts (WGLC / forthcoming WGLC) Last meeting todos | 10mn
7:15 | Starting 6P shepherding (Pascal) | 5mn
7:20 | 6P WGLC issues resolution (Xavi) | 15mn
7:35 | SFx Readiness (Diego) | 5mn
7:40 | SF0 what's the plan? (Thomas) | 5mn
7:45 | Reroute for RPL (Pascal) | 15mn
7:58 | AOB | QS

## Slide 5
5
5
Milestones
Before
After
Date | Milestone
Dec 2017 | 6TiSCH architecture and terminology in RFC publication queue
Apr 2017 | Initial submission of 6TiSCH architecture to the IESG draft-ietf-6tisch-architecture
Apr 2017 | Initial submission of 6TiSCH terminology to the IESG draft-ietf-6tisch-terminology
Dec 2016 | Evaluate WG progress, propose new charter to the IESG
Dec 2016 | Initial submission of draft-ietf-6tisch-6top-sf0 to the IESG
Dec 2016 | Initial submission of draft-ietf-6tisch-6top-protocol to the IESG draft-ietf-6tisch-6top-protocol
Date | Milestone
Dec 2018 | 6TiSCH architecture and terminology in RFC publication queue
Nov 2018 | Initial submission of 6TiSCH architecture to the IESG draft-ietf-6tisch-architecture
Oct 2018 | Initial submission of 6TiSCH terminology to the IESG draft-ietf-6tisch-terminology
Jul 2018 | Initial submission of draft-ietf-6tisch-dtsecurity-zerotouch-join to the IESG draft-ietf-6tisch-dtsecurity-zerotouch-join
Feb 2018 | Initial submission of draft-ietf-6tisch-minimal-security to the IESG draft-ietf-6tisch-minimal-security
Oct 2017 | Initial submission of draft-ietf-6tisch-6top-sfx to the IESG draft-ietf-6tisch-6top-sfx
Oct 2017 | Initial submission of draft-ietf-6tisch-6top-protocol to the IESG draft-ietf-6tisch-6top-protocol

## Slide 6: Minute takers, jabber scribes
Minutes
  Etherpad: https://etherpad.tools.ietf.org/p/notes-ietf-100-6tisch?useMonospaceFont=true
  Minute takers volunteers?
Remote participation
  Meetecho: http://www.meetecho.com/ietf100/6tisch
  Jabber: 6tisch@jabber.ietf.org
    Jabber scribe volunteers?
Mailing list: 6tisch@ietf.org
  To subscribe: https://www.ietf.org/mailman/listinfo/6tisch
Meeting materials: https://datatracker.ietf.org/meeting/100/materials.html/#6tisch

## Slide 7: 6P Shepherding and WGLC issues resolution

## Slide 8: 6P shepherding
IPR

## Slide 9
Status
Last Call process
Received some comments from Pascal and Diego
Will produce v09 addressing the comments
  8 comments still to be addressed.

## Slide 10
List of issues

## Slide 11
Discussion
Version Checking comment:
  Do nodes need to advertise the supported version?
Proposal (as per Pascal suggestion):
  When a VER_ERR code is returned the payload of the message contains the version number(s) supported by the responding node.

## Slide 12
Discussion
Timeout dependency:
  Is there a dependency on the value of a timer on one side vs. the other? Eg in a 3-step, do we want the requester to time out first and retry, or the responder to retry his response before the requester times out?
Response: We want that the timeout on one side enables all possible attempts from the other side to respond. This is, has to take into account the number of L2 retransmissions that are possible.

## Slide 13
Discussion
Inconsistency handling
  3.4.6.2. Detecting and Handling Schedule Inconsistency Inconsistency may happen when L2 acknowledgment of the last packet in a transaction is lost, i.e. RESPONSE (in 2-step 6P transaction) or CONFIRMATION (in 3-step 6P transaction) have been received on one side while timeout happens on the other side. Take 2-step 6P transaction as example, i.e. timeout happens when node B is waiting for L2 acknowledgment to its Response message. Upon the timeout, the SF running on the node that timeout (e.g node B) MUST take action to validate the schedule state on both sides.
  Question: Should we suggest an action? e.g counting or listing cells to see if schedules still match?
  Same for the case that one side has reset and INCO_ERR is returned. What should 6P do next?

## Slide 14: Scheduling functions

## Slide 15: SFx Readiness
Proposal: editorial discussion with Diego
Moved SF0 to SFX as an experimental version of SF0.
SF0 will follow when the parameter values and/or ranges are calculated from the required experiments
Added an “Experimental Requirements” section to define which experiments are needed: Values for OVERPROVISION, PDR_THRESHOLD, SF0THRESH, Timeout and churn/stability analysis.

## Slide 16: SF0
internal discussions ongoing, not finalized yet

## Slide 17: Fast reroute for RPL
Using central computation for non-congruent routes to root

## Slide 18: ARC Root concept
R
A
B
A node which is the only exit for a DAG
Example:
  R is a node if locally generated prefix
  R is a pseudo-node if A & B are ABR / ASBR
  Head-end of a autonomous sub-DAG
  R can be abstract, eg the Internet

## Slide 19: ARC Heir concept
R
A
B
First level where at least two nodes are connected to a root
If a root has one only heir, then this heir becomes root

## Slide 20: ARC Leaf concept
N
A
A leaf is a node with a single link
A leaf cannot be a junction
A leaf an be a root for a nested graph

## Slide 21: ARC Junction concept
R
A
D
B
C
A junction is a node that no single failure can isolate; IOW it is a node that has 2 non congruent paths to the root.
Defining a Safe Node and root, heir or junction:
A node is a junction (and thus a Safe Node) if it is connected to two Safe Nodes over non congruent paths
E
Establishing an Arc always starts at a junction

## Slide 22: Junction concept
R
A
D
B
C
R is root as it injects prefix
A & B are heirs as they are directly connected to R
C is a junction as it has two independent paths to R (via A & B heirs)
D is a junction as it has two independent paths to R (via A & C junctions)
…
Resolution of link reversibility is always starting from a junction

## Slide 23: Leaf concept
N
A
A leaf is a node with a single link
A leaf cannot be a junction
A leaf can be a root for a nested graph

## Slide 24: Arc concept
An Arc is a 2 ended reversible path
Edges are directed outwards; links within are reversible
An arc is resilient to any link or Junction break by returning links
Links are oriented from cursor to edges and returned by moving the cursor.
We build Arcs between Junctions
C
Rev
Rev
Rev
Rev
Edge
Cursor

## Slide 25: Arc concept (cont’d)
An infrastructure Arc is multihop
An Edge Junction terminates one reversible link
An Intermediate Junction terminates two reversible links
Links are oriented from a mobile cursor (C) Junction outwards
R
A collapsed Arc does not have an Intermediate Junction
An Edge Junction may belong to multiple collapsed Arcs
C
Rev
Rev
Rev
Rev
Edge Junction
Intermediate Junction

## Slide 26: Arc concept (cont’d)
Junctions may have multiple incoming links
An Edge Junction might have multiple outgoing links
An intermediate Junction has no outgoing link but along the Arc
J
No
Yes
Yes
Yes
Yes
C
Rev
Rev
Rev
Rev

## Slide 27
ROOT
A
B
Software-defined Projected ARROW
Arcs for RPL Routing Over Wireless
Metrics are accumulated as usual in RPL (separated from Rank)
Siblings are allowed (all ARC members have the same Rank)
Rank of ARC members defines ARC height

## Slide 28: Conditoins on RPL operation
Sparrow requires non storing mode (NS-mode).
Nodes must advertise at least 2 parents and report metrics
Root computes ARC Set based on NS-mode DAO

## Slide 29: ARROW Example: Initial topology
R
A
D
L
B
K
J
C
E
F
G
H
I
M
M

## Slide 30: Say standard RPL gives:
In blue the preferred parent path
In red the alt path as RPL computes them based on Rank relationship.
These « arrows » are advertised to the root using NS-Mode
We see that most nodes do not have 2 non-congruent solutions
(in fact, only J does!)
R
A
D
L
B
K
J
C
E
F
G
H
I
M
N
Rank = 1
Rank = 3
Rank = 2
Rank = 4
Rank = 5
Rank = 6
Rank = 5
Rank = 7
Rank = 10
Rank = 8
Rank = 5
Rank = 10
Rank = 9
Rank = 10
Rank = 12

## Slide 31: Result of the ARC algorithm:

Original RPL DAG
R
A
D
L
B
K
J
C
E
F
G
H
I
M
N
ARC Re-organized DAG
R
A
D
L
B
K
J
C
E
F
G
H
I
Rev
Rev
Rev
Rev
Rev
Rev
M
N
Rev

## Slide 32: Result of the algorithm:
DAG visualization
==
ARC visualization
R
A
D
L
B
K
J
C
E
F
G
H
I
M
N
R
A
D
L
B
K
J
C
E
F
G
H
I
Rev
Rev
Rev
Rev
Rev
Rev
M
N
Rev

## Slide 33: Adapting to RPL
Root considers changes made on DODAG and notifies nodes, e.g. it tells C that D is not more a feasible successor and it tells D that C is a feasible successor. Same goes between E and F. This can be done with a novel variation of the DAO projection
For collapsed ARCs, e.g. D, we are all set
For other nodes that are not on collased ARCs, the root computes a path along the ARC towards the other exit of the ARC. For Node C that is Node B.
R
A
D
L
B
K
J
C
E
F
G
H
I
M
N
R
A
D
L
B
K
J
C
E
F
G
H
I
Rev
Rev
Rev
Rev
Rev
Rev
M
N
Rev
Use C as alt parent
Do Not Use D as alt parent

## Slide 34: Cont…
The path to B is installed as either storing or non storing projected DAO
In NS Mode the source route path from the node to the other ARC edge is indicated to each node
In Storing Mode, a route is created from both ends of the ARC allowing each edge (a,d all nodes in between) to route to the other edge
If C loses connectivity to A, it uses a tunnel to B till RPL completes local repair. Tunnel has a routing header in NS mode.
When the Edge decaps, it must forward outside the ARC; it cannot reinject in the ARC.
R
A
D
L
B
K
J
C
E
F
G
H
I
Rev
Rev
Rev
Rev
Rev
Rev
M
N
Rev
Non storing DAO:
indicating
Source Route path to B
Source Route path to B
Projected DAO
R
A
D
L
B
K
J
C
E
F
G
H
I
Rev
Rev
Rev
Rev
Rev
Rev
M
N
Rev
DAO Ack
Storing mode Route to B
Projected DAO

## Slide 35: Any Other Business?

## Slide 36: PANID compression bit
src addr: short
dest addr: short
single PAN address
src addr: short
dest addr: short
No PAN address
?