## Slide 1: Keyword-Based Mobile Application Sharing through Information-Centric Connectivity
Dr Ioannis Psaras
EPSRC Fellow / Lecturer
University College London
Email: i.psaras@ucl.ac.uk
Web: http://www.ee.ucl.ac.uk/~ipsaras/
I. Psaras, S. Rene, K.V. Katsaros, V. Sourlas, N. Bezirgiannidis,
S. Diamantopoulos, I. Komnios, V. Tsaoussidis, G. Pavlou
ICNRG Interim Meeting
16th July 2017
Prague
Best Paper Award
ACM MobiArch 2016

## Slide 2: The Cloud is not enough
<rant>
Always trying to reach the cloud does
not work
  E.g. trains, airplances, crowded areas
5G needs to integrate some edge-computing functionality
The cloud is neither the only nor the best way
There are enormous amounts of computation and storage available around us
  5G has to exploit the computation, storage and software resources of edge devices (smartphones, tablets, Raspberry PIs, WiFi APs)
Connecting randomly to the nearest device does not work
  Information-Centric Connectivity becomes necessity when we need to specify to which of the 100s of smartphone devices to connect to.
  This need does not exist when we always connect to the main cell tower
</rant>
Notes: <number>

## Slide 3: What is KEBAPP – Contribution
Route Finder App
Game or Video-Streaming Server
Super Boring!
An application sharing and information-processing framework for smartphone apps
Notes: <number>

## Slide 4: What applications does KEBAPP deal with – Design Space
By and large, smartphone apps target:
  Static content, e.g., news updates
  Personalised content, e.g., Facebook/Twitter updates
  Processed information, e.g., route finder, gaming
    Keep demand for local services, locally!
We envision a pool of application resources to provide D2D access to processed and non-personalised information

## Slide 5: Where/When do we need KEBAPP (Target environments)
Overcrowded areas
  Airports, festivals, stadiums, IETF :)
Fragmented networks
  Natural disasters (floods, earthquakes)
Not (or poorly) connected environments
  Airplanes, trains, ferries, developing regions
In most of those cases, Internet connectivity is not even necessary!

## Slide 6: How does KEBAPP work?
Application-centric naming
  Applications share common name-spaces and support the use of keywords
Application-centric connectivity
  Applications manage connectivity by defining and/or joining WiFi broadcast domains
Information-centric forwarding
  Extending Named Data Networking
  primitives
Applications act both as clients and as servers
Three Main Components

## Slide 8: Information-Centric Mobility
Content is the addressable entity
  Not the host!
Content is the routing target
  Not the host!
Interface to the content is used
  Not to a socket!
Content is secured individually
  Not the communication channel!
No need to keep references of moving nodes

## Slide 9: Information Exposure through Names
ICN can enable features not possible with IP
  Exposure of information through names.
A network-layer naming scheme that enables fine-grained description of the desired processed information

## Slide 10: Application-Centric Naming (App IDs)
Needs to support fine-grained description of the desired processed information
Fixed part: NDN hierarchical naming, longest prefix match
  Needs to guarantee compatibility between applications
  Can define static content: /NewsApp/politics/
  Or invoke computation: /myTravelAdvisor/Top10Restos
  App GUI indicates naming, users do not have to be aware of naming
Hashtags: free keywords to assist application processing
  Enables partial matching of responses to requests
  /myTravelAdvisor/Top10Restos #userRating; #London; #indian
  /routeFinder/tube #euston; #waterloo
Notes: <number>

## Slide 11: Application-Centric Connectivity
Application-specific 802.11 broadcast domains, through Basic Service Set(s), BSSs
  Need a “hook” between BSS and the corresponding application
  Every KEBAPP application advertises its own SSID, through WiFi Direct Groups
  WiFi Neighbour-Awareness Networking (NAN) can find applications behind BSSs – also optimised for energy efficiency
gameX
tripAdvisor
routeFinder
*K.V. Katsaros et. al. “Information-Centric Connectivity”
IEEE Communications Magazine, August 2016.

## Slide 12: Information-Centric Forwarding
We build on a modified version of NDN
Forward messages to single-hop broadcasting (BSS) domains
Single-hop operation
gameX
tripAdvisor
routeFinder
Name Prefix | BSSID | if
/travel/tripAdvisor #x #y | tripAdvisor | #1
/gaming/gameX #z | gameX | #2
Name Prefix | BSSID | if
/travel/routeFinder #x | routeFinder | #1
Broadcast domains are considered as node interfaces
FIB is populated with neighbouring BSSIDs

## Slide 13
WiFi Manager populates
FIB with hierarchical name
advertised by SSID
BSSIDs are the new
interfaces
Server part of app
internalFace entry links
BSSID to specific app that
listens to this SSID.
One PIT entry per request

## Slide 14: Feasibility – RouteFinder App
Setup
Mobility trace from 3300 users in a Stockholm
subway station throughout one hour
All users: 3300
KEBAB
Users (10%)
RouteFinder
App Users

## Slide 15: Route Finder App

## Slide 16: Vision: An Edge ICN IoT Platform based on Information-Centric Connectivity
The long-term plan is to develop a platform for IoT applications
  users can build applications or applets
  API should be lightweight and easy to use, e.g., IFTTT-like
Some applications already implemented in Raspberry PIs – plan to extend to WiFi APs through OpenWRT

## Slide 17: How to implement KEBAPP?
Android implementation components
KEBAPP Application Activity
KEBAPP Application Service
KEBAPP Application Model
KEBAPP Application
KEBAPP framework
jndn (java libs)
WiFiDirect libs
jndn-manager
Naming / partial matching functions
Application model / functionalities
KEBAPP background service
KEBAPP Foreground app UI
NFD<->WiFiDirect interface
NDN
tables / routing / fwd options
Service discovery / connectivity
Network devices
KEBAPP APP software
KEBAPP middleware
Android OS
NFD

## Slide 18
Thanks!
Dr Ioannis Psaras
University College London
http://www.ee.ucl.ac.uk/~ipsaras/
i.psaras@ucl.ac.uk

## Slide 19: BACKUP SLIDES

## Slide 20: Taxi Share App / Carpooling
Group commuters into taxis/vehicles locally
  User 1 wants to travel from A – C
  User 2 wants to travel from A – B, where B is along the route A – C
  User 3 travels from A – D and so on
Can’t think of many good reasons
not to do this locally...

## Slide 21: Online vs Offline Micropayment
Online Mode
Offline Micropayment
Central trusted authority issues certificates
Certificates trusted by nodes who pay with vouchers
Vouchers later validated when users get back online