## Slide 1: Multi-service Tag in ICN
draft-xia-icn-multiservtag-03
Yong Xia, Shihui Duan, Shu Liu, Rachel Huang
ietf99@Prague

## Slide 2: Motivation
Service delivery in current network lacks of correlation between content and IP addresses
  Difficult to do traffic engineering based on the services.
  The content delivery is not the most optimal.
ICN is born to solve the above problems by retooling the current protocol stack, so that host can be accessed by name-based data
  It is content aware.
To fulfill the requirement of ICN, a scheme that can mapping the service information into forwarding level will be necessary
  Multi-Service Tag is such a scheme to achieve the above mapping.

## Slide 3: What is Multi-Service Tag
Multi-service tag is a scheme like URI hierarchy naming scheme follows certain principles
  xlables = base64( CID + content summary + type + random number + signature )
  It’s a string which identifies tags and encrypts the contained information using base64.
  It can be contained in the packet header so that ICN routers or devices can easily analyze it to have the knowledge of the received data.
  It can work with the name to achieve specific network treatments, e.g., load balance, priority, etc.

## Slide 4: Multi-Service Tag Usage
Three elements
  Generating node (GN):
    Responsible for generating multi-service tag(s) for specific host or content.
    deployed in the edge of ICN network.
  Assembly node (AN):
    Responsible for maintaining the whole map of the multi-service tag in the network. Responsible for tag resolution for the first time.
    Specific server in the network
  Forwarding node (FN):
    Analyzing the receiving multi-service tag, and taking specific actions for it
    ICN routers in the network
FN
BFER
AN
ICN network
Source
GN
FN
GN
End user
Data flow
Control flow

## Slide 5: Benefits of Multi-Service Tag
Provide methods for network to aware content and take different treatments:
  Easy to network caching.
  Easy to priority services.
  Easy to do traffic engineering.

## Slide 6: Next Step
Welcome reviews.
Seeking for suggestions on the follow-up.