## Slide 1: NDN Protocol Design Principles Alex Afanasyev speaking for NDN Team https://named-data.net/project/ndn-design-principles/
July 16, 2017
ICNRG Interim Meeting, Prague

## Slide 2: NDN Protocol Principles Summary
Universality
Data-Centricity / Data immutability
Securing Data Directly
Hierarchical Naming
In-network name discovery
Hop-by-hop flow balance

## Slide 3: 1. Universality
NDN should be a common network protocol for all applications and network environments
Supported environments should include but not limited to:
  Direct device-to-device (D2D)
    IoT, wireless mesh networks, vehicle-to-vehicle networking, etc.
  DTN-style, unidirectional
  Today’s infrastructure-based communication
Protocol and packet format
  should be flexible, extensible, evolvable without flag days
  should not depend on “strong” absolute time clock synchronization

## Slide 4: 2. Data-Centricity / Data immutability
NDN should fetch uniquely named, immutable “data packets” requested using “interest packets”
Protocol and packet format should include only elements directly related to data
  Other elements needed in specific environments (e.g., in today’s infrastructure-based Internet) should go to the adaptation layer(s).
Data packets should have unique identifiers (names)
  Enable “disambiguation” in distributed system without centralized coordination.
  Any change of the carried content should be reflected as part of the data packet name (e.g., versioning)
  Related reference: “Immutability Changes Everything” by P. Helland

## Slide 5: 3. Securing Data Directly
Security should be the property of data packets, staying the same whether the packets are in motion or at rest
Directly secured and uniquely named data
  removes the requirement for direct channels between communicating ends and
  enables asynchronous production and consumption of named and secured data, e.g., using in-network caches and managed repos.
Consumers should be able to validate individual data
  Ideally, each packet should be verifiable on its own.
  As an engineering optimization, packets can be made verifiable in the context of others, provided that the context can be inferred from the data packet itself (its name or information in signature field).

## Slide 6: 4. Hierarchical Naming
Packets should carry hierarchical names to enable demultiplexing and provide structured context
Name hierarchy provides context to implement and enforce various security models, i.e., give structured restrictions on which keys can sign which data.
Hierarchical names allow “flat” naming models, if needed/desired by applications.

## Slide 7: 5. In-Network Name Discovery
Interests should be able use incomplete names to retrieve data packets
A consumer may not know the complete network-level name for data, as some parts of the name cannot be guessed, computed, or inferred beforehand.
Once initial data is received, naming conventions can help determine complete names of other related data
  majority of interests is expected to carry complete names
  in-network name discovery is expected to be used to bootstrap communication

## Slide 8: 6. Hop-by-Hop Flow Balancing
Over each link, one interest packet should bring back no more than one data packet
Hop-by-hop flow balancing enables each node to control load over its links.
  By deciding to sending interest over a link, router commits bandwidth for the returned data.
  By limiting the number of interests sent, each router and client node in the network control how much data it will receive.