## Slide 1
LPWAN WG
WG Chairs:
Alexander Pelov <a@ackl.io>
Pascal Thubert <pthubert@cisco.com>
AD: Suresh Krishnan
<suresh.krishnan@ericsson.com>
Interim Webex, April 26th, 2017

## Slide 2: Note Well
Any submission to the IETF intended by the Contributor for publication as all or part of an IETF Internet-Draft or RFC and any statement made within the context of an IETF activity is considered an "IETF Contribution". Such statements include oral statements in IETF sessions, as well as written and electronic communications made at any time or place, which are addressed to:
The IETF plenary session
The IESG, or any member thereof on behalf of the IESG
Any IETF mailing list, including the IETF list itself, any working group or design team list, or any other list functioning under IETF auspices
Any IETF working group or portion thereof
Any Birds of a Feather (BOF) session
The IAB or any member thereof on behalf of the IAB
The RFC Editor or the Internet-Drafts function
All IETF Contributions are subject to the rules of RFC 5378 and RFC 3979 (updated by RFC 4879).
Statements made outside of an IETF session, mailing list or other function, that are clearly not intended to be input to an IETF activity, group or function, are not IETF Contributions in the context of this notice. Please consult RFC 5378 and RFC 3979 for details.
A participant in any IETF activity is deemed to accept all IETF rules of process, as documented in Best Current Practices RFCs and IESG Statements.
A participant in any IETF activity acknowledges that written, audio and video records of meetings may be made and may be available to the public.

## Slide 3
Reminder: Minutes are taken * This meeting is recorded ** Presence is logged ***
* Scribe; please contribute online to the minutes at: http://etherpad.tools.ietf.org:9000/p/lpwan
** Recordings and Minutes are public and may be subject to discovery in the event of litigation.
*** From the Webex login

## Slide 4
4
4
4
4
4
Agenda bashing
16:00> Opening, agenda bashing (Chairs) [2min]
  Note-Well, Blue Sheets, Scribes, Agenda Bashing
  Milestones
16:02> Status of Drafts (Chairs) [5min]
16:07> LPWAN Overview Presentation and Discussion (Stephen Farrel) [10min]
  https://datatracker.ietf.org/doc/draft-ietf-lpwan-overview/
16:17> Static Context Header Compression for IPv6 and UDP (Ana, Laurent) [15min]
  https://datatracker.ietf.org/doc/draft-ietf-lpwan-ipv6-static-context-hc/
13:32> Static Context Header Compression Fragmentation Header (Carles Gomez) [20min]
  https://datatracker.ietf.org/doc/draft-ietf-lpwan-ipv6-static-context-hc/
13:52> LPWAN Static Context Header Compression (SCHC) for CoAP (Laurent) [5min]
  https://datatracker.ietf.org/doc/draft-ietf-lpwan-coap-static-context-hc/
13:55> AOB [QS]
Notes: 13:00> Opening, agenda bashing (5 min, Alexander, Pascal)
13:05> LPWAN Overview Presentation and Discussion (15 min) Presenter: Stephen Farrell https://datatracker.ietf.org/doc/draft-ietf-lpwan-overview/
13:20> LoRaWAN overview (15 min + 5mn Q&A) Presenter: Alper Yegin https://datatracker.ietf.org/doc/draft-farrell-lpwan-lora-overview/
13:40> SCHC LPWAN Fragmentation Header (15 min) Presenter: Carles Gomez https://datatracker.ietf.org/doc/draft-ietf-lpwan-ipv6-static-context-hc/
13:55> LPWAN Static Context Header Compression (SCHC) for IPv6 and UDP (10 min + 5mn Q&A) Presenter: Laurent Toutain, Ana Minaburo
https://datatracker.ietf.org/doc/draft-ietf-lpwan-ipv6-static-context-hc/
14:10> LPWAN SCHC for CoAP (20 min) Presenter: Laurent Toutain, Ana Minaburo https://datatracker.ietf.org/doc/draft-ietf-lpwan-coap-static-context-hc/
14:30> SCHC Implementation (5 mn) Presenter: Tomas Lagos14:35> Implementation of SCHC over Sigfox (5 mn) Presenter: Juan Carlos Zuniga14:40> Overview of 802.15.LPWA Interest Group Activities (10 min) Presenter: Charlie Perkins14:50> Possible future work items (10 mn) Presenter: Sri Gundavelli15:00> 0 min flextime

## Slide 5: Status
WG formed October 14th
Charter item #1 (Informational document)
  Baseline technology description
Charter item #2 (Standards track document)
  Enable the compression and fragmentation of a CoAP/UDP/IPv6 packet over LPWA networks

## Slide 6: Charter - Milestones

## Slide 7: IETF 98 Action items
Announce decision of SCHC IP/UDP/CoAP document structure.
Follow-up on the WI-SUN contribution for the LPWAN overview document.
Identify reviewers for the IP/UDP draft.
Follow-up on the reviewers who volunteered to review the SCHC CoAP draft.
  Diego Dujovne, Juan-Carlos Zuniga, Michel Veillette Carsten Borman

## Slide 8: Milestones
Dec 2016
Adopt LPWAN overview draft
Apr 2017
WG Last Call

## Slide 9: Milestones
Dec 2016
Adopt LPWAN overview draft
Adopt IP/UDP compression & fragmentation
Apr 2017
May 2017
WG Last Call

## Slide 10: Milestones
Dec 2016
Adopt LPWAN overview draft
Adopt CoAP compression
Apr 2017
May 2017
Jun 2017
WG Last Call
Adopt IP/UDP compression & fragmentation

## Slide 11: Milestones
Dec 2016
Adopt LPWAN overview draft
Adopt CoAP compression
Apr 2017
May 2017
Jun 2017
Adopt IP/UDP compression & fragmentation
Design team
Mar 2017

## Slide 12
LPWAN Overview
Editor: Stephen Farrell
(many contributors)
draft-ietf-lpwan-overview

## Slide 13: Wi-Sun Contribution?
Expected, no received
« I think the only action wrt the overview is that since we have no new contributed text with references on Wi-Sun (as was promised in Chicago) we ought decide to excise that section or to take some other action that would allow us to finish. »

## Slide 14
LPWAN IPv6/UDP SCHC
Authors:
Ana Minaburo <ana@ackl.io>
Laurent Toutain <laurent.toutain@imt-atlantique.fr>
Carles Gomez <carlesgo@entel.upc.edu>
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 15: Changes in IPv6 HC
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 16: Status
Proposed updates to draft-ietf-lpwan-ipv6-static-context-hc
  Intended as basis of new content for -03
Input from the list and from hallway meetings
  Thanks!
New text already on github
  https://github.com/lp-wan/ip-compression
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 17: Major changes
Move all CoAP SCHC specific behavior in IPv6
  Directions
    used for HL
  Position
    mapping-sent
Simplify LSB
  No arguments
  Compressed field length – MSB specified size
  Useful for variable length fields
Define the size of mapping-sent
  The minimum number of bit to send the index
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 18: Rules
Direction
Most of IP/UDP fields are bidirectional, except for Hop Limit
Position
Possible options as IPv6 addresses
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 19: Compression Decompression Functions
Add mapping-sent (from CoAP draft)
  Index is sent corresponding to the FV
  { 0: 2001:db8:1:1,
  1: 2001:db8:2:3
  2: 2001:db8:3:7}
Rename compute-length and compute-checksum
  More generic (IPv6, UDP, …)
draft-ietf-lpwan-ipv6-static-context-hc
Notes: So the CDF will only send the index of the list in order to identify the value used.
We have also changed the name of the compute*, we have put the name of the field that have to be computed as:
Compute-length or compute-checksum, etc. It is more generic and easily identified for IPv6 and UDP.

## Slide 20: Fragmentation
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 21: Reliability options: definition
Clarifying the available reliability options
Reluctance about “NACK” term
Reliability options
  No ACK
  Packet mode – ACK “Always”
  Packet mode – ACK on error
  Window mode – ACK “Always”
  Window mode – ACK on error
New terms used throughout current working (github) version
  Instead of the former UnR, RpP, RpW
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 22: Reliability options: discussion
Discussion on pros/cons of each reliability option
  Text plus summary table
  ‘No ACK’ not in the table: not actually tied to Packet or Window modes
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 23: Fragmentation header formats
Not the last fragment:
Last fragment:
Datagram Tag
Allows interleaving fragments from different IPv6 datagrams
Sequentially increasing
Starts from 0, wraps from 2T-1 to 0
T≥0
R, T, N, M to be decided by underlying L2 technology
Rule ID to signal “a fragment”: allows interleaving non-fragmented and fragmented IPv6 datagrams
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 24: ACK format
General format
Example
  11 fragments, 2nd and 9th lost
- Same value as DTag in the fragments for which this ACK is provided
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 25: ACK on error timer
Upon reception of the first fragment from an IPv6 datagram, the receiver starts a timer
The timer is reset every time a new fragment (same IPv6 packet) is received
  Assumption: not many long bursts of losses, so the initial timer value may be kept relatively small (e.g. a few expected RTTs)
  Difficult to estimate the time needed for a whole packet or window (may be large)
Upon timer expiration
  Packet mode: if last fragment not received, ACK transmitted
  Window mode: if last frag of window not received, ACK transm.

## Slide 26: ACK “Always” timer
Sender starts a timer upon sending last fragment
  Of the packet (Packet mode)
  Of the current window (Window mode)
Upon timer expiration, if no ACK received
  Sender retransmits last fragment and restarts the timer
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 27: Fragment renumbering
Minimize ambiguity about resent frags in Packet modes
Fragment renumbering
As for a new sequence of fragments
But last resent frag does not carry CFN=11..1
In -02
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 28: Aborting a fragmented transmission
Support both sender and receiver aborting fragm’ed tx
If fragment sender aborts
  It sends a format equivalent to a fragmentation header (without MIC) with Rule ID set to TBD_ABORT_TX, and CFN=11..1
If fragment receiver aborts
  It sends a Rule ID set to TBD_ABORT_RX
Resources are released
Question
  Aborting one specific IPv6 datagram vs aborting all on-going interleaved fragmented IPv6 datagram transmissions?
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 29: Editorial improvements
In different sections (e.g. also in the Introduction section)
No reordering assumption now introduced
  In the Introduction section
  In the introductory part of the Fragmentation section
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 30: Pending
Window bit for Window mode
  What about this?
L2 MTU variation
  Problem: L2 MTU becomes smaller and fragments need to be resent
  Option 1: abort the IPv6 datagram transmission?
  Option 2: trying to handle this (complex, increases overhead)
Quick downlink fragment delivery
  In some technologies, DL transmission only possible after UL transmission
  Uplink feedback after each fragment as an option?
A section to describe the tools before we use them
  CFN, ACK, bitmap, datagram tag…
draft-ietf-lpwan-ipv6-static-context-hc

## Slide 31
LPWAN CoAP SCHC
Authors:
Ana Minaburo <ana@ackl.io>
Laurent Toutain <laurent.toutain@imt-atlantique.fr>
draft-ietf-lpwan-coap-static-context-hc

## Slide 32: CoAP
No more normative
Description of CoAP fields compression
  Work in progress…
Read it !
Questions on
  Block / fragmentation
Analysis of common exchanges
  CoMi, LWM2M, IoTivity ?
  URI-path/Query not flexible: is it a problem?
Definition of timers:
  Impact in MID and Token size.
draft-ietf-lpwan-coap-static-context-hc

## Slide 33
AOB ?