## Slide 1: BGP-Based SPF RTGWG - Jan 2017
Keyur Patel, Arrcus
Acee Lindem, Cisco
Shawn Zandi, Linkedin
Gunter Van de Velde, Nokia
Derek Yeung, Arrcus
Abhay Roy, Cisco
Venu Venugopal, Cisco
<number>
Notes: <number>

## Slide 2: Motivation
Massively Scalable Data Centers (MSDCs) have implemented simplified layer3 routing
Operational simplicity has lead MSDCs to converge on BGP as their routing protocol
  Has support to announce both the underlay routes as well as the overlay routes using separate AFI/SAFIs
Centralized route control using some controller-based solution for simplified management
<number>

## Slide 3: Motivation (Cont’d)
Route Controller has a similar functionality as a Route Reflector
  May Reflect Routes
  Central Database for policy enforcements, management, etc.
However Route Reflector (not in the forwarding path) assumes a presence of an IGP protocol that help resolve bgp nexthop and its adjacencies for its clients
  IGP’s SPF builds directed graphs that ultimately resolves non connected nexthops
BGP based MSDCs solves this problem by establishing hop-by-hop (in-band) peering sessions
  Nexthop is always an address of a directly connected switch
Proposed solution helps towards deployment of Route Controllers and yet preserve operational simplicity by using BGP for underlay as well as the overlay routing
<number>

## Slide 4: Advantages of BGP SPF over Traditional BGP Distance Vector
Nodes have complete view of topology
  Ideal when BGP is used as an underlay for other BGP address families
Only network failures (e.g., link) need be advertised vis-à-vis all routes impacted by failure.
  Faster convergence
  Better scaling
SPF lends itself better to optimal path selection in Route-Reflector (RR) and controller topologies.
<number>
Notes: <number>

## Slide 5: Advantages of BGP-Based Solution
Already movement toward BGP as sole MSDC protocol as evidenced by “Use BGP for Routing in Large-Scale Data Centers” work in RTGWG
Robust and scalable implementations exist
Wide Acceptance – minimal learning curve
Reliable Transport
Guaranteed In-order Delivery
Incremental Updates
Incremental Updates upon session restart
No Flooding and selective filtering
Leads itself to multiple peering models including those with Route-Reflectors and Controllers
<number>

## Slide 6: Advantages of BGP-Based Controller Solution
Sparse BGP session topology with session paths for redundancy. Two cases:
  Control channel to every node.
  Hierarchy of Route-Reflectors which are directly or loopback connected (with static routes for the latter)
BGP SPF used for underlay with other BGP AFs used for overlay services
  Faster convergence of underlay and services in BGP
Controller also used for end-to-end traffic engineering paths possibly spanning other networks (e.g., core or access).
<number>

## Slide 7: BGP based Link-State Routing
Defined a new SAFI
  NLRI format is exactly same as BGP LS Address Family to carry link state information
BGP MP Capability and BGP-LS Node attribute to assure compatibility
Multiple Peering Models
BGP runs Dijkstra instead of Best Path Decision process
<number>

## Slide 8: BGP Best-Path
Next-Hop and Path Attribute basically along for the ride for BGP Link-State Address Family anyway
  Need to be announced based on RFC 4271 error handling
Decision Process Phases 1 and 2 replaced by SPF algorithm
Decision Process Phase 3 may be short-circuited since NLRI is unique per BGP speaker.
Need to assure the most recent version of NLRI is always used and re-advertised.
  Assured by existing protocol mechanisms
<number>

## Slide 9: BGP SPF
Starting with greatly simplified SPF with P2P only links in single area (i.e., SPT)
Will scale very well to many use cases.
Could support computation of LFAs, Segment Routing SIDs, and other IGP features.
  BGP-LS format includes necessary Link-State
Link-State AF is dual-stack AF since both IPv4 and IPv6 addresses/prefixes advertised
  BGP-LS format also supports VPNs but SPF behavior not defined.
  Work needed to define interaction with existing unicast AFs.
    Matter of local implementation policy
<number>

## Slide 10: Peering Model
BGP sessions with Route-Reflector or controller hierarchy.
  Link discovery/liveliness detection outside of BGP.
RR hierarchy can be less than fully connected but must provide redundancy
  Must not be dependent on SPF for connectivity
Controller could learn the expected topology through some other means and inject it.
  SPF Computation is distributed though.
  Similar to “Jupiter Rising: A Decade of Clos Topologies and Centralized Control in Google’s Datacenter Network”
<number>

## Slide 11: Next Steps
Further discussion
Collaboration
Consider Draft adoption
<number>