## Slide 1: Data Center Routing Challenges - LinkedIn
Shawn Zandi
Russ White

## Slide 2
Pod W
Spine
Spine
Spine
Leaf
Leaf
Leaf
Leaf
Spine
Pod X
Spine
Spine
Spine
Leaf
Leaf
Leaf
Leaf
Spine
Pod Y
Spine
Spine
Spine
Leaf
Leaf
Leaf
Leaf
Spine
Pod Z
Spine
Spine
Spine
Leaf
Leaf
Leaf
Leaf
Spine
Fabric 2
Spine
Spine
Spine
Fabric 4
Spine
Spine
Spine
Fabric 1
Spine
Spine
Spine
4,096 x100G ports
Non-Blocking
Scale-out
Spine
Spine
Spine
Fabric 3
Single SKU Data Center

## Slide 3: Complexity within Chassis
Chassis: Robust-yet-Fragile
  Complex due to NSR, ISSU, feature-sets, etc.
  Larger fault domain, Failover/Fail-back
  Indeterministic boot up process and long upgrade procedures
Moved complexity from big boxes to pizza boxes, where we can easily manage and control!
Better control and visibility to internals by removing black-box abstraction!
Same Switch SKU on ToR, Leaf and Spine (Entire DC)
Single chipset uniform IO design (same bandwidth, latency and buffering)
  True 5-Staged Clos Topology! with deterministic latency
Dedicated control plane, OAM and CPU for each ASIC

## Slide 4
W
X
Y
Z
W
X
Y
Z
W
X
Y
Z
Control Plane Complexity at Scale
Pod 1
2
32
…
1
Pod 11
322
352
…
321
Pod 21
642
672
…
641
Pod 31
962
992
…
961
W
X
Y
Z
2171
2170
2169
2168
2131
2130
2129
2128
2091
2090
2089
2088
2051
2050
2049
2048
2339
2338
2337
2336
2368
2369
2370
2371
2400
2401
2402
2403
2307
2306
2305
2304

## Slide 5: Control Plane Requirements
Fast, simple distributed control plane
No tags, bells, or whistles (no hacks, no policy)
Auto discover neighbors and build RIB
Minimal (to zero) configuration
Must use TLVs for future, backward compatible, extensibility
Must carry MPLS labels (per node/interface)

## Slide 6: Control Plane
Heavy weight; lots of features and “stuff” that are not needed
Modifications to support single IP configuration required
Does not supply full topology view
Proven scaling
BGP
Not proven to scale in this environment Light weight Most requirements for zero configuration are already met Provides full topology view
IS-IS
A lot of work
But could use bits and pieces from other places
Build New

## Slide 7: Forwarding Challenges
ECMP is blind
End to end path selection is required for some applications.
Application / Operator cannot easily enforce a path...

## Slide 8
Reachability ≠ Availability

## Slide 9: Other challenges
Auto-Configuration is important. Protocols should negotiate and come up without any manual configuration...
Provisioning can be simplified (lack of standardization)
Turning on a network requires another network (out of band)
(To hardware vendors) BMC in every switch is a MUST!