## Slide 1: IS-IS Spine-Leaf DC RTGWG Interim
draft-shen-isis-spine-leaf-ext-03
January 24, 2017

## Slide 2: Agenda
Spine-Leaf Use Cases
Extension Basics
TLV in Hello and/or CSF-LSP
Link and Node Down (Pure Clos)
Spine-Leaf Summary

## Slide 3: Spine-Leaf Use Cases
Spine-Leaf Setup popular in Data Center and Campus
Normally leaf-to-leaf traffic goes through one of the spine nodes, for east-west
Basically some ECMP load sharing from leaf to spine nodes
Rich mesh of spine-leaf IGP topology generates LSP flooding issues, in particular in the events of link and node down

## Slide 4: Extension Basics
ISIS Hello, Leaf-bit set
ISIS LSP flood to Spine
ISIS Hello, Use me as ‘default’
Normal ISIS Operation
Full IS-IS Database
Only default routes to Spines
S1
S2
L1
L2
L3
Core Layer with IS-IS
Access Layer
Aggregation Layer
0/0 -> S1, S2

## Slide 5: TLV in Hello/CSF-LSP
L: Leaf mode bit; R: Default Route Gateway bit; B: Leaf-Leaf bit
‘Default Route metric’ is removed. Can use IS-IS Reverse Metric from Spine to Leaf nodes
Optional Sub-TLVs: Leaf-Set, Info-Req, IPv4/6 Info-Advertise

## Slide 6: Link/Node Down (CLOS)
IIH S-bit, Leaf-Set
IIH L-bit, LSPs
S1
S2
L1
L2
L3
p1, p2, p3
L5
L6
S4
C1
C2
L4 picks S3 0/0, forward to L6 for p3
S3-L6 link down
S3 Leaf-Set lost L6 in sub-TLV
0/0 -> S3, S4
L4 picks S4, sending “forward prefixes behind node L6” Info-Req sub-TLV
S4 replies with “Prefixes are: p1, and p3 for L6” Info-Adv sub-TLV
p1, p3 -> S4
L4 adds more specific entries p1, p3 with nexthop to S4
L4 picks S4 lookup p3, forward to L6 for p3
S3
L4
Normal IS-IS, or L1-L2
Normal IS-IS,
Or L1-L2
S1-S4 include Leaf-Set sub-TLV when sending Spine-Leaf TLV
Info-Adv: p1, p3
Info-Req: L6
L3 Node down. Nothing special to do
S2 Node down. Nothing special to do

## Slide 7: Spine-Leaf Summary
Leaf (ToR) nodes have no topology of the network, SPF is not even needed
Rich connectivity without IGP flooding issues
If topology has interconnections among Spine nodes, or core layer connectivity, reroute is possible in events of link/node down
For pure CLOS without core layer, or to guarantee DC data forwarding latency, ‘negative routing’ or ‘conversational learning’ can be utilized to learn specific prefixes
Can be a ‘thin-layer’ of underlay in an overlay routing/forwarding Data Centers