## Slide 1: DetNet IP PSN vs. MPLS PSN A DetNet perspective Based on many discussions on the mailing list …
Balázs Varga, János Farkas
balazs.a.varga@ericsson.com, janos.farkas@ericsson.com
DetNet WG
Interim, 14th February, 2018

## Slide 2: DetNet functions & nodes (as per draft-ietf-detnet-architecture)
DetNet functions
  Congestion protection (Queuing) need: flow-ID
  Explicit routes (TE) need: flow-ID
  Service protection (PREF, IOD) need: flow-ID + Seq#
  Note: These three techniques can be applied independently …
DetNet nodes
  Edge node req.functions: 1, 2, 3
  Relay node req.functions: 1, 2, 3
  Transit node req.functions: 1, 2
TSN Edge Transit Relay DetNet
End System Node Node Node End System
+---------+ +.........+ +---------+
| Appl. |<---:Svc Proxy:-- End to End Service ---------->| Appl. |
+---------+ +---------+ +---------+ +---------+
| TSN | |TSN| |Svc|<-- DetNet flow ---: Service :-->| Service |
+---------+ +---+ +---+ +---------+ +---------+ +---------+
|Transport| |Trp| |Trp| |Transport| |Trp| |Trp| |Transport|
+-------.-+ +-.-+ +-.-+ +--.----.-+ +-.-+ +-.-+ +---.-----+
: Link : / ,-----. \ : Link : / ,-----. \
+........+ +-[ Sub ]-+ +........+ +-[ Sub ]-+
[Network] [Network]
`-----' `-----'

## Slide 3: Encapsulation? … Yes please, a DetNet pseudowire (DN-PW)
Encapsulation options analyzed in “draft-ietf-detnet-dp-alt”
  DN Service layer
  DN Transport layer
Criteria for data plane solution alternatives
  #1 ... #10
Application flow (Appl-PDU) encapsulated by end-system
  Appl-PDU_over_Ethernet
  Appl-PDU_over_IP
  And it may have its own proprietary fields …
Within the DN domain
  We do not define end-system encapsulation format, we should be agnostic
  We assume some kind of PW for the DN flow  build a concept based on spirit of rfc3985 + extended with IP as “emulated service”
.
.
+--------------+
| DN Service | PW, RTP/(UDP), GRE, …
+--------------+
| DN Transport | (UDP)/IPvX, MPLS LSPs/(TE)
+--------------+
.
.

## Slide 4: DN-PW over PSN based on spirit of rfc3985
What is needed for DN-PW?
  Flow-ID
  Seq#
What is NOT needed for DN-PW?
  Timing
  Flags, Frag
+---------------------+ +-------------------------+
| Payload |------------->| Raw payload if possible |
/=====================\ +-------------------------+
H Payload Convergence H-----------+->| Flags, seq #, etc. |
H---------------------H / +-------------------------+
H Timing H---------/--->| RTP |
H---------------------H / +-------------+ |
H Sequencing H----one of | |
\=====================/ \ | +-----------+
| PW Demultiplexer |---------+--->| L2TP, MPLS, etc. |
+---------------------+ +-------------------------+
| PSN Convergence |------------->| Not needed |
+---------------------+ +-------------------------+
| PSN |------------->| IP |
+---------------------+ +-------------------------+
| Data-Link |------------->| Data-link |
+---------------------+ +-------------------------+
| Physical |------------->| Physical |
+---------------------+ +-------------------------+
+---------------------+
| Payload |
/=====================\
H Payload Convergence H--+
H---------------------H | +--------------------------------+
H Timing H--------->| RTP |
H---------------------H | +--------------------------------+
H Sequencing H--+------>| Flags, Frag, Len, Seq #, etc |
\=====================/ | +--------------------------------+
| PW Demultiplexer |--------->| PW Label |
+---------------------+ | +--------------------------------+
| PSN Convergence |--+ +--->| Outer Label or MPLS-in-IP encap|
+---------------------+ | +--------------------------------+
| PSN |-----+
+---------------------+
| Data-Link |
+---------------------+
| Physical |
+---------------------+
dispensable
The common denominator: PW-label + Control-word
IP PSN
MPLS PSN

## Slide 5: Implementation? Simplicity …
Simplicity is the ultimate sophistication …
Should we bind end-system and DN domain encapsulation?
  We intend to be end-system agnostic …
  Appl-PDU will be tunneled anyway and encapsulated by DN Edge node
  Target of DN encapsulation: add flow-ID, Seq# + forwarding-rules
Ask the right question(s):
  Why to have different DN PW format for IP and MPLS?
  Why to implement DN functions twice (for both PSN type)?
!!! NOTE !!! We can split the data plane document
  if that helps to involve experts of IP / MPLS forwarding paradigm …

## Slide 6: Encapsulation examples
IP PSN
  Appl-PDU_o_PW+CW_o_IP
  or
  Appl-PDU_o_PW+CW_o_UDP_o_IP
MPLS PSN
  Appl-PDU_o_PW+CW_o_LSP
Conclusion stops here for DetNet WG (so far)
  Flow-ID and Seq# encoded using PW+CW
  Different technology domains have to interwork
    Difficulties at IP and MPLS domain borders minimized by common DN encapsulation
IP
MPLS
DetNet domain
Technology domains
Notes: RFC3985:
The PSN Convergence layer provides the enhancements needed to make the PSN conform to the assumed PSN service requirement. Therefore, this layer provides a consistent interface to the PW, making the PW independent of the PSN type. If the PSN already meets the service requirements, this layer is empty.
The Payload Convergence sub-layer is highly tailored to the specific payload type. However grouping a number of target payload types into a generic class, and then providing a single convergence sub-layer type common to the group, reduces the number of payload convergence sub-layer types. This decreases implementation complexity.

## Slide 7: Further possible work
To be done together with corresponding WGs
How to make flow identification easier for Transit nodes?
  Leverage PSN convergence layer
  Both for IP PSN and MPLS PSN scenarios
…
2/14/2018
7
+---------------------+ +-------------------------+
| Payload |------------->| Raw payload if possible |
/=====================\ +-------------------------+
H Payload Convergence H-----------+->| Flags, seq #, etc. |
H---------------------H / +-------------------------+
H Timing H---------/--->| RTP |
H---------------------H / +-------------+ |
H Sequencing H----one of | |
\=====================/ \ | +-----------+
| PW Demultiplexer |---------+--->| L2TP, MPLS, etc. |
+---------------------+ +-------------------------+
| PSN Convergence |------------->| Not needed |
+---------------------+ +-------------------------+
| PSN |------------->| IP |
+---------------------+ +-------------------------+
| Data-Link |------------->| Data-link |
+---------------------+ +-------------------------+
| Physical |------------->| Physical |
+---------------------+ +-------------------------+
+---------------------+
| Payload |
/=====================\
H Payload Convergence H--+
H---------------------H | +--------------------------------+
H Timing H--------->| RTP |
H---------------------H | +--------------------------------+
H Sequencing H--+------>| Flags, Frag, Len, Seq #, etc |
\=====================/ | +--------------------------------+
| PW Demultiplexer |--------->| PW Label |
+---------------------+ | +--------------------------------+
| PSN Convergence |--+ +--->| Outer Label or MPLS-in-IP encap|
+---------------------+ | +--------------------------------+
| PSN |-----+
+---------------------+
| Data-Link |
+---------------------+
| Physical |
+---------------------+
IP PSN
MPLS PSN
Notes: The PSN Convergence layer provides the enhancements needed to make the PSN conform to the assumed PSN service requirement. Therefore, this layer provides a consistent interface to the PW, making the PW independent of the PSN type. If the PSN already meets the service requirements, this layer is empty.
The Payload Convergence sub-layer is highly tailored to the specific payload type. However grouping a number of target payload types into a generic class, and then providing a single convergence sub-layer type common to the group, reduces the number of payload convergence sub-layer types. This decreases implementation complexity.