## Slide 1: Mobile Data Repositories at the Edge
Ioannis Psaras, Onur Ascigil, Sergi Reñé , George Pavlou
UCL, London, UK
Alex Afanasyev
Florida International University, Miami, USA
Lixia Zhang
UCLA, Los Angeles, USA
USENIX Workshop on Hot Topics in Edge Computing (HotEdge ’18)
Boston, MA, July 10, 2018

## Slide 2: Disruptive Edge Application Deployment
Humongous data production at the edges
  Global edge data production to exceed 1.6 zettabytes by 2020 [Cisco].
  Traffic flow is reversing – Intel proposed a reverse CDN
Problems
  Edge networks are not engineered for such large reverse flows
  Mobile backhaul network capacity is limited
  Upgrades to infrastructure are costly

## Slide 3: Edge-Data Production Examples
Biker’s helmet camera or car’s dash camera
  A system to report accident-related videos to insurance companies
  Only accident/collision related data is useful
  Detect collision and send, filter out the rest
Amber Alert system
  A system to detect missing children
  Uses public camera feeds and image processing
  Requires support for real-time storage/processing ideally near where data originates
Mobile Content Generating Apps
  Stream videos from phones

## Slide 4: Plain Connectivity is NOT the Answer
Data Upload
  Limited bandwidth and storage resources
Data Sharing
  Some data is useful locally
Data Processing
  Limited battery life
Cloud services
Edge data repositories
Internet
IoT
Vehicular networks
User devices
Public
Hotspot
Home
Hotspot
WISP
Notes: Just plain “Connectivity” is not sufficient to deal with the huge data production at the edges!

## Slide 5: Edge Data Repositories
Our proposal
  Complement network wire/cell connectivity with local edge data repositories
  Virtual user storage allowance
  Possibly as a service from the MNO
  A data-centric communication approach that secures data not the channel

## Slide 6: Edge Data Repositories
Store – Process – Send

## Slide 7: Edge Data Repositories
Benefits
  Support for asynchronous data collection
  Support for local processing of data
  Use storage as buffering to reduce peak data sending rates
  Provides inherent support for producer mobility
  Reduce Costs for ISP and MNO

## Slide 8: Store-Process-Send Model
Local processing of data
  Bandwidth (i.e., cost) reduction
  Increased performance (low latency) for users
Edge ISP
Cloud

## Slide 9: IP Challenges For Edge Data Production
IP = Point-to-point, “wire” connectivity between end-points
“Synchronous” communication is the only service offered
  IP forces applications to synchronize data immediately with cloud
    Uploading data to Dropbox does not actually require synchronous communication
Store-process-send model is not natively supported
  Local processing before synchronizing with cloud
    Can significantly reduce the information sent upstream
“Access to information” is not in the forefront
  Focuses on the location of information storage points
    Secures channels not the information itself
Mobility is problematic in IP
  Can break session-based communications

## Slide 10: Named Data Networking Communication Model
In-network storage
Caches
Interest
Data
Name
Optional fields
Interest packets
Name
Content
Signature
Data packets
Data is explicitly named instead of hosts
  The smallest unit of data (fits in a single packet) is a chunk
Naming data chunks enables the network to route based on names
  A persistent name that does not change with mobility
Data contains additional meta-data for authenticating data directly
  Signature: computed over the data
  Key verification info.: name or location of a certificate to verify signing keys
https://named-data.net/publications/tutorials/
Notes: Network figures out how to find the requested data
  Data is secured
  -> Can come from data producers, caches, in-network storage
Use hierarchical name to guide interests towards right network, box, application
Hop-by-hop forwarding
Symmetric paths for Interest-Data ->>> FEEDBACK
Stateful forwarding

## Slide 11: Name-Based Forwarding in NDN
/tmobile/a01abcd1/storage -> face X
/func/video/yolo -> face Y
/tmobile/a01abcd1/storage -> face X
/func/video/yolo -> face Y
/func/video/yolo -> face Y
….
/func/video/yolo -> face Y
….
/func/video/yolo -> face Y
….
/func/video/yolo -> face Y
….
/func/video/yolo -> face Y
….
/func/video/yolo -> face Y
….

## Slide 12: Cost Savings with Edge Processors and Repositories
Peering
Transit ISP
Eyeball ISP B
Eyeball ISP A
Transit
Transit
Transit
Cloud services
With Cost
No Cost

## Slide 13: Technical Challenges
Name resolution & producer mobility
  Steering requests for named data to the right storage location
    Challenging especially for near real-time applications
  Possible Solution: “DNS”-like system
    APs informs an authoritative NDNS server of a “forwarding hint”
Pulling application data at the APs
  Instantiate lightweight versions of applications inside the edge repositories.

## Slide 14: Future Directions: How to Manage Edge Data?
Metadata includes “hints” on how to manage data
  Data access Scope: local to the edge ISP, global or a mix of both
  Shelf-life: data is irrelevant after expiration
  Processing requirements: what kind of processing and where
  Deadlines: processing images to extract information within a certain time
Data management at the edges
  Pro-active: send all the incoming data to the cloud
  Re-active: inform the cloud of the arrival of data and wait for a request to send data
  Hybrid: use the meta-data to decide based on access scope, urgency, etc.
- How long and where to store data locally at the edges?
- When to process data locally?
- When to send data to cloud?

## Slide 15: Future Directions: Deployment considerations
How much storage/processing resources are needed at the edge?
  Applications may require keeping data around (e.g., for forensics)
Who owns and manages the storage and processing infrastructure?
  Edge ISP, third-party (e.g., CDN model), cloud service provider, etc.
Design of the edge repository architecture
  Service model and API
Deployment of data-centric communication at the edges
  Compatibility with IP
  Overlay vs underlay

## Slide 16: Conclusions
Edge Data Repositories to mitigate challenges of massive data production
  Buffer data when channel capacity is not sufficient and send it later
Store-process-send data for bandwidth savings and low-latency
Next step: developing mechanisms to manage data in a distributed system with heterogeneous (federated) control
Notes: Looking for feedback
Controversial points
Open issues not addressed in the paper
When would fail

## Slide 17: Backup Slides

## Slide 18: Increasing Data Production at the Edges
Cell networks do not have the capacity
  Mobile backhaul network capacity is limited
Increasing ISP costs.
  Orders of magnitude more upload traffic requires expensive upgrades to network
  ISPs will have to increase their charges/subscription costs
  This can be a show-stopper for IoT
Mobile Users
  Changing point of attachment (handoff) disrupts communications