## Slide 1: Network Measurement Framework and Path Tracing Utility for NDN
{ Lotfi.Benmohamed , Davide.Pesavento }@nist.gov

## Slide 2
Network Measurement
Network measurement is fundamental to network operation, application performance, and policy (not just research)
Stakeholder communities involved:
  Network user community
    What the network is doing to my packets
    measure QoS/QoE/SLA
    Academic community: networking research
  Network operators
    Anomaly detection/capacity planning
    Monitor network health/network forensics
  Network policy makers
    Define baseline for policies/pricing
    Measure adoption of technologies

## Slide 3
Goal
Empower NDN with a built-in measurement framework that
  can support multiple use cases,
  can be used by different applications that need to produce and/or consume network measurements
As new applications are developed, they
  can be instrumented with measurement probes, and
  make use of the framework to meet their measurement needs

## Slide 4
Design
Client-Agent interaction:
  4-way handshake
  Similar to RICE approach
     Measurement request
     Reply containing token
     Interest with token
     Data with results

## Slide 5
New Effort
DNMP: Distributed Network Measurement Protocol
  Pollere’s project funded under a NIST SBIR Phase1, started August 1.
Uses a brokerless publish-subscribe communications model for both the measurement requests and the resulting measurement data
  with goal to automate process of adding measurement probes using trust schema templates
 | Purpose | Duration | Funding level
Phase I | Feasibility | 6 months | Up to $100K
Phase II | R&D with commercialization plan | 2 years | Up to $300K

## Slide 6
Path Tracing
Think of path tracing as just one of the probes within the NDN Measurement Framework
Challenges for tracing in ICN vs. in IP
  In IP: one next-hop, one path
  In ICN, due to Caching/Multiple paths/Forwarding strategy: path(s) followed by one Interest can change over time even if routing (i.e. FIB entry) doesn’t change
Send a “trace” Interest to discover how a “regular” Interest would be routed
  Returns list of traversed nodes
  Associated RTTs
  Potentially other information as well
Parameters in trace request include:
  Exploring multiple paths
  Discover all available paths while bypassing strategy
  Ignore cached content to discover producers

## Slide 7
NDN-Trace Design

## Slide 8
CCNinfo / Contrace (https://tools.ietf.org/html/draft-asaeda-icnrg-ccninfo-01)
  For tracing multiple paths:
    requires PIT entries (created by trace requests) to be kept alive for some timeout period
    represents a significant departure from the “flow balance” principle
  Does not provide RTT measurements between the client node and intermediate nodes on the path
    only provides RTT between client and the node where the content is found (same as ping)
    also provides one-way delay, but requires synchronized clocks
  Trace built in the request packet as it travels upstream
ICN Traceroute (https://tools.ietf.org/html/draft-mastorakis-icnrg-icntraceroute-03)
  Resembles the mechanism used by IP traceroute tool
  Iteratively discovers the path by issuing Interests with a progressively increasing HopLimit field
  Uses new PathSteering header:
    constructed hop-by-hop while the reply travels back to the client
    included in subsequent trace requests that must be forwarded along the same path
Other Traceroute Proposals

## Slide 9: NMF: NDN Network Measurement Framework
NDN-Trace is just one of the many “probes” of the NDN Measurement Framework.
Poster at ACM ICN’17
  https://conferences.sigcomm.org/acm-icn/2017/proceedings/icn17-1005.pdf

## Slide 10: NMF: Status
Completed implementation of first version, including:
  Node agent with a few measurement probes
    https://github.com/usnistgov/nmf-agent
  C++ client library and interactive command-line tool
    https://github.com/usnistgov/nmf-client
Design of new features ongoing
  “Long-term” storage of measurements data (repo?)
  Access control (NAC?)
  Capability discovery/negotiation (pub-sub?)
Two main use cases
  Monitoring of operator networks, POV of the operator
  Measure/probe the network from the edge (RIPE Atlas, CAIDA Ark)

## Slide 11: NMF: Basic Interaction

## Slide 12: NMF: Eventual Goals
Extensibility
  Anyone can add a custom probe
  We will define an internal API for probes and provide a small library to help writing new probes
  App developers can integrate the framework in their app
Integration with access control protocols
  Measurement data can be sensitive
  Different clients have different access privileges
Long-term storage and querying of historical data

## Slide 13: NMF: Protocol Details
Verbs
  measure
  query
  retrieve
  interrupt
We have defined:
  Packet format, including TLV encoding
  Client <-> agent protocol

## Slide 14: NMF: Protocol Details
/<domain>/<node>/NMF/<verb>/<MParams>/<CIComps> (still based on v0.2 packet format)

## Slide 15: Old NDN-Trace Design

## Slide 16: Old NDN-Trace Design
Current v1 implementation is considered “done”
  Paper at ACM ICN’17
    https://conferences.sigcomm.org/acm-icn/2017/proceedings/icn17-86.pdf
  Tested by John DeHart on ONL
However:
  It requires non-trivial changes to every strategy
  Code is hard to maintain
  We’d like to have more power over the tracing process (e.g., trace only a subset of next hops)

## Slide 17: NDN-Trace: New “In-Forwarder” Design
Forwarding plane dispatches trace requests and responses to a traceroute module.
Strategy’s Interest forwarding API adds a dry-run mode.
  In dry-run mode, the chosen strategy offers its forwarding decisions, but does not transmit Interests or alter any state or data structures.
The traceroute module invokes strategy dry-run mode, transmits trace requests to next hops as needed, and collects and returns responses.

## Slide 18: NDN-Trace: Router Behavior
Let the strategy decide which next hops it would use for an Interest, assuming the Interest was retransmitted T times (T=0 for new Interests).
Send trace requests to the first K next hops chosen by the strategy.
Collect the first R trace responses that come back before a timeout TO expires, discard the rest.
Combine the responses into one (how?) and send it back.
trace module
forwarding
strategy
FIB
downstream
upstream

## Slide 19: NDN-Trace: Request
NFD 1
NFD 2
NFD 3
Client
I1
NFD 4
I2
I4
I3

## Slide 20: NDN-Trace: Reply
NFD 1
NFD 2
NFD 3
Client
D4
NFD 4
D3
D2
D1

## Slide 21: NDN-Trace: Router Behavior
Reply forwarding/aggregation: two approaches
  Hop-by-hop wrapping and signing, maintains existing signatures
  Discard signature, re-sign, send downstream
Trace process termination
  Producer
  Cache
  Either producer or cache, whichever is found first
  Abnormal termination
    No route
    Administratively prohibited
    …

## Slide 22: Bypassing the Forwarding Strategy
It can be argued that a path (next hop) that appears in FIB but would never be considered by a strategy is not a meaningful path.
  Some strategies do not use the FIB, e.g.:
    Flooding strategy always floods.
    Self-learning strategy may flood. FIB may be empty.
    Hyperbolic FIB (in eventual implementation) maps prefixes to coordinates instead of next hops. FIB does not contain next hops.
  Therefore the traceroute module should never look at the raw FIB entries without going through a strategy.
But what if we need to explore alternative paths that the current strategy would not consider?
  Do we need this functionality, e.g. for strategy debugging?

## Slide 23: NDN-Trace: Future Work
Currently exploring how to adapt NDN-Trace to take advantage of new features in NDN Packet Format v0.3
  Use typed name components to recognize trace Interests?
  Carry parameters in Interest Parameters TLV
Explore deployment/testing on the NDN Testbed
Lots more…