## Slide 1: Cross-domain network and service management in IBN
NMRG meeting // IEEE IM 2019
Focus on Intent-Based Networking (IBN)
Amina Boubendir
Orange Labs
France

## Slide 2: Cross-domain management in IBN

## Slide 3: Cross-domain management in IBN
Service Delivery and Network Slicing
Resource federation based on exposure APIs,
On-demand slice design,
Cross-domain deployment and orchestration
Automation of Orchestration & Management
Network and Service Exposure APIs
Multi-domain Resource Federation & Brokering

## Slide 4: Multi-domain federation and brokering
Different research works proposed models and frameworks for federated clouds through brokering to solve the issue of resource limitations so that Cloud service providers can share their resources as one Cloud infrastructure [1]–[3].
Also, components for resource discovery, resource allocation and mapping of virtual topologies over a federated multi-domain network virtualization environment have been proposed [4].
Moreover, a broker and federation architecture for resource allocation as per end-to-end SLA established in Cloud Networking Environment (IaaS and NaaS) has been proposed in [5].
Particularly, a model of Virtual Cloud using the interaction model of “Rent Out the Rented Resources” based on renting 3rd-party resources to provide its own services was defined in [6]. It aims at reducing cloud service costs by virtualizing already virtualized infrastructures where a cloud provider offers its own cloud services by acquiring and federating underutilized resources from 3rd-party enterprises.
Furthermore, falling within the “Edge Cloud” paradigm, solutions like Blue Horizon [7] proposes to extend the Cloud to the edge by gathering data from the edge.
Federation of resources through brokering has been a vast topic mainly for Cloud and IT resources, while a larger scope needs to be considered to embrace IT and all network (connectivity, access and core) resources belonging to different profiles of actors, not only cloud providers (enterprises, local organizations, etc.) for resource optimization.

## Slide 5: Network and Service Exposure
From the architectural point of view, many initiatives have targeted to address the challenges that operators face today in providing network services to OTT 3rd party actors.
Open Networking Foundation (ONF) defined SDN-based solution for “Operator Network Monetization” promoting SDN as a framework to enable interactions between operator’s network and applications [8] and has proposed “A Flexible NFV Networking Solution” using SDN for VNF deployment [9].
Also, an SDN-aware NFV architecture for operators is presented in [10] enabling dynamic provisioning of network services.
Moreover, T-NOVA project [11] proposed an operator architecture framework for providing network functions-as-a service while UNIFY project proposed a network unified programmability framework [12].
Such initiatives have focused on the integration of SDN and NFV to enable efficient deployment of network services for applications. The interactions between the network operator and 3rd-party actors and the federation of their resources have not been jointly addressed.

## Slide 6: Network Slicing for a cross-domain service
Regarding network slicing, there is no consensus on one definition for a network slice. Several definitions exist in the literature [19]–[24]. For example, the logical architecture for network slicing based 5G systems proposed in [22] includes an introduction to the fundamental concepts of network slicing.
These approach does not take into account the integration of resources from different actors and the means of enabling an interaction between different 5G system domains.
In [25], a network slicing mechanism was defined for network edge nodes. This approach relies on cloud edge to achieve network slicing and core network functions and entities need to be shifted and placed into the network edge.
It is important to consider that a network slice spans end-to-end across different network domains and may include network functions deployed in the core, access and edge networks [26].

## Slide 7: Automated Management and Orchestration
Regarding orchestration and management, ETSI NFV reference framework defines virtual resource management and network service orchestration [27]. Different initiatives like TeNOR NFV orchestrator platform [28] provide orchestration for automated management of network services over virtualized infrastructures.
Further, Open Source projects like Open NFV (OPNFV) [29], Open Source MANO [30], Open Baton [31] have implemented ETSI NFV architectural framework for NFV orchestration and management. However, these initiatives have been designed for the orchestration of a single domain where NFVO has full access and control over resources.
More recently, Open Network Automation Platform (ONAP) [32] has emerged as the orchestration platform for carrier-scale automatic VNF and network services orchestration and management. The Active and Available Inventory (AAI) in ONAP provides real-time views of available resources and services and their relationships and is thus equivalent to a Resources Cartography. However, ONAP AAI, in its actual version, stores the resources and services of a single provider or tenant.
The orchestration layers defined in these initiatives do not consider embracing resources from different domains and actors; they do not define resources federation orchestration and management functions with a brokering layer enabling multi-actors interactions and are not suitable for multi-domains network service orchestration. It is important to rely on approaches like X-MANO [33], BluePlanet [34] and ONAP future developments, as bases to allow for cross-domain multi-actors management and orchestration.

## Slide 8: Network (Slice)-as-a-Service Architecture
Network Operator
Tenant / Vertical actor
Network Domains
Private Infrastructure Domains
Network Slice as a Service
Multi-Domain Resource Broker
Virtual Network/Applicative Functions Provider

## Slide 9: Network (Slice)-as-a-Service Architecture
OSS/BSS functions
Management Operations, SLAs
Application providers, Application developers, Application users,…
NFV Infrastructure
Virtual Computing
Computing Hardware
Virtual Storage
Storage Hardware
Virtual Networking
Networking Hardware
Virtualization Layer
VM 2
VN 2
VM 1
VN 1
EM 5
VNF5
EM 4
VNF 4
EM 3
VNF 3
EM 4
VNF 4
EM 2
VNF 2
EM 1
VNF 1
Management and Orchestration
SDN Controller
SDI Manager
VI Manager
VNF Managers
VN Controller
VN Manager
Orchestrator and SDN Applications
NaaS Software Infrastructure Layer
Network Service Description
Network-as-a-Service Exposition Layer
Network Service Composition
Network Service
Discovery
NaaS Exposition Layer
Publish descriptions
Discovery and Selection

## Slide 10: Automation for Management and Orchestration

## Slide 11: Multi-actor cross-domain management
Access
Advertisement
Non
-
shareabl
e
area
S
hareab
le
area
Access
Advertisement
Non
-
shareabl
e
area
S
hareab
le
area
Neighbourhood
discover
y
Neighbourhood
discover
y
Neighbourhood
discover
y
Database
MNO’s cloud (central and edge)
Private Infrastructure owner
3
rd
party
performance DB
Operator access nodes
Non operator
access nodes
Crowd
-
sourced performance databases
g
ather
throughput&latency
measurements
made on the
various
accesses
.
Tenant
Access
Advertisement
Non
-
share
-
able
area
Share
-
able
area
Neighbourhood
discover
y
Access and
resources
cartography
(e.g.
scan+ANQP
)
Neighbourhood
discover
y
GW
GW
Non
-
shareable
area
S
hareable
area
Access
registration
Network
slicing
RNCE
Slice
instanciatio
n

## Slide 12: Application of cross-domain slicing

## Slide 13: Identified challenges
Need to consider a large scope of resources embracing IT and all network (connectivity, access and core) resources belonging to different profiles of actors,
The interactions between the network operator and 3rd-party actors and the federation of their resources need to be jointly addressed,
Need to investigate management and orchestration of network slices that span across different network domains and may include network functions deployed in the core, access and edge networks,
Work on evolving approaches and initiatives targeting the cross-domain multi-actors management and orchestration,
….

## Slide 14: Merci

## Slide 15: References
[1] Y. Demchenko, C. Ngo, C. de Laat, and C. Lee, “Federated access control in heterogeneous intercloud environment: Basic models and architecture patterns,” in 2014 IEEE International Conference on Cloud Engineering, pp. 439–445, March 2014.
[2] S. S. Chauhan, E. S. Pilli, and R. C. Joshi, “A broker based framework for federated cloud environment,” in 2016 International Conference on Emerging Trends in Communication Technologies (ETCT), pp. 1–5, Nov 2016.
[3] M. Aazam and E. N. Huh, “Broker as a service (baas) pricing and resource estimation model,” in 2014 IEEE 6th International Conference on Cloud Computing Technology and Science, pp. 463–468, Dec 2014.
[4] C. Pittaras, C. Papagianni, A. Leivadeas, P. Grosso, J. van der Ham, and S. Papavassiliou, “Resource discovery and allocation for federated virtualized infrastructures,” Future Generation Computer Systems, vol. 42, no. Supplement C, pp. 55 – 63, 2015.
[5] M. Hamze, N. Mbarek, and O. Togni, “Broker and federation based cloud networking architecture for iaas and naas qos guarantee,” in 2016 13th IEEE Annual Consumer Communications Networking Conference (CCNC), pp. 705–710, Jan 2016.
[6] S. Malik and F. Huet, “Virtual cloud: Rent out the rented resources,” in 2011 International Conference for Internet Technology and Secured Transactions, pp. 536–541, Dec 2011.
[7] Horizon Project. Blue Horizon, Edge Insights. [Online] Available on: https://bluehorizon.network/documentation/introduction.

## Slide 16: References
[8 ] ONF, Solution Brief, Operator Network Monetization Through OpenFlow-Enabled, April 2013.
[9] Open Networking Foundation (ONF). Solution Brief, OpenFlow-Enabled SDN and Network Functions Virtualization, February 2014.
[10] J. Matias, J. Garay, N. Toledo, J. Unzilla, and E. Jacob, “Toward an sdn-enabled nfv architecture,” IEEE Communications Magazine, vol. 53, pp. 187–193, April 2015.
[11] G. Xilouris, E. Trouva, F. Lobillo, J. M. Soares, J. Carapinha, M. J. McGrath, G. Gardikis, P. Paglierani, E. Pallis, L. Zuccaro, Y. Rebahi, and A. Kourtis, “T-nova: A marketplace for virtualized network functions,” in 2014 European Conference on Networks and Communications (EuCNC), pp. 1–5, June 2014.
[12] P. Skldstrm, B. Sonkoly, A. Gulys, F. Nmeth, M. Kind, F. J. Westphal, W. John, J. Garay, E. Jacob, D. Jocha, J. Elek, R. Szab, W. Tavernier, G. Agapiou, A. Manzalini, M. Rost, N. Sarrar, and S. Schmid, “Towards unified programmability of cloud and carrier infrastructure,” in 2014 Third European Workshop on Software Defined Networks, pp. 55–60, Sept 2014.
[13] A. Gran, S. C. Lin, and I. F. Akyildiz, “Towards wireless infrastructure-as-a-service (wlaas) for 5g software-defined cellular systems,” in 2017 IEEE International Conference on Communications (ICC), pp. 1–6, May 2017.
[14] I. F. Akyildiz, P. Wang, and S.-C. Lin, “Softair: A software defined networking architecture for 5g wireless systems,” Computer Networks, vol. 85, no. Supplement C, pp. 1 – 18, 2015.]

## Slide 17: References
[15] G. Xilouris, E. Trouva, F. Lobillo, J. M. Soares, J. Carapinha, M. J. McGrath, G. Gardikis, P. Paglierani, E. Pallis, L.
[19] M. Berman, J. S. Chase, L. Landweber, A. Nakao, M. Ott, D. Raychaudhuri, R. Ricci, and I. Seskar, “Geni: A federated testbed for innovative network experiments,” Comput. Netw., vol. 61, pp. 5–23, Mar. 2014.
[20] G. Americas, Network Slicing for 5G Networks and Services; White paper, November 2016.
[21] X. Li, M. Samaka, H. A. Chan, D. Bhamare, L. Gupta, C. Guo, and R. Jain, “Network slicing for 5g: Challenges and opportunities,” IEEE Internet Computing, vol. 21, no. 5, pp. 20–27, 2017.
[22] H. Zhang, N. Liu, X. Chu, K. Long, A. H. Aghvami, and V. C. M. Leung, “Network slicing based 5g and future mobile networks: Mobility, resource management, and challenges,” IEEE Communications Magazine, vol. 55, no. 8, pp. 138–145, 2017.
[23] R. Trivisonno, X. An, and Q. Wei, “Network slicing for 5g systems: A review from an architecture and standardization perspective,” in 2017 IEEE Conference on Standards for Communications and Networking (CSCN), pp. 36–41, Sept 2017.
[24] Z. Kotulski, T. Nowak, M. Sepczuk, M. Tunia, R. Artych, K. Bocianiak, T. Osko, and J. P. Wary, “On end-to-end approach for slice isolation in 5g networks. fundamental challenges,” in 2017 Federated Conference on Computer Science and Information Systems (FedCSIS), pp. 783–792, Sept 2017.
[25] J. Heinonen, P. Korja, T. Partti, H. Flinck, and P. Pyhnen, “Mobility management enhancements for 5g low latency services,” in 2016 IEEE International Conference on Communications Workshops (ICC), pp. 68–73, May 2016.
[26] M. Richart, J. Baliosian, J. Serrat, and J. L. Gorricho, “Resource slicing in virtual wireless networks: A survey,” IEEE Transactions on Network and Service Management, vol. 13, pp. 462–476, Sept 2016.

## Slide 18: References
[15] G. Xilouris, E. Trouva, F. Lobillo, J. M. Soares, J. Carapinha, M. J. McGrath, G. Gardikis, P. Paglierani, E. Pallis, L.
[27] ETSI NFV ISG, Network Functions Virtualisation (NFV); Management and Orchestration. ETSI GS NFV-MAN 001 V1.1.1.
http://www.etsi.org/technologies-clusters/technologies/nfv, Dec 2014.
[28] T-NOVA Project. TeNOR NFV Orchestrator. [Online] Available on: http://www.t-nova.eu/open-source/.
[29] Linux Foundation. Open Platform for NFV (OPNFV). [Online] Available on: https://www.opnfv.org/.
[30] ETSI NFV ISG. Open Source Management And Orchestration (OSMANO). [Online] Available on: https://osm.etsi.org/.
[31] Open Baton, NFV-MANO compliant framework. [Online] Available on: https://openbaton.github.io/.
[32] Open Networking Automation Platform (ONAP) project. [Online] Available on: https://www.onap.org/.
[33] A. Francescon, G. Baggio, R. Fedrizzi, E. Orsini, and R. Riggio, “Xmano: An open-source platform for cross domain management and orchestration,” in 2017 IEEE Conference on Network Softwarization (NetSoft), pp. 1–6, July 2017.
[34] Ciena, Blueplanet. Multi-domain service orchestration. [Online] Available on:/http://www.blueplanet.com/products/multi-domainservice-orchestration.html.

## Slide 19: Multi-domain Orchestration: X-MANO
The aim is to show that the X-MANO is able to deploy network services with a negligible overhead and without imposing limitations on the underlying domains.
The X-MANO architecture. A federation manager (fm) is interfaced with one or more federation agents (fa). The user interacts with the FM trough a web dashboard. Each domain is locally managed by its local domain orchestrator/manager (dom).
A cross-domain link is created between the two domains using openvpn. Zabbix is used to monitor each domain. Each instantiated VNF can be accessed by the FA to trigger actions (i.e., local scripts).