## Slide 1: ACP status IETF 2020 virtual interim 1
draft-ietf-anima-autonomic-control-plane-24
Toerless Eckert tte+ietf@cs.fau.de (Futurewei USA)
Michael Behringer michael.h.behringer@gmail.com
Steinthor Bjarnason sbjarnason@arbor.net
v1.0

## Slide 2: Status
Around IETF 106:
  draft-ietf-anima-autonomic-control-plane-21
  Open Discuss about use of rfc822name by security review
  Assignment of new AD responsible for document: Eric Vyncke
    Ignas Bagdonas excused
  Invalidation of (2) IESG reviews due to IESG member term ends
  Eric Vyncke:
    Provide his Review
    Then open 2nd IETF last call, then back to final approval by IESG
Since then
  Jan: Review from Eric
  Feb/March: work on -23/24
  Review by Russ Housley
  Discuss with IPsec experts

## Slide 3: Status
Open issues:
  Still rfc822name discuss. (Ben Kaduk, Russ Hously, Valery Smyslov?)
  Argument: “Using rfc822name seems wrong”
    Other solutions have choosen different approach
  No supporting arguments / rfc references why this would be wrong
  No discuss yet reviewing the list of bullet points from ACP section 6.1.2
  Finalizing review from Russ
  Issue with some security reviews: lot of “this is not right”, but little help “this is what would be right” (text proposals)
  (not applicable to Bens feedback, long/detailled proposal how to change rfc822name)
  Finalizing of IPsec text details (need to remove some text, references to existing docs should be sufficient)

## Slide 4: Mayor -21 to -24 changes
Restructured secure channel text
  6.7.1 (new) general considerations
    No MTI protocol, weakest link security, physical link security, Reuse of L2 encryption
  6.7.2 (new) common requirements
    Forward Secrecy, encryption equal better AES265, explicit closure of channels upon authentication expiry, create strict profiles for new channel protocols (do not include legacy crypto, attempt to minimize MTI).
  6.7.3 IPsec
    RFC8221 (IPsec/ESP) adjustments (stricter profile) – no NULL encrypt, only ENCR_AES_GCM_16 MTI, PERFORMANCE based requirement against ENCR_CHACHA20_POLY1305, ENCR_AES_CBC, ENCR_AES_CCM_8 – if faster ! Explanations, e.g.: Fallback crypto (ENCR_CHACHA20_POLY1305) only useful if it does not kill performance.
    RFC847 (IKEv2) – use of ACP certificate (ID_IPv6_ADDR ACP addr), MUST use digital signature requirements.
    Not trying to strip RFC8221 option (compared to Ipsec): assume reuse of big („bloated“) RFC8221 implementation still safer than attempting to define subset (software only, not performance issue!).

## Slide 5: Mayor -21 to -24 changes
6.1.3.1 Real time clock (non) requirement
  Stolen partially from BRSKI. MUST use RT clock if assume reliable to verify time-stamps of certs. MAY ignore if no RT clock, but re-check once trusted time acrosss ACP available. Ultimately, there are some clock risks when theree is no RT clock (property of cert based crypto systems).
DTLS
  MUST DTLS v1.2, or any newer version that can negotiate down to 1.2. Text to encourage DTLS 1.3 once RFC, avoid blocking reference against DTLS1.33 draft. RFC-editor note that this text will become MUST if there is DTLS 1.3 RFC in ACP RFC AUTH48.
  Explanations how ACP implementation space will be slot to support DTLS 1.3 to justify MTI for 1.2.
  DTLS (string in grasp, meaning in doc): Any version that can negotiate down to DTLS 1.2. Future ACP RFC rev could introduce “DTLS1.3” = any version that can negotiate down to 1.3, once we know DTLS1.2 is really obsolete in firmware of IOT devices.

## Slide 6: Mayor -21 to -24 changes
TLS (for end-to-end GRASP inside ACP)
  MUST TLS 1.2, SHOULD TLS 1.3.
  Small limited profile of crypto, (AES >= 256, >= SHA384), TLS_ECDHE_RSA_WITH_AES_256_GCM_SHA384 and TLS_ECDHE_ECDSA_WITH_AES_256_GCM_SHA384
  Goal is to be close to TLS 1.3 without expecting all APC devices to support TLS 1.3
  Hopefully faster to do followup RFC to retire TLS 1.2 than DTLS 1.2, but very unsure about low-end (IOT like) devices.
RPL
  Decoder ring explanation for RPL data plane artefact RFCs.

## Slide 7: Mayor -21 to -24 changes
6.12.5.2
  Alaborated better on how to map secure channels into ACP (virtual) interface
ACP over L2
  Section had very little (no ?) review in before Eric. Rewrote explanation how L2/L3 switches can implement ACP with no new HW requirements (filtering GRASP messages sufficient to break L2 into multiple ACP subnets). Moved security issues with this to security section.
8.1.1 Added requirement for filtering of RPI headers on ACP edge nodes.

## Slide 8
time
Thank You!