## Slide 1: A YANG Model for Network and VPN Service Performance Monitoring draft-www-bess-yang-vpn-service-pm-06
Qin Wu (Huawei)
Mohamed Boucadair (Orange)
Oscar Gonzalez de Dios (Telefonica)
Wen Bin (Comcast)
Change Liu (China Unicom)
Honglei Xu (China Telecom)
IETF 107
April 28, 2020
<number>
IETF107 BESS Virtual meeting
Notes: <number>

## Slide 2: Recap
Lower layer Network performance measurement protocol and methodology for Ethernet traffic, IP traffic, MPLS traffic:
  IP traffic performance measurement protocol such as OWAMP, TWAMP
  IP traffic performance metric such as one way delay, roundtrip delay, loss, PDV
  MPLS traffic performance measurement such as MPLS loss and delay measurement for MPLS[RFC6374], MPLS-TP loss and delay measurement[RFC6375]
  Ethernet traffic performance measurement such as Y.1731
None of these performance monitoring mechanism can be used to report service level or end to end network performance
This document defines a YANG model for both Network Performance Monitoring and VPN Service Performance Monitoring that can be used to
  monitor and manage network performance on the topology at higher layer
  or the service topology between VPN sites.
IETF107 BESS Virtual meeting
<number>

## Slide 3: Status update since Singapore meeting
Firstly discussed in IETF 103 BESS meeting in Bangkok and there were consensus to adopt this work as BESS work item and It was in the queue for WG adoption.
Secondly presented in IETF 106 TEAS meeting in Singapore and solicit input and feedback.
Update since last version:
  Add Mohamed Boucadair and Oscar as new coauthors of this draft
  Add VPN summary statistics parameters at the network level.
  Add reference time and measurement interval associated with performance measurement data
  Replace average-delay-value at the link level with low-delay-percentile, middle-delay-percentile and high-delay-percentile
  Replace average-jitter-value at the link level with low-jitter-percentile, middle-jitter-percentile and high-jitter-percentile
  Add low-percentile, middle-percentile, high-percentile at the network level
  YANG data model changes

## Slide 4
Use Case:Real Time VPN Service Monitoring
Network Performance data source: Network device, management system
Performance measurement method: IPPM method, MPLS Loss and Delay Measurement
End to end Network performance calculation method: using PCEP solution [RFC8233] [RFC7471] [RFC7810] [RFC8571]
The goal: Report end to end network performance or service level VPN network performance
One way delay between PE1 in site A and PE2 in SiteB
Packet loss between CE1 and PE1 in site A
WAN link bandwidth between CE2 and PE2 within Site B
Measure per link network performance in the underlying network using MPLS loss and delay measurement method and report in aggregated way.
A
B
C
D
E
F
100
200
300
400
500
Controller
VPN
Node C
Node E
Link 500
Monitor per tunnel network performance report via pub/sub model or on demand RPC retrieval model
Optimize network based on VPN service performance monitoring
3
2
1

## Slide 5: Relationship between VPN service topology and underlay topology
Mapping between Overlay and Underaly:
  The Site-1,A,B,C are mapped to node (1,2),(3,4),(4,5)
  while Site-2 A,B,C are mapped to node (6,7),(8,9)(10,11) in the underlying physical network.
VPN-svc 1: supporting hub-spoke communication for Customer 1 with connecting the customer’s access at 3 sites.
VPN-svc 2: supporting hub-spoke disjoint communication for Customer 2 with connecting the customer’s access at 3 sites
IETF107 BESS Virtual meeting
<number>
Establish the relationship between underlay topology and VPN service topology
and bind the VPN service to the tunnel (e.g., SR-TE tunnel)

## Slide 6: Model Design Overview
Augment I2RS Network Topo model [RFC8345]
  with service topology parameters and vpn summary statistics info at network level
  With site role of service topology parameters at node level
  With performance attribute at link level and termination-point level
The measurement interval and reference-time associated with these performance data usually depends on configuration parameters.
<number>
IETF107 BESS Virtual meeting
I2RS Network Topo
Model
VPN Service Performance Model
Changes to the previous version

## Slide 7: Performance Monitoring Data Retrieval
Use subscription model [RFC8641] to subscribe to their interested network performance data in the data source.
IETF107 BESS Virtual meeting
<number>
Use RPC model to fetch network performance data on demand, e.g., the client requests packet-loss- count between PE1 in site 1 and PE2 in site 2 belonging to VPN1.
1.Retrieval via YANG Push
2.On-demand Retrieval via RPC polling model

## Slide 8: Way Forward
Sufficient support in IETF 103 and already in the queue for WG adoption.
Adoption?
  The authors believe this draft is a good shape for WG adoption
IETF107 BESS Virtual meeting
<number>