## Slide 1: IGMP and MLD Proxy for EVPN
Interim meeting IETF 107 , APR 2020

## Slide 2: Current Status
WGLC had been done IETF 106.
During WGLC, there was comment on one of the filed for Route type 8. Had discussion between multiple vendors & looks there is no real use case and good to remove this field.
During update here, showing what change is being proposed for draft.

## Slide 3: Discussion post IETF 106
 | Option 1 | Option 2 | Option 3
Change | Remove Sync Seq # (4 bytes) from route 8 | Make Sync Seq # as reserved field | Leave EVPN RT-8 as is. And get new code point for route without Seq number. And slowly migrate to only new route
Impact | RR needs to understand both len (Old and New) All routers need to understand both length (in case some implementation do session reset ) | Implementation who do not Seq number need to add 4 byte reserve field. | More implementation need from each vendor, and possible new CLI . May add complexity to vendors as well as customers to operate.

## Slide 4: Proposed NLRI Change 9.3 Multicast Leave Synch Route
Current Text
Proposed Text

## Slide 5: Impact to known Vendors
Vendor | Current implementation | Expected change Change
Cisco | EVPN route type 8 , sends without Seq number. As RR accept both route | Send and reflect EVPN RT-8 with 4 bytes of reserve field
Juniper | EVPN route type 8, sends with Seq number | No change
Nokia | Supports with and without seq number and originates without sequence number | Add support for reserve field. Sends RT-8 with 4 byte of reserve field and accepts routes with 4 byte of reserve field.
Arista | Handles both case (using CLI) | No change, but rest other vendor always going to be with reserve field
This list is having only Vendors name who confirmed implementation. It may not be complete list

## Slide 6: Questions ??