## Slide 1: draft-ietf-bier-mld BIER Ingress Multicast Flow Overlay using Multicast Listener Discovery Protocols
Pierre Pfister, pierre.pfister@darou.fr
IJsbrand Wijnands, ice@cisco.com
Markus Stenberg, markus.stenberg@iki.fi
Stig Venaas, stig@cisco.com
Cui (Linda) Wang, lindawangjoy@gmail.com
Zheng (Sandy) Zhang, zhang.zheng@zte.com.cn

## Slide 2: BIER MLD/IGMP Sender Info
Currently the source address is assumed to be the BIER prefix so that one can derive the BFR-ID of the sender, and using configuration and potentially the destination address to determine the sub-domain.
This info can be derived from the BIER header, but the L3 code may not have access to the BIER header.
For pim it was decided to add a join attribute with Sender Info.
For BIER IGMP/MLD use extension mechanism in draft-ietf-pim-igmp-mld-extension.
  The extension would only need to be supported by BIER routers that use BIER/IGMP overlay.
  Fairly small code change, mostly just parsing the extension.

## Slide 3: IGMP/MLD BIER Extension Format
  0 1 2 3
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  |Extension Type | Sub-domain ID | BFR-ID |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  | BFR-Prefix |
  ~ ~
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  The extension type would be a fixed value assigned by IANA identifying this particular format
  The remaining fields identifies the BIER router that originated the IGMP/MLD message