## Slide 1: A Yang Data Model for Optical Impairment-aware Topology
Co-authors (editors):
Young Lee (SKKU)
Jean Luc Auge (Orange)
Victor Lopez (Telefonica)
Gabriele Galimberti (Cisco)
Dieter Beller (Nokia)
Co-authors/contributors:
Haomian Zheng (Huawei)
Italo Busi (Huawei)
Nicola Sambo (Scuola superior S.Anna)
Julien Meuric (Orange)
Esther Le Rouzic (Orange)
Sergio Belotti (Nokia)
Enrico Griseri (Nokia)
Gert Grammel (Juniper)
Jonas Martenson (RISE)
Aihua Guo (Futurewei)
draft-ietf-ccamp-optical-impairment-topology-yang-03

## Slide 2: Major Activities since May Interim Meeting
Weekly CCAMP WebEx meetings (Thu, 4-5pm CEST)
Topics addressed: TRANSPONDER model
  Reconcile the different transponder models (WSON, flexgrid, optical impairments) present in CCAMP
  Reconcile the transponder model with complementary interface model contained in draft-ietf-ccamp-dwdm-if-param-yang
  Proceed with new layer0-types-ext draft containing common YANG structures and definitions (typedefs, identities, groupings)

## Slide 3: Optical transponder properties capabilities model
Definition of Optical transponder capabilities
  3 different modes to express the transceiver capability of a transponder:
    ITU-T G.698.2 application codes. Guarantees interoperability since encompass also optical path constraints parameters for a single fiber type.
    Organizational/vendor specific set of parameters subsumed by an “operational mode” identifier. It guarantees transponder interoperability but is not defined by an SDO.
    Explicit mode, with an explicit list of parameters to consistently configure the mode of operation for the transceivers. No optical path parameters: it does not guarantee interoperability. An if-mode represents the identifier for an “explicit” set of parameters.
    See definitions https://github.com/ietf-ccamp-wg/ietf-ccamp-layer0-types-ext/blob/transponder-model-types/modes-definitions.md
  3 new common groupings defined in the layer0-types-ext to represent the attributes for capabilities and configuration
  New common structure to define the supported modes of operation:
    supported-mode

## Slide 4
TX
(foo)
RX
(bar)
WDM network
SS
RS
{ A, B, C }
{ B, C, D }
Path computation should compute a path meeting optical requirements of B or C
If the optimal path is compliant with optical requirements in B:
  The domain controller setup the path
  The domain controller configures TX and RX device controllers with application code B
    TX device controller internally configures if-mode 1 (foo)
    RX device controller internally configures if-mode 2 (bar)
the mapping between the application code, selected by path computation, and the if-mode is done internally by the transponder device
Two transceivers supporting the same application code/organizational mode and a line system matching the constraints, defined in ITU-T G.698.2 or by the organization, for that application code/organizational will interoperate.
if-mode 1
{ B, C }
if-mode 2
{ A }
if-mode 1
{ D }
if-mode 2
{ B }
if-mode 3
{ C }
Application code/organizational mode case (topology model)

## Slide 5
TX
(foo)
RX
(bar)
WDM network
SS
RS
{ A, B, C }
{ B, C, D }
Path computation should compute a path meeting optical requirements of B or C
If the optimal path is compliant with optical requirements in B:
  The domain controller setup the path
  The domain controller configures TX device controller with if-mode 1 (foo)
  The domain controller configures RX device controller with if-mode 2 (bar)
the domain controller configured the if-mode which supports the application code selected based on path computation results,
The if-mode is an identifier for an explicit set of parameters.
The if-modes specify the interface configurations only and do not define interoperability requirements
if-mode 1
{ B, C }
if-mode 2
{ A }
if-mode 1
{ D }
if-mode 2
{ B }
if-mode 3
{ C }
If-mode case from draft-ietf-ccamp-dwdm-if-param-yang

## Slide 6: Capability parameters
Optical impairment limits for each operational mode (min OSNR, max PMD, max CD, max PDL, Q-factor limit, etc.)  layer0-types-ext grouping common-transceiver-capabilities-organizational-mode
Alternatively: explicit parameter list and supported parameter values/ranges
Common set of parameters for both options:
  supported transmitter tuning range [f_tx_min, f_tx_max]
  supported transmitter tunability grid (in GHz)
  supported transmitter power range [p_tx-min, p_tx_max]
  supported receiver power range [p_rx-min, p_rx_max]
  Supported max rx optical power
   layer0-types-ext grouping common-transceiver-capabilities-organizational-explicit

## Slide 7
augment /nw:networks/nw:network/nw:node/tet:te/tet:tunnel-termination-point:
+--ro OTSiG-element* [OTSiG-identifier]
| +--ro OTSiG-identifier int16
| +--ro OTSiG-container
| +--ro OTSi* [OTSi-carrier-id]
| +--ro OTSi-carrier-id int16
| <common grouping for configured mode>  grouping common-transceiver-configured-param
| <reference to a transceiver>
+--ro transponders-list* [transponder-id]
+--ro transponder-id uint32
+--ro transceivers-list* [tranceiver-id]
+--ro transceiver* [transceiver-id]
+--ro transceiver-id uint32
+--ro supported-mode [mode-id]
| <common attributes ranges/limit for supported modes>  grouping common-transceiver-capabilities-organizational-mode
<common attributes for other transceiver’s capabilities (if any)>  grouping common-transceiver-capabilities-organizational-explicit
+--ro if-supported-mode
| +--ro supported-mode [mode-id]
| | <common attributes ranges/limit for supported modes>
| | <additional attributes for supported modes (if any)>
| <common attributes for other transceiver’s capabilities (if any)>  grouping common-transceiver-capabilities-organizational-explicit
| <additional attributes for other transceiver’s capabilities (if any)>
+--rw current-opt-if-och-mode-params
| <common grouping for configured mode>
| <additional attributes>
Reference YANG with underlined commonalities
(in red) (in blue name of YANG groupings)

## Slide 8: Topology model basic update
+--ro transponder-list* [transponder-id]
+--ro transponder-id uint32
+--ro transceiver-list* [transceiver-id]
+--ro transceiver-id uint32
+--ro supported-modes* [mode-id]
+--ro mode-id string
+--ro (mode)
+--:(G.692.2)
| +--ro standard-mode? standard-mode
+--:(organizational-mode)
| +--ro operational-mode? operational-mode
| +--ro organization-identifier?
| organization-identifier
+--:(explicit-mode)
+--ro supported-std-modes
+--ro supported-application-codes*
| -> ../../mode-id
+--ro supported-organizational-modes*
-> ../../mode-id

## Slide 9: Open Issues https://github.com/ietf-ccamp-wg/draft-ietf-ccamp-optical-impairment-topology-yang/issues
Alignment with ITU-T terminology and definitions for the data plane
  Sub-sections in section 2.3 will have to be updated
  Open issue on GitHub: #25
Open issues #5 and #12 to be closed since related to #29 Transponder model , almost completed
Other issues: see GitHub link above
Repositories : https://github.com/ietf-ccamp-wg

## Slide 10: Next Steps
Completion of review of layer0-types-ext for transponders
  Joint effort with authors of draft-ietf-ccamp-dwdm-if-param-yang
Completion of configuration part of optical transponder model revision.
Modeling of 3R regenerators based on optical transponder model
Address the other open issues on GitHub

## Slide 11: Thank You!