## Slide 1: DetNet Data Plane Drafts TSN-related
Balázs Varga, János Farkas, Andrew Malis, Stewart Bryant, Don Fedyk
DetNet WG
Interim, 11st June, 2020

## Slide 2: Data plane documents Status
Building block approach
DetNet Data plane drafts
draft-ietf-detnet-data-plane-framework
draft-ietf-detnet-ip
draft-ietf-detnet-mpls
draft-ietf-detnet-ip-over-mpls
draft-ietf-detnet-mpls-over-udp-ip
draft-ietf-detnet-ip-over-tsn
draft-ietf-detnet-mpls-over-tsn
draft-ietf-detnet-tsn-vpn-over-mpls
TSN VPN over DetNet
DetNet over sub-net
DetNet IP|MPLS
Data plane framework

## Slide 3: DetNet Data Plane: TSN related cases
DetNet Data Plane: IP over IEEE 802.1 Time Sensitive Networking (TSN) draft-ietf-detnet-ip-over-tsn
DetNet Data Plane: MPLS over IEEE 802.1 Time Sensitive Networking (TSN) draft-ietf-detnet-mpls-over-tsn
DetNet Data Plane: IEEE 802.1 Time Sensitive Networking over MPLS draft-ietf-detnet-tsn-vpn-over-mpls

## Slide 4: DetNet Data Plane: IP over 802.1 TSN draft-ietf-detnet-ip-over-tsn
Content
  specifies the Deterministic Networking IP data plane when operating over a TSN sub-network.
DetNet IP Data Plane
  DetNet IP DP only provides the DetNet forwarding sub-layer
  Service protection is provided by TSN sub-network
Management and Control Information Summary
Security
  Sub-network scenario specific

## Slide 5: DetNet Data Plane: IP over 802.1 TSN Management and Control Information Summary
TSN-aware IP DetNet nodes are member of both the DetNet domain and the TSN sub-network.
  Within the TSN sub-network the TSN-aware IP (DetNet) node has a TSN-aware Talker/Listener role.
  DetNet flow ID and flow related parameters/requirements must be converted to a TSN Stream ID and stream related parameters/requirements.
The following summarizes the set of information that is needed to configure DetNet IP over TSN:
  DetNet IP related configuration information according to the DetNet role of the DetNet IP node, as per [I-D.ietf-detnet-ip].
  TSN related configuration information according to the TSN role of the DetNet IP node, as per [IEEE8021Q], [IEEE8021CB] and [IEEEP8021CBdb].
  Mapping between DetNet IP flow(s) (as flow identification defined in [I-D.ietf-detnet-ip], it is summarized in Section 5.1 of that document, and includes all wildcards, port ranges and the ability to ignore specific IP fields) and TSN Stream(s) (as stream identification information defined in [IEEE8021CB] and [IEEEP8021CBdb]). Note, that managed objects for TSN Stream identification can be found in [IEEEP8021CBcv].

## Slide 6: DetNet Data Plane: MPLS over 802.1 TSN draft-ietf-detnet-mpls-over-tsn
Content
  specifies the Deterministic Networking MPLS data plane when operating over a TSN sub-network.
DetNet MPLS Data Plane
  DetNet MPLS DP provides both DN service and forwarding sub-layers
  Service protection interworking between MPLS and TSN are left for further study.
Management and Control Information Summary
Security
  Sub-network scenario specific

## Slide 7: DetNet Data Plane: MPLS over 802.1 TSN Management and Control Information Summary
TSN-aware MPLS DetNet nodes are member of both the DetNet domain and the TSN sub-network.
  Within the TSN sub-network the TSN-aware MPLS (DetNet) node has a TSN-aware Talker/Listener role.
  DetNet flow ID and flow related parameters/requirements must be converted to a TSN Stream ID and stream related parameters/requirements.
Service protection interworking between MPLS and TSN are left for further study.
The following summarizes the set of information that is needed to configure DetNet MPLS over TSN:
  DetNet MPLS related configuration information according to the DetNet role of the DetNet MPLS node, as per [I-D.ietf-detnet-mpls].
  TSN related configuration information according to the TSN role of the DetNet MPLS node, as per [IEEE8021Q], [IEEE8021CB] and [IEEEP8021CBdb].
  Mapping between DetNet MPLS flow(s) (label information: A-labels, S-labels and F-labels as defined in [I-D.ietf-detnet-mpls]) and TSN Stream(s) (as stream identification information defined in [IEEEP8021CBdb]). Note, that managed objects for TSN Stream identification can be found in [IEEEP8021CBcv].

## Slide 8: DetNet Data Plane: 802.1 TSN over MPLS draft-ietf-detnet-tsn-vpn-over-mpls
Content
  specifies the Deterministic Networking data plane when TSN networks are interconnected over a DetNet MPLS Network.
Concept
  TSN Stream(s) treated as DetNet App-flow.
  DetNet domain behaves as a TSN relay node for the TSN streams
  Service proxy behaves as a port of that TSN relay node.
TSN over MPLS Data Plane Procedures:
  TSN related
  DetNet Service Proxy
  DetNet service and forwarding sub-layer
  Service protection interworking scenarios are left for further study
Management and Control Information Summary
Security

## Slide 9: DetNet Data Plane: 802.1 TSN over MPLS Management and Control Information Summary
DetNet flow and TSN Stream mapping related information are required:
  for the service proxy function of MPLS (DetNet) Edge nodes
  MPLS DetNet Edge nodes are member of both the DetNet domain and the connected TSN network.
  From the TSN network perspective the MPLS (DetNet) Edge node has a "TSN relay node" role, so TSN specific management and control plane functionalities must be implemented.
Service protection interworking scenarios are left for further study.
The following summarizes the set of information that is needed to configure TSN over DetNet MPLS:
  TSN related configuration information according to the TSN role of the DetNet MPLS node, as per [IEEE8021Q], [IEEE8021CB] and [IEEEP8021CBdb].
  DetNet MPLS related configuration information according to the DetNet role of the DetNet MPLS node, as per [I-D.ietf-detnet-mpls].
  App-Flow identification information to map received TSN Stream(s) to the DetNet flow. Parameters fo TSN stream identification are defined in [IEEE8021CB] and [IEEEP8021CBdb].

## Slide 10: Summary – Next Steps
Editorial updates: DONE
  Abbreviations, References, etc.
Adding conformance language: DONE
Security section update: DONE
Shepherd reviews comments: DONE

## Slide 11
Thanks …