## Slide 1: DetNet Configuration YANG Model
Xuesong Geng (gengxuesong@huawei.com)
Mach Chen (mach.chen@huawei.com)
Yeoncheol Ryoo (dbduscjf@etri.re.kr)
Zhenqiang Li (lizhengqiang@chinamobile.com)
Reshad Rahman(rrahman@cisco.com)
Don Fedyk(dfedyk@labn.net )
draft-ietf-detnet-yang-06

## Slide 2: History
Version 00: accepted as a WG document after IETF 102
Version 01: ietf-detnet-topology-yang is defined independently
Version 02: updated following the feedback from IETF103
  Add ‘Sequence Number Generation’
    OAM considerations
  Add ‘DetNet Service Decapsulation’
  Add ‘DetNet Transport Tunnel Decapsulation’
Version 03: DetNet Configuration Structure Update in IETF104 and IETF105
Version 04 :
  Modify the scope of DetNet YANG Model
Version 05/06:
  Two YANG Models Discussion -> Comparison
WG Call Meeting Every Week
Notes: Version00 接受WG draft时间

## Slide 3: Scenarios Covered by DetNet YANG Model (w/o Aggregation)
MPLS
IP
ip
IP
MPLS
Ethernet
Application
Service Sub-layer
Forwarding Sub-layer
IP
MPLS
Ethernet
MPLS
IP
IP
Data
Ethernet
IP
Ethernet
MPLS
Data
Not shown Ethernet or other Tunnels as be underlay
ip-over-mpls
mpls
tsn-vpn-over-mpls
IP
mpls-over-udp-ip (future)
MPLS
TSN (Future)
Corresponding Data Plane drafts:
draft-ietf-detnet-ip-06
draft-ietf-detnet-ip-over-mpls-06
draft-ietf-detnet-mpls-07
draft-ietf-detnet-mpls-over-udp-ip-06 (Partial)
draft-ietf-detnet-tsn-vpn-over-mpls-03 (Partial)
draft-ietf-detnet-mpls-over-tsn-03(Not yet)
draft-ietf-detnet-ip-over-tsn-03(Not yet)

## Slide 4: DetNet YANG Model Meetings Learnings
After reviewing the models:
  Architecture of the DetNet YANG Model
    There are a few ways to envision the model
    The structural model has benefits
  Building Blocks of the DetNet YANG model
    We spent time reviewing basic building blocks related to the model
    most of the building blocks have been aligned
  Duplication Avoidance
    A question of how much duplication of information various layers
    Reuse of common blocks – Implementation may opt to have a leaner model.
  Aggregation:
    Consider a Main line case of an IP Application, an MPLS DetNet service sub-layer, an MPLS Forwarding Sub-layer.
    Once this is agreed we can add aggregation

## Slide 5: Comparison Between Two Existing YANG Models
Similarities
  Layer based: including application, service sub-layer, forwarding sub-layer;
  Data Plane followed: covering the existing data plane solutions
    IP, IP over MPLS, IP over TSN, MPLS, MPLS over UPD/IP, MPLS over TSN , TSN over MPLS
  Aggregation allowed: supporting flow aggregation in different layers
    Different application-> same service sub-layer; different service sub-layer-> same forwarding sub-layer
Differences
  Direction aware or direction unaware?
  Different groups of parameters combined flexibly based on the requirement or same structure for all the cases by configuring the corresponding group;

## Slide 6: YANG Model 1: App-flow
+--rw app-flows
| +--rw app-flow* [name]
| +--rw name string
| +--ro app-id? uint16
| +--rw app-flow-bidir-congruent? boolean
| +--rw traffic-requirements
| +--rw traffic-specification
| +--rw in-segment
| | +--rw interface? if:interface-ref
| | +--rw (data-flow-type)?
| | +--:(tsn-app-flow)
| | +--:(ip-app-flow)
| | +--:(mpls-app-flow)
| +--rw out-segment
| +--rw (outgoing-options)
| +--:(ingress-proxy)
| | +--rw service-sub-layer* service-sub-layer-ref
| +--:(egress)
| +--rw (next-hop-options)
| +--:(simple-next-hop)
| | +--rw mpls-header
| | | +--rw mpls-label-stack
| | | +--rw entry* [id]
| | | +--rw id uint8
| | | +--rw label? rt-types:mpls-label
| | | +--rw ttl? uint8
| | | +--rw traffic-class? uint8
| | +--rw outgoing-interface? if:interface-ref
| +--:(next-hop-list)
| +--rw next-hop-list
| +--rw next-hop* [hop-index]
| +--rw hop-index uint8
| +--rw mpls-header
| | +--rw mpls-label-stack
| | +--rw entry* [id]
| | +--rw id uint8
| | +--rw label? rt-types:mpls-label
| | +--rw ttl? uint8
| | +--rw traffic-class? uint8
| +--rw outgoing-interface? if:interface-ref
Leafref - Service reference
Leafref - Interface reference
Application identification value
Using at
ingress node
Using at
egress node

## Slide 7: YANG Model 1: Service Sub-layer
+--rw service-sub-layer
| +--rw service-sub-layer-list* [name]
| +--rw name string
| +--ro service-id? uint16
| +--rw service-rank? uint8
| +--rw traffic-requirements
| +--rw traffic-specification
| +--rw service-protection
| | +--rw service-protection-type? service-protection-type
| | +--rw sequence-number-length? sequence-number-field
| +--rw service-operation-type? service-operation-type
| +--rw in-segment
| | +--rw (incoming-options)
| | +--:(ingress-proxy)
| | | +--rw app-flow* app-flow-ref
| | +--:(detnet-service-identification)
| | +--rw (detnet-flow-type)?
| | +--:(ip-detnet-flow)
| | +--:(mpls-detnet-flow)
| +--rw out-segment
| +--rw (outgoing-options)
| +--:(egress-proxy)
| | +--rw app-flow* app-flow-ref
| +--:(detnet-service-output)
| +--rw service-output-list* [service-output-index]
| +--rw service-output-index uint8
| +--rw (header-type)?
| | +--:(detnet-mpls-header)
| | | +--rw mpls-label-stack
| | | +--rw entry* [id]
| | | +--rw id uint8
| | | +--rw label? rt-types:mpls-label
| | | +--rw ttl? uint8
| | | +--rw traffic-class? uint8
| | +--:(detnet-ip-header)
| | +--rw src-ip-address? inet:ip-address
| | +--rw dest-ip-address? inet:ip-address
| | +--rw next-header? uint8
| | +--rw traffic-class? uint8
| | +--rw flow-label? inet:ipv6-flow-label
| | +--rw source-port? inet:port-number
| | +--rw destination-port? inet:port-number
| +--rw next-layer* [index]
| +--rw index uint8
| +--rw forwarding-sub-layer? forwarding-sub-layer-ref
Leafref - Application reference
Service identification value
Leafref - Application reference
Leafref - forwarding reference
Using at ingress node
Using at
Egress node
Using at relay node

## Slide 8: YANG Model 1: Forwarding Sub-layer
+--rw forwarding-sub-layer
| +--rw forwarding-sub-layer-list* [name]
| +--rw name string
| +--ro forwarding-id? uint16
| +--rw traffic-requirements
| +--rw traffic-specification
| +--rw forwarding-operation-type? forwarding-operations-type
| +--rw in-segment
| | +--rw (incoming-options)
| | +--:(detnet-service-forwarding)
| | | +--rw service-sub-layer* service-sub-layer-ref
| | +--:(detnet-forwarding-identification)
| | +--rw interface? if:interface-ref
| | +--rw (detnet-flow-type)?
| | +--:(ip-detnet-flow)
| | +--:(mpls-detnet-flow)
| +--rw out-segment
| +--rw (outgoing-options)
| +--:(service-operation)
| | +--rw service-sub-layer* service-sub-layer-ref
| +--:(detnet-forwarding-output)
| +--rw (next-hop-options)
| +--:(simple-next-hop)
| | +--rw (header-type)?
| | | +--:(detnet-mpls-header)
| | | +--:(detnet-ip-header)
| | +--rw outgoing-interface? if:interface-ref
| +--:(next-hop-list)
| +--rw next-hop-list
| +--rw next-hop* [hop-index]
| +--rw hop-index uint8
| +--rw (header-type)?
| | +--:(detnet-mpls-header)
| | +--:(detnet-ip-header)
| +--rw outgoing-interface? if:interface-ref
Leafref - Service reference
Leafref - Service reference
Leafref - Interface reference
Forwarding identification value
Using at transit node
Using at
relay/egress node
for forwarding input
Using at
relay/Ingress node
for forwarding output

## Slide 9: YANG Model 1: Example
Source
1.1.1.1
Ingress
2.2.2.2
Relay 1
3.3.3.3
Relay 2
6.6.6.6
Egress
7.7.7.7
Transit 2
5.5.5.5
Transit 1
4.4.4.4
Destination
8.8.8.8
End-to-End Service
DetNet MPLS Service
DATA
MPLS
S-label 66666
MPLS
F-label 43
DATA
IP 1.1.1.1/32
8.8.8.8/32
MPLS
S-label 66666
MPLS
F-label 44
DATA
IP 1.1.1.1/32
8.8.8.8/32
MPLS
S-label 66666
MPLS
F-label 45
DATA
IP 1.1.1.1/32
8.8.8.8/32
MPLS
S-label 66666
MPLS
F-label 46
DATA
IP 1.1.1.1/32
8.8.8.8/32
DATA
IP 1.1.1.1/32
8.8.8.8/32
IP 1.1.1.1/32
8.8.8.8/32
MPLS
S-label 55555
MPLS
F-label 42
DATA
IP 1.1.1.1/32
8.8.8.8/32
MPLS
S-label 77777
MPLS
F-label 47
DATA
IP 1.1.1.1/32
8.8.8.8/32

## Slide 10: YANG Model 1: Example(ingress edge node)
"app-flows": {
"app-flow": [
{
"name": "app1",
"app-id": "1",
"app-flow-bidir-congruent": "false",
"in-segment": {
"interface": "eht0",
"source": "1.1.1.1/32",
"destination": ”8.8.8.8/32",
"next-header": "6",
"traffic-class": "40"
},
"out-segment": {
"service-sub-layer": "ssl1"
}
}
]
},
"service-sub-layer": {
"service-sub-layer-list": [
{
"name": "ssl1",
"service-id": "1",
"service-rank": "10",
"traffic-requirements": {
"min-bandwidth": "100000000",
"max-latency": "100000000",
"max-latency-variation": "2000000",
"max-loss": "2",
"max-consecutive-loss-tolerance": "5",
"max-misordering": "0"
},
"service-protection": {
"service-protection-type": "none",
"sequence-number-length": "long-sn"
},
"service-operation-type": "service-initiation",
"in-segment": {
"app-flow": [
"app1”
]
},
"out-segment": {
"detnet-service-output-list": [
{
"service-output-index": "1",
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": "55555"
}
]
},
"next-layer": [
{
"index": "1",
"forwarding-sub-layer": ”fsl1"
}
]
}
]
}
}
]
},
"forwarding-sub-layer": {
"forwarding-sub-layer-list": [
{
"name": "fsl1",
"forwarding-id": "1",
"traffic-specification": {
"interval": "5",
"max-packets-per-interval": "10",
"max-payload-size": "1500"
},
"forwarding-operation-type": "impose-and-forward",
"in-segment": {
"service-sub-layer": [
"ssl1”
]
},
"out-segment": {
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": "42",
"traffic-class": "5"
}
]
},
"outgoing-interface": "eth1"
}
}
]
},
Ingress Node |  | 
Name = app1 | Name = ssl1 T-req OperType = Initiation Seq len = 28 bit Protection = None | Name = fsl1 T-spec OperType = Impose-and-Forward
In-segment IP = 1.1.1.1/32 2.2.2.2/32 | In-segment ref = app 1 | In-segment ref = ssl1
Out-segment ref = ssl 1 | Out-segment S-label = 55555 ref = fsl 1 | Out-segment F-label = 42 ref = eth 1

## Slide 11: YANG Model 1: Example(relay node - replication)
"service-sub-layer": {
"service-sub-layer-list": [
{
"name": "ssl1",
"service-id": "1",
"service-rank": "10",
"traffic-requirements": {
"min-bandwidth": "100000000",
"max-latency": "100000000",
"max-latency-variation": "2000000",
"max-loss": "2",
"max-consecutive-loss-tolerance": "5",
"max-misordering": "0"
},
"service-protection": {
"service-protection-type": ”replication",
"sequence-number-length": "long-sn"
},
"service-operation-type": "service-relay",
"in-segment": {
”label": ”55555”
},
"out-segment": {
"detnet-service-output-list": [
{
"service-output-index": "1",
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": ”66666"
}
]
},
"next-layer": [
{
"index": "1",
"forwarding-sub-layer": ”fsl2"
},
{
"index": ”2",
"forwarding-sub-layer": ”fsl3"
}
]
}
]
}
}
]
},
"forwarding-sub-layer": {
"forwarding-sub-layer-list": [
{
"name": "fsl1",
"forwarding-id": "1",
"forwarding-operation-type": ”pop-and-lookup",
"in-segment": {
"interface": "eth0”,
”label": ”42”
},
"out-segment": {
”service-sub-layer": [
“ssl1”
]
}
},
{
"name": "fsl2",
"forwarding-id": ”2",
"traffic-specification": {
"interval": "5",
"max-packets-per-interval": "10",
"max-payload-size": "1500"
},
"forwarding-operation-type": "impose-and-forward",
"in-segment": {
"service-sub-layer": [
"ssl1”
]
},
"out-segment": {
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": "43",
"traffic-class": "5"
}
]
},
"outgoing-interface": "eth1"
}
},
{
"name": "fsl3",
"forwarding-id": ”3",
"traffic-specification": {
"interval": "5",
"max-packets-per-interval": "10",
"max-payload-size": "1500"
},
"forwarding-operation-type": "impose-and-forward",
"in-segment": {
"service-sub-layer": [
"ssl1”
]
},
"out-segment": {
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": "44",
"traffic-class": "5"
}
]
},
"outgoing-interface": "eth2"
}
}
]
},
Relay node 1 |  |  | 
Name = fsl1 OperType = pop-and-lookup | Name = ssl1 T-Req OperType = Relay Seq len = 28 bit Protection = PRF | Name = fsl2 T-spec OperType = Impose-and-Forward | Name = fsl3 T-spec OperType = Impose-and-Forward
In-segment F-label = 42 | In-segment S-label = 55555 | In-segment ref = ssl1 | In-segment ref = ssl1
Out-segment ref = ssl 1 | Out-segment S-label = 66666 ref = fsl2 fsl3 | Out-segment F-label = 43 ref = eth1 | Out-segment F-label = 44 ref = eth2

## Slide 12: YANG Model 1: Example(transit node)
"forwarding-sub-layer": {
"forwarding-sub-layer-list": [
{
"name": "fsl2",
"forwarding-id": "1",
"traffic-specification": {
"interval": "5",
"max-packets-per-interval": "10",
"max-payload-size": "1500"
},
"forwarding-operation-type": "swap-and-forward",
"in-segment": {
"interface": "eth0”,
”label": ”43”
},
"out-segment": {
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": "45",
"traffic-class": "5"
}
]
},
"outgoing-interface": "eth1"
}
}
]
},
"forwarding-sub-layer": {
"forwarding-sub-layer-list": [
{
"name": "fsl3",
"forwarding-id": "1",
"traffic-specification": {
"interval": "5",
"max-packets-per-interval": "10",
"max-payload-size": "1500"
},
"forwarding-operation-type": "swap-and-forward",
"in-segment": {
"interface": "eth0”,
”label": ”44”
},
"out-segment": {
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": "46",
"traffic-class": "5"
}
]
},
"outgoing-interface": "eth1"
}
}
]
},
Transit Node 1
Name = fsl2 T-spec OperType = swap-and-Forward
In-segment F-label = 43
Out-segment F-label = 45 ref = eth1
Transit Node 2
Name = fsl3 T-spec OperType = swap-and-Forward
In-segment F-label = 44
Out-segment F-label = 46 ref = eth1

## Slide 13: YANG Model 1: Example(relay node - elimination)
"service-sub-layer": {
"service-sub-layer-list": [
{
"name": "ssl1",
"service-id": "1",
"service-rank": "10",
"traffic-requirements": {
"min-bandwidth": "100000000",
"max-latency": "100000000",
"max-latency-variation": "2000000",
"max-loss": "2",
"max-consecutive-loss-tolerance": "5",
"max-misordering": "0"
},
"service-protection": {
"service-protection-type": ”elimination",
"sequence-number-length": "long-sn"
},
"service-operation-type": "service-relay",
"in-segment": {
”label": ”666666”
},
"out-segment": {
"detnet-service-output-list": [
{
"service-output-index": "1",
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": ”77777"
}
]
},
"next-layer": [
{
"index": "1",
"forwarding-sub-layer": ”fsl4"
}
]
}
]
}
}
]
},
"forwarding-sub-layer": {
"forwarding-sub-layer-list": [
{
"name": "fsl2",
"forwarding-id": "1",
"forwarding-operation-type": ”pop-and-lookup",
"in-segment": {
"interface": "eth0”,
”label": ”45”
},
"out-segment": {
”service-sub-layer": [
“ssl1”
]
}
},
{
"name": "fsl3",
"forwarding-id": ”2",
"forwarding-operation-type": ”pop-and-lookup",
"in-segment": {
"interface": "eth1”,
”label": ”46”
},
"out-segment": {
”service-sub-layer": [
“ssl1”
]
}
},
{
"name": "fsl4",
"forwarding-id": ”3",
"traffic-specification": {
"interval": "5",
"max-packets-per-interval": "10",
"max-payload-size": "1500"
},
"forwarding-operation-type": "impose-and-forward",
"in-segment": {
"service-sub-layer": [
"ssl1”
]
},
"out-segment": {
"mpls-label-stack": {
"entry": [
{
"id": "1",
"label": "47",
"traffic-class": "5"
}
]
},
"outgoing-interface": "eth2"
}
},
Relay node 2 |  |  | 
Name = fsl2 OperType = pop-and-lookup | Name = fsl3 OperType = pop-and-lookup | Name = ssl1 T-Req OperType = Relay Seq len = 28 bit Protection = PEF | Name = fsl4 T-spec OperType = Impose-and-Forward
In-segment F-label = 45 | In-segment F-label = 46 | In-segment S-label = 66666 | In-segment ref = ssl1
Out-segment ref = ssl1 | Out-segment ref = ssl1 | Out-segment S-label = 77777 ref = fsl4 | Out-segment F-label = 47 ref = eth2

## Slide 14: YANG Model 1: Example(egress edge node)
"app-flows": {
"app-flow": [
{
"name": "app1",
"app-id": "1",
"app-flow-bidir-congruent": "false",
"in-segment": {
"interface": "eht0",
"source": "1.1.1.1/32",
"destination": ”8.8.8.8/32",
"next-header": "6",
"traffic-class": "40"
},
"out-segment": {
”outgoing-interface": ”eth1"
}
}
]
},
"service-sub-layer": {
"service-sub-layer-list": [
{
"name": "ssl1",
"service-id": "1",
"service-rank": "10",
"traffic-requirements": {
"min-bandwidth": "100000000",
"max-latency": "100000000",
"max-latency-variation": "2000000",
"max-loss": "2",
"max-consecutive-loss-tolerance": "5",
"max-misordering": "0"
},
"service-protection": {
"service-protection-type": "none",
"sequence-number-length": "long-sn"
},
"service-operation-type": "service-termination",
"in-segment": {
”label": ”77777"
},
"out-segment": {
"app-flow": [
"app1”
]
}
}
]
},
"forwarding-sub-layer": {
"forwarding-sub-layer-list": [
{
"name": "fs4",
"forwarding-id": "1",
"traffic-specification": {
"interval": "5",
"max-packets-per-interval": "10",
"max-payload-size": "1500"
},
"forwarding-operation-type": ”pop-and-lookup",
"in-segment": {
"interface": "eth0”,
”label": ”47”
},
"out-segment": {
”service-sub-layer": [
“ssl1”
]
}
}
]
},
Egress Node |  | 
Name = fsl4 T-spec OperType = pop-and-lookup | Name = ssl1 T-req OperType = Termination Seq len = 28 bit Protection = None | Name = app1
In-segment F-label = 47 | In-segment S-label = 77777 | In-segment IP = 1.1.1.1/32 2.2.2.2/32
Out-segment ref = ssl 1 | Out-segment ref = app1 | Out-segment ref = eth1

## Slide 15: YANG Model 2: Motivation
To align the DetNet YANG model with the Flow Information Model and the IP and MPLS data plane drafts.
Started with the existing DetNet Yang model trying to align with the Information flow model
Reorganized with Application, Service, and Forwarding Layer
After a couple of iterations it was clear there was a lot of similarity between:
  Applications and Service
  Applications ingress/egress and Forwarding Sublayer input/output.
  Common Building Blocks
Reorganized the YANG model to:
  Leverage the symmetry
  Reuse existing IP and MPLS YANG from other IETF drafts and RFCs.
  Align with existing QoS / Traffic specifications

## Slide 16: Structure of the Attributes App-flow, DetNet flow and DetNet service
DN Service
DnServiceID: unique (manag.) ID
DnServiceDeliveryType: Eth, MPLS, IP
DnServiceConnectivity: p2p, p2mp
DnServiceRank
DnServiceDeliveryProfile: MaxBW, MaxLatency, MaxLatencyVariation, MaxLoss, MaxConsecutiveLossTolerance, MaxMisordering
DnServiceBiDir
DnServiceStatus
Service Requirements similar to e.g., 802.1Qcc Attributes like UserToNetworkRequirements
draft-ietf-detnet-flow-information-model
App-flow
Characteristics
FlowID: unique (manag.) ID
FlowType: Eth, MPLS, IP
DataFlowSpecification: src/dst-addr, label, VLAN, etc.
TrafficSpecification: interval, pckt-size, max-packet
FlowEndPoints: Src, Dst(s)
FlowRank
FlowStatus
Requirements
FlowRequirements: MinBW, PD, PDV, Loss, etc.
FlowBiDir
DetNet flow
Characteristics
DnFlowID: unique (manag.) ID
DnPayloadType: Eth, MPLS, IP
DnFlowFormat: MPLS, IP
DnFlowSpecification: Label, 6-tuple
DnTrafficSpecification interval, pckt-size, max-packet
DnFlowEndPoints: Ingress, Egress(s)
DnFlowRank
DnFlowStatus
Requirements
DnFlowRequirements: MinBW, MaxLatency, MaxLatencyVariation, MaxLoss, MaxConsecutiveLossTolerance, MaxMisordering
DnFlowBiDir
A DetNet flow contains one or more App-flows (N:1 mapping).
A DetNet service supports one or more DetNet-flows (M:1 mapping).

## Slide 17: Edge Node
Interface
Application
Service
Outbound
Service
Inbound
Application
Application
fwd-sub-layer-output
fwd-sub-layer-input
Interface
fwd-sub-layer-output
fwd-sub-layer-input
fwd-sub-layer-output
fwd-sub-layer-input
n : 1
Applications : Service
m : 1
DetNet Flows : Service
x : 1
Forwarding-Sub-layers Input/Output : Service
y : 1
Interfaces: Forwarding-Sub-layers Input/Output
k : 1
Interfaces: Application Ingress/Egress

## Slide 18: YANG Model 2: Applications Summary
module: ietf-detnet-configa
+--rw detnet
+--rw applications
+--rw app-list* [name]
+--rw name string
+--ro app-id? uint16
+--rw app-flow-bidir-congruent? boolean
+--ro service-outbound? service-ref
+--ro service-inbound? service-ref
+--rw traffic-requirements
+--rw traffic-specification
+--rw app-ingress* [name]
| +--rw name string
| +--ro app-flow-status? identityref
| +--rw incoming-interface* ietf-interfaces:interface-ref
| +--rw (detnet-forwarding-type)?
| +--:(ethernet)
| +--:(ip)
| | +--rw ip
| | +--rw (l4)?
| | +--:(tcp)
| | +--:(udp)
| | +--:(ipsec)
| | +--rw ipsec
| | +--rw ipsec-spi? ipsec-spi
| +--:(mpls)
+--rw app-egress* [name]
+--rw name string
+--ro app-flow-status? identityref
+--rw next-hop
+--rw (application-type)?
+--:(ethernet)
| +--rw ethernet
| +--rw ethernet-place-holder? string
+--:(ip-mpls)
+--rw ip-mpls
+--rw (next-hop-options)
+--:(simple-next-hop)
+--:(special-next-hop)
+--:(next-hop)
+--rw outgoing-interface? ietf-interfaces:interface-ref
General structure
(read draft for full tree)
Leafref References
  Service (configured at service sub-layer
  Interfaces
Aplication
Leafref - Service references
Leafref - Interface reference
Application identification value

## Slide 19: YANG Model 2: Service Sub-layer
module: ietf-detnet-configa
+--rw detnet
+--rw services
+--rw service-list* [name]
+--rw name string
+--ro service-id? uint16
+--rw service-rank? uint8
+--rw outbound
| +--rw forward-sublayer-output* fwd-sub-layer-output-ref
| +--rw service-protection-type? identityref
| +--rw sequence_number_length? uint8 <0>
| +--rw application-input* [name]
| | +--rw name application-ref
| | +--rw (detnet-forwarding-type)?
| | +--:(ip)
| | | +--rw ip
| | | +--rw source ietf-inet-types:ip-prefix
| | | +--rw destination ietf-inet-types:ip-prefix
| | | +--rw protocol-next uint8
| | | +--rw dscp* uint8
| | | +--rw ipv6-flow-label? ietf-inet-types:ipv6-flow-label
| | | +--rw (l4)?
| | | +--:(tcp)
| | | +--:(udp)
| | | +--:(ipsec)
| | +--:(mpls-service-label)
| +--rw prev-relay-services* [name]
| | +--rw (detnet-forwarding-type)?
| | +--:(ip)
| | | +--rw ip
| | +--:(mpls-service-label)
| +--rw traffic-requirements
| +--rw traffic-specification
+--rw inbound
+--rw forward-sublayer-input* fwd-sub-layer-input-ref
+--rw service-protection-type? identityref
+--rw sequence_number_length? uint8 <0>
+--rw application-output* [name]
| +--rw name application-ref
| +--rw (detnet-forwarding-type)?
| +--:(ip)
| +--:(mpls-service-label)
+--rw next-relay-services* [name]
+--rw name service-ref
+--rw (detnet-forwarding-type)?
+--:(ip)
+--:(mpls-service-label)
General structure
(read draft for full tree)
Leafref References
  Application to Service Instance
  Service Instance to Forwarding
  Maybe unidirectional or bidirectional in configuration
(To Do: aggregation Label)
Leafref - Application reference
Service identification value
Leafref - Application reference

## Slide 20: YANG Model 2: Forwarding Sub-layers
module: ietf-detnet-configa
+--rw detnet
+--rw fwd-sub-layer-input* [name]
| +--rw name string
| +--rw incoming-interface* ietf-interfaces:interface-ref
| +--rw (connectors)?
| | +--:(service-sub-layers)
| | | +--ro service-sub-layers* service-ref
| | +--:(forwarding-sub-layers)
| | +--ro forwarding-sub-layers* fwd-sub-layer-output-ref
| +--rw (detnet-forwarding-type)?
| +--:(ip)
| +--:(mpls)
+--rw fwd-sub-layer-output* [name]
+--rw name string
+--rw connectors
| +--rw outbound-service* service-ref
| +--rw prev-forward-sub-layer* fwd-sub-layer-output-ref
+--rw traffic-requirements
+--rw traffic-specification
+--rw next-hop
+--rw (next-hop-options)
+--:(simple-next-hop)
+--:(special-next-hop)
+--:(next-hop)
+--rw next-hop* [hop-index]
+--rw hop-index uint8
+--rw outgoing-interface? ietf-interfaces:interface-ref
General structure
(read draft for full tree)
Leafref References
  Forwarding Sublayer to Interface
  Service (configured at service sub-layer)
(To Do:
aggregation Label
Service relay model)
Leafref – Service Reference
Leafref - Service reference
Leafref - Interface reference
Forwarding identification value

## Slide 21: Example Edge Configuration Unidirectional Ingress (Green Line)
> data -t config -f json test-detnet-edge-ingress.xml
{
"ietf-interfaces:interfaces": {
"interface": [
{
"name": "eth0",
"type": "iana-if-type:ethernetCsmacd"
},
{
"name": "eth1",
"type": "iana-if-type:ethernetCsmacd"
}
]
},
"ietf-detnet-configa:detnet": {
"applications": {
"app-list": [
{
"name": "app1",
"app-flow-bidir-congruent": false,
"app-ingress": [
{
"name": "port1",
"incoming-interface": [
"eth0"
],
"ip": {
"source": "1.1.1.1/32",
"destination": "2.2.2.2/32",
"protocol-next": 6,
"dscp": [
40
]
}
}
]
}
]
},
"fwd-sub-layer-output": [
{
"name": "fsl1",
"next-hop": {
"next-hop": [
{
"hop-index": 1,
"outgoing-interface": "eth1",
"mpls-label-stack": {
"entry": [
{
"id": 1,
"label": 42,
"traffic-class": 5
}
]
}
}
]
}
}
]
}
}
"services": {
"service-list": [
{
"name": "ssl1",
"service-rank": 10,
"outbound": {
"forward-sublayer-output": [
"fsl1"
],
"sequence_number_length": 0,
"application-input": [
{
"name": "app1",
"mpls-service-label": 55555
}
],
"traffic-requirements": {
"min-bandwidth": "100000000",
"max-latency": 10000000,
"max-latency-variation": 2000000,
"max-loss": 2,
"max-consecutive-loss-tolerance": 5,
"max-misordering": 0
},
"traffic-specification": {
"interval": 5,
"max-packets-per-interval": "10",
"max-payload-size": 1500
}
}
}
]
},
Interface
Application
Service
Outbound
Service
Inbound
Application
Application
fwd-sub-layer-output
fwd-sub-layer-input
Interface
fwd-sub-layer-output
fwd-sub-layer-input
fwd-sub-layer-output
fwd-sub-layer-input

## Slide 22: Examples Edge Configuration Unidirectional Egress (Red Line)
> data -t config -f json test-detnet-edge-egress.xml
{
"ietf-interfaces:interfaces": {
"interface": [
{
"name": "eth2",
"type": "iana-if-type:ethernetCsmacd"
},
{
"name": "eth3",
"type": "iana-if-type:ethernetCsmacd"
}
]
},
"ietf-detnet-configa:detnet": {
"applications": {
"app-list": [
{
"name": "app1",
"app-flow-bidir-congruent": false,
"app-egress": [
{
"name": "port1",
"next-hop": {
"ip-mpls": {
"next-hop": [
{
"hop-index": 1,
"outgoing-interface": "eth2"
}
]
}
}
}
]
}
]
},
"services": {
"service-list": [
{
"name": "ssl1",
"service-rank": 10,
"inbound": {
"forward-sublayer-input": [
"fsl1"
],
"sequence_number_length": 0,
"application-output": [
{
"name": "app1",
"mpls-service-label": 55555
}
]
}
}
]
},
Interface
Application
Service
Outbound
Service
Inbound
Application
Application
fwd-sub-layer-output
fwd-sub-layer-input
Interface
fwd-sub-layer-output
fwd-sub-layer-input
fwd-sub-layer-output
fwd-sub-layer-input
"fwd-sub-layer-input": [
{
"name": "fsl1",
"incoming-interface": [
"eth3"
],
"mpls": {
"interface": {
"mpls-label-stack": {
"entry": [
{
"id": 1,
"label": 42,
"traffic-class": 5
}
]
}
}
}
}
]
}
}

## Slide 23: Next Step
Make a choice or do combination
Feedback/ suggestions from WG

## Slide 24
Thanks