## Slide 1: LISP MS Federation
Victor Moreno (vimoreno@cisco.com)
IETF 107 - Virtual

## Slide 2: Agenda
Ground Base LISP refresher
Multi-operator Federation Requirements
Solutions discussed

## Slide 3: Ground Based LISP (GBL) - Reference Topology
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
A-R
handover
Multi-link / Handover
AC-R
AC-R
A/G-R
A/G-R
G/G-R
LISP MS/MR
IPv6 ICAO Net X
IPv6 ICAO Net Y
A/G-R: Air/Ground Router (LISP XTR)
G/G-R: Ground/Ground Router (LISP XTR)
ATS-E: ATS End-system
AC-R: Access Ground Router
A-R: Airborne Router
A-E: Airborne End-system
SP-West
SP-East
SP-South

## Slide 4: Ground Based LISP (GBL) – Behavior (1)
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
AC-R
A/G-R1
A/G-R2
G/G-R
LISP MS/MR
IPv6 ICAO Net X
Aircraft attaches to one or more A/G Networks
A/G Network advertises reachability of the aircraft delegated prefix (EID)
Mapping Server maintains RLOC-EID mapping
Each AGR has RLOC address
Aircraft preference and link QoS can be signalled over A/G Network
Radio Region 3
AC-R
A/G-R3
GGR needs to query which RLOC(s) serve destination EID
Traffic tunnelled over Internetwork
EID | RLOC
Y | AGR1 – Priority 1, 50% AGR2 – Priority 1, 50%
Map-cache:
Y via
AGR2(50) & AGR1(50)

## Slide 5: Ground Based LISP (GBL) – Behavior (2)
AOC - ATS Region X
Radio Region 1
Radio Region 2
Interworking Region (LISP RLOC Space)
A-R
AC-R
AC-R
A/G-R1
A/G-R2
G/G-R
LISP MS/MR
IPv6 ICAO Net X
Aircraft attaches to one or more A/G Networks
A/G Network advertises reachability of the aircraft delegated prefix (EID)
Each AGR has RLOC address
Aircraft preference and link QoS can be signalled over A/G Network
Radio Region 3
AC-R
A/G-R3
Traffic tunnelled over Internetwork
Route optimised for served ground users
Map-cache:
Y via
AGR2(50) & AGR1(50)
EID | RLOC
Y | AGR1 – Priority 1, 50% AGR2 – Priority 1, 50%
EID | RLOC
Y | AGR1 – Priority 1, 50% AGR2 – Priority 2, 50% AGR3 – Priority 1, 50%
Map-cache:
Y via
AGR3(50) & AGR1(50)

## Slide 6: ICAO Federated Network
The International Civil Aviation Organization (ICAO) Aeronautical Telecommunications Network (ATN) is run by a consortium of different providers.
  This network must support mobility and multi-homing across the different providers
The Uberlay model has been proposed as a way to architect this mixed environment. Each provider owns and operates their own xTRs, border-RTRs and Map Servers.
Each operator is autonomous in their policies.
The providers require a mechanism to peer with each other without requiring an intermediary organization to run the Uberlay for them.
  A federated Uberlay Mapping System amongst the providers is desirable.

## Slide 7: ICAO – Existing peering agreements
Radio Region
Radio Region
Mobility Provider West
Mobility Provider East
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
Mobility Provider South
Underlay Inter AS EBGP
EBGP
EBGP
EBGP
Underlay ASBR

## Slide 8: ICAO – Uberlay Structure
Radio Region
Radio Region
Mobility Protider West
Mobility Provider East
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
BR-W
BR-E
Mobility Provider South
A/G-R
G/G-R
AOC/ATC
BR-S
Underlay Inter AS EBGP
Uberlay LISP MS Federation
EBGP
EBGP
EBGP
Underlay ASBR
Uberlay
Site-Overlay
Site-Overlay
Site-Overlay

## Slide 9: ICAO – Uberlay Mapping System Federation
Radio Region
Radio Region
Mobility Protider West
Mobility Provider East
A/G-R
A/G-R
G/G-R
G/G-R
LISP MS/MR
Border Router
AOC/ATC
AOC/ATC
BR-W
BR-E
Mobility Provider South
A/G-R
G/G-R
AOC/ATC
BR-S
Mapping System Federation
Underlay Inter AS EBGP
Uberlay LISP MS Federation
EBGP
EBGP
EBGP
Underlay ASBR

## Slide 10: Generalized Mapping System Federation
RLOC space
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E1
MS-W
MS-S
MS-E
XTR-E2
Each MS/MR services a scope of xTRs
The MS will hold mappings for the xTRs in its scope
MS = MS+MR in all diagrams
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 11: Requirements for a Federated Mapping System
The Uberlay runs over a multi-provider backbone/underlay.
BGP peering agreements exist between the multiple providers in the underlay.
The Federated Mapping System in the Uberlay should support the peering agreements by different mechanisms (e.g. engineered paths, denial of service, etc.)
Each SP should be autonomous in defining and enforcing policy for EIDs connected to their network.
An aircraft (EID) may multi-home to 2 or more provider networks. So policies would likely need to be enforced at a flow level (rather than an EID level)

## Slide 12: Options to Consider
Cache Referral System / DDT
New Mobility enhancements for a Federated Mapping System
LISP De-cent
Others …

## Slide 13: Concerns
Avoid replicating the underlay BGP peering topology in the overlay
The policy applied must be consistent with the underlay peering agreements
In a federated environment, the policy is flow specific. Destination based policies may not suffice.
Mobility of EID registrations between Administrative Domains may be a hard requirement. This would mean moving the point of authority in the MS federation (ruling out a few of the existing mechanisms)

## Slide 14: Cache Referral System

## Slide 15: MS Federation: Referral Cache – Map-Register - 0
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
1. Map-Register to Ladies MS
1. Map-Register to Boys MS
Paul @ XTR-S
Mary
Paul
Mary
Paul
MS-W
MS-S
MS-E
Mary @ XTR-W
Map-Referral Cache is programmed at every Map-Resolver:
Boys: Use MS-S
Ladies: Use MS-W
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 16: MS Federation: Referral Cache – Map-Request - 1
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
1. Map-Request to local Map-Resolver
2. DB Match:
Generate Reply
Optional: Add subs to Paul
Paul @ XTR-S
XTR-W sub to Paul
Mary
Paul
Mary
Paul
MS-W
MS-S
MS-E
2. Forward Map-Request per Referral Cache
Map-Referral Cache is programmed at every Map-Resolver:
Boys: Use MS-S
Ladies: Use MS-W
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 17: MS Federation: Referral Cache – Map-Reply - 2
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
3. Map Reply with specific EID (Paul)
Mary
Paul
Mary
Paul
Paul @ XTR-S
MS-W sub to Paul
Paul @ XTR-S
MS-W
MS-S
MS-E
Map-Referral Cache is programmed at every Map-Resolver:
Boys: Use MS-S
Ladies: Use MS-W
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 18: MS Federation: Referral Cache – Registrations/EID Moves - 3
LISP MS/MR
Border Router
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
7. Map-Notify
(Paul @ XTR-E)
5. Relay Map-Register per Referral Cache
Mary
Paul
Mary
Paul
Paul @ XTR-S
XTR-W sub to Paul
Paul @ XTR-S
Paul
4. Map-Register (Paul @ XTR-E)
Paul @ XTR-E
6. Receive Map-Register, update Mappings
Paul @ XTR-E
Paul @ XTR-E
8. Receive Map-Notify, update Map-cache
MS-W
MS-S
MS-E
Map-Referral Cache is programmed at every Map-Resolver:
Boys: Use MS-S
Ladies: Use MS-W
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 19: Notes for Discussion
Pros:
  Very simple model, aligned with DDT logic (single tier).
Cons:
  May not satisfy all requirements. SP wants control over EIDs registered in their network so that policies can be enforced.

## Slide 20: Uberlay extensions proposal

## Slide 21: MS Federation – Map-Request - 1
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
1. Map-Request
2. DB Miss, cache Map-Request
3. Send ECM Map Request to All Federation Peers
4. DB Match:
Generate Reply
Optional: Add subs to Paul
4. No DB Match:
Calculate Covering Prefix Generate NMR
Paul @ XTR-S
MS-W sub to Paul
Mary
Paul
Mary
Paul
MS-W
MS-S
MS-E
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 22: MS Federation – Map-Reply - 2
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
7. Map-Reply
6. Install/register Mapping for More specific EID (Paul
6.a. Instantiate subscription to Paul for XTR-W
5. Map Reply with specific EID (Paul)
5. NMR with Covering Prefix (boys)
Mary
Paul
Mary
Paul
Paul @ XTR-S
Paul @ XTR-S
XTR-W sub to Paul
Paul @ XTR-S
MS-W
MS-S
MS-E
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 23: MS Federation – Registrations/EID Moves - 3
LISP MS/MR
Border Router
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
11. Map-Notify
(Paul @ XTR-E)
9. Map-Notify (Paul @ XTR-E)
Mary
Paul
Mary
Paul
Paul @ XTR-S
Paul @ XTR-S
XTR-W sub to Paul
Paul @ XTR-S
Paul
8. Map-Register
Paul @ XTR-E
Paul @ XTR-E
10. Receive Map-Notify, update Mappings if present
Paul @ XTR-E
10. Receive Map-Notify, update Mappings if present
Paul @ XTR-E
12. Receive Map-Notify, update Map-cache
MS-W
MS-S
MS-E
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 24: MS Federation – Unknown Destinations – 1a
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
1. Map-Request
2. DB Miss, cache Map-Request
3. Send ECM Map Request to All Federation Peers
4. No DB Match:
Calculate Covering Prefix Generate NMR
4. No DB Match:
Calculate Covering Prefix Generate NMR
Mary
Peter
Mary
Paul
MS-W
MS-S
MS-E
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 25: MS Federation – Unknown Destinations – 2a
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
7. NMR (boys-E)
6. Received all NMRs:
Select/calculate covering prefix for Peter from the different NMRs.
Install/register Covering Prefix with empty RLOC set.in MS ??? Do this? or just send an NMR and hold this info in the Map-cache of the requestor?
Issue NMR
5. NMR with Covering Prefix (boys-S)
5. NMR with Covering Prefix (boys-E)
Mary
Peter
Mary
Paul
Boys-E @ Fwd-Native
MS-W
MS-S
MS-E
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 26: MS Federation Resiliency – Map-Request – 1b
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
1. Map-Request
2. DB Miss, cache Map-Request
3. Send ECM Map Request to All Federation Peers
4. DB Match:
Generate Reply
Optional: Add subs to Paul
4. No DB Match:
Calculate Covering Prefix Generate NMR
Paul @ XTR-S
MS-W sub to Paul
Mary
Paul
Mary
Paul
MS-W
MS-S
MS-E
Map-resolver anycast address
Map-requests are sent to MR anycast
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 27: MS Federation Resiliency – Map-Reply – 2b
LISP MS/MR
Border Router
Mapping System Federation
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
7. Map-Reply
6. Install/register Mapping for More specific EID (Paul
6.a. Instantiate subscription to Paul for XTR-W
5. Map Reply with specific EID (Paul)
5. NMR with Covering Prefix (boys)
Mary
Paul
Mary
Paul
Paul @ XTR-S
MS-W sub to Paul
Paul @ XTR-S
XTR-W sub to Paul
Paul @ XTR-S
MS-W
MS-S
MS-E
Need sync mechanism for 6 and 6a.
Send 2 NMR messages per area?
Other options/ideas …
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 28: MS Federation Resiliency – Registrations/EID Moves – 3b
LISP MS/MR
Border Router
LISP MS Federation
Underlay ASBR
XTR-S
XTR-W
XTR-E
11. Map-Notify
(Paul @ XTR-E)
9. Map-Notify (Paul @ XTR-E)
Mary
Paul
Mary
Paul
Paul @ XTR-S
Paul @ XTR-S
XTR-W sub to Paul
Paul @ XTR-S
Paul
8. Map-Register
Paul @ XTR-E
Paul @ XTR-E
10. Receive Map-Notify, update Mappings if present
Paul @ XTR-E
10. Receive Map-Notify, update Mappings if present
Paul @ XTR-E
12. Receive Map-Notify, update Map-cache
MS-W
MS-S
MS-E
Send register/notify messages to all MS/MR nodes.
Notes: All SP MS in the core handle the EIDs for the sites/regions that attach to them ( per our current proposal)
If an MS does not have information about a particular EID, it assumes it is in a different SP region. At that point the MS will forward the map-request to all other SP MS (in a way, this is a flat DDT). Only the authoritative MS will reply. This informs the requesting MS who the authoritative MS is and also provides the mapping.
The requesting MS will subscribe to the EID on the authoritative MS.
When the EID moves to a different region, the local MS will notify the border xTR. The border xTR will then register with the uberlay MS. If the EID was not previously present in the uberlay MS for that particular SP, the SP MS will try to resolve the old registration, upon resolution, it will notify the old SP MS of the move and the old SP MS can in turn notify its subscribers.

## Slide 29: LISP-SEC
ITR
1 ITR-OTK & Nonce
MR
MS
ETR
3 EID_Conf = Longest configured EID prefix match
4 HMAC-4(ITR-OTK, EID_Conf)
5 MS-OTK = KDF(ITR-OTK)
7 Map-Reply-7(EID-RLOC + HMAC-4)
8 HMAC-8(MS-OTK, Map-Reply-7)
10 Re-generate MS-OTK = KDF(ITR-OTK)
11 Verify hash HMAC-8 (authentication, integrity, anti-replay) ✔︎
12 Verify hash HMAC-4 (overclaim check) ✔
6 HMAC-4 +MS-OTK
(in ECM-Map-Request)
9 HMAC-8 (includes HMAC-4)
(in Map-Reply)
2 ITR-OTK
(in ECM-Map-Request)

## Slide 30: Federated LISP-SEC
ITR
1 ITR-OTK & Nonce
MR
MS1
MS2
3 EID_Conf = Longest configured EID prefix match
4 HMAC-4(ITR-OTK, EID_Conf)
5 MS-OTK = KDF(ITR-OTK)
7 Map-Reply-7(EID-RLOC + HMAC-4)
8 HMAC-8(MS-OTK, Map-Reply-7)
10 Re-generate MS-OTK = KDF(ITR-OTK)
11 Verify hash HMAC-8 (authentication, integrity, anti-replay) ✔︎
12 Verify hash HMAC-4 (overclaim check) ✔
6 HMAC-4 +MS-OTK
(in ECM-Map-Request)
9 HMAC-8 (includes HMAC-4)
(in Map-Reply)
2 ITR-OTK
(in ECM-Map-Request)
If there is a match in MS1  6, 7 and 8 take place in MS1 and 9 is sent from MS1