## Slide 1
LPWAN WG
WG Chairs:
Alexander Pelov <a@ackl.io>
Pascal Thubert <pthubert@cisco.com>
AD: Suresh Krishnan
<suresh@kaloom.com>
Webex

## Slide 2: Note Well
This is a reminder of IETF policies in effect on various topics such as patents or code of conduct. It is only meant to point you in the right direction. Exceptions may apply. The IETF's patent policy and the definition of an IETF "contribution" and "participation" are set forth in BCP 79; please read it carefully.
As a reminder:
By participating in the IETF, you agree to follow IETF processes and policies.
If you are aware that any IETF contribution is covered by patents or patent applications that are owned or controlled by you or your sponsor, you must disclose that fact, or not participate in the discussion.
As a participant in or attendee to any IETF activity you acknowledge that written, audio, video, and photographic records of meetings may be made public.
Personal information that you provide to IETF will be handled in accordance with the IETF Privacy Statement.
As a participant or attendee, you agree to work respectfully with other participants; please contact the ombudsteam (https://www.ietf.org/contact/ombudsteam/) if you have questions or concerns about this.
Definitive information is in the documents listed below and other IETF BCPs. For advice, please talk to WG chairs or ADs:
BCP 9 (Internet Standards Process)
BCP 25 (Working Group processes)
BCP 25 (Anti-Harassment Procedures)
BCP 54 (Code of Conduct)
BCP 78 (Copyright)
BCP 79 (Patents, Participation)
https://www.ietf.org/privacy-policy/ (Privacy Policy)

## Slide 3
Reminder: Minutes are taken * This meeting might be recorded ** Presence is logged ***
* Scribe; please contribute online to the minutes at: https://etherpad.tools.ietf.org/p/lpwan
** Recordings and Minutes are public and may be subject to discovery in the event of litigation.
*** From the Webex login

## Slide 4: Agenda bashing
[16:05] Administrivia [ 5min]
o Note-Well, Scribes, Agenda Bashing
o Status of drafts
[16:10] IETF 107 attendance / Covid-19 [10min]
[16:20] Rechartering in progress [10min]
[16:30] SCHC CoAP draft security section [15min]
[16:45] LoRaWAN IID [15min]
[ ] AOB [ QS ]

## Slide 5: WG progress

## Slide 6: IETF 107 Dates
2020-02-28 (Friday): Final agenda to be published.
2020-03-09 (Monday): Internet Draft submission cut-off (for all drafts, including -00) by UTC 23:59. Upload using the ID Submission Tool.
2020-03-09 (Monday): Standard rate registration and payment cut-off at UTC 23:59..
2020-03-11 (Wednesday): Draft Working Group agendas due by UTC 23:59. Upload using the Meeting Materials Management Tool.
2020-03-16 (Monday): Registration cancellation cut-off at UTC 23:59.
2020-03-16 (Monday): Revised Working Group agendas due by UTC 23:59. Upload using the Meeting Materials Management Tool.
2020-04-17 (Friday): Proceedings submission cutoff date by UTC 23:59. Upload using the Meeting Materials Management Tool.
2020-05-11 (Monday): Proceedings submission corrections cutoff date by UTC 23:59.

## Slide 7: Document advancement

## Slide 8: IETF 107 LPWAN Meeting

## Slide 9: COVID-19 vs IETF 107
Expect a low attendance
Many companies withdrawing
IETF official position unchanged so far
Cancelling your registration:
  Email to ietf-registrar@ietf.org
  You’ll get a 90% refund till March 16th

## Slide 10: Charter 2.0
https://datatracker.ietf.org/doc/charter-ietf-lpwan/
On agenda of IESG telechat tomorrow with enough positions to pass
  Perform SCHC Maintenance, including enabling SCHC mechanisms for Upper layer Protocols.
  Produce Standard Track documents to apply SCHC IPv6/UDP over the baseline technologies.
  Produce a Standards Track document to provide a mechanism to improve the reliability of delivering fragmented multicast packets.
  Produce a Standards Track document to define the generic data models to formalize the compression and fragmentation contexts.
  Produce a Standards Track document to enable operations, administration and maintenance (OAM) to the LPWAN device, including support for delayed or proxied liveness verification (Ping).

## Slide 11: draft-ietf-lpwan-schc-over-lorawan IID Computation
Editors:
Ivaylo Petrov (ivaylo@ackl.io)
Olivier Gimenez (ogimenez@semtech.com)
Interim meeting, Feb 19th, 2020

## Slide 12: New IID proposition
Device only know a « local » IP
SCHC gateway can solve conflicts
No need of out of band sharing of data
« Outside » adress can respect RFC7217

## Slide 13: Other IID Proposition
key = LoRaWAN AppSKey
cmac = aes128_cmac(key, devEui)
IID = cmac[0..7]
LoRa Alliance should accept to reuse AppSKey, then indroduce another key for this purpose later

## Slide 14: NAT like - Devices does not know its public IP address
Pros:
  Easy to implement
  Conflicts are resolved by the gateway itself
  No need to share the network 64 bits prefix beforehand
Cons:
  Some upper layer might require to know their public address. FTP and Skype might not be a real concern for LPWAN but it is an issue for DLMS, so it is a no go for me.

## Slide 15: Derive IID from AppSKey and DevEUI
Pros:
  Device has access to its public IP, no "NAT"
  Conflicts can be resolved by changing AppSKey with new join
Cons:
  Need to share network 64bits prefix beforehand. Mitigated as the rules also need to be shared so it can be part of the same mechanism
  Application need to define a way to create a new join

## Slide 16: Proposition
There is a small probability of IID collision in a network, if such event occur the IID can be changed by rekeying the device (ie: rejoin). The way the device is rekeyed is out of scope of this document and left to the implementation.
Idea: Can we allow a « special » ruleId for that ? Ex:
If a message is delivered with ruleId XXX, device must rejoin.
We might even go a step further and use this port for configuration:
Rejoin command
Network prefix
Rules, in few years 

## Slide 17
draft-ietf-lpwan-ipv6-static-context-hc status
Authors:
Laurent Toutain <Laurent.Toutain@imt-atlantique.fr>
Carles Gomez <carlesgo@entel.upc.edu>
Ana Minaburo <ana@acklio.io>
Dominique Barthel <dominique.barthel@orange.com>
Juan Carlos Zuniga <juancarlos.zuniga@sigfox.com>

## Slide 18: AUTH48 status
draft-ietf-lpwan-ipv6-static-context-hc-24 was sent off to RFC Editor on Dec 11th
Entered AUTH48 status on Jan 30th
  RFC number 8724 was assigned

## Slide 19: What did RFC Editor do?
Conversion from authors-provided xml v2 to xml v3
General editing work (punctuation, capitalization, spelling …)
  Changes can be seen at https://www.rfc-editor.org/authors/rfc8724-diff.html
Addressed the co-authors with 15 questions
  Some extremely easy to answer
  Some open-ended
Responded to authors’question about the title
  Is SCHC an initialism standing for "Static Context Header Compression" in that you would want to expand it as such in other places in the document or in future specifications (forgetting about its use in the title)? Or is it the case that SCHC is being used to represent a whole concept and should not really be expanded as “Static Context Header Compression” in this document or later specifications?
  If we just want a prettier title, we can just not expand it there and expand it in the Abstract etc….But if we are going for moving away from the 1:1 relationship, we would probably prefer to do that whenever it appears.

## Slide 20: What did the co-authors do?
Checked RFC Editor’s general editing work
  https://www.rfc-editor.org/authors/rfc8724-diff.html
  Thanks to Carles and Juan Carlos for thorough review!
  Reported “no mistake spotted, no disagreement with changes made (pending on-going discussions)”
Engaged dialog with RFC Editor on RFC title
Asked WG to vote about title and use/meaning of SCHC
Addressed the 15 questions
Threw in a few extra text improvements as a bonus
Submitted resulting xml file to RFC Editor Feb 25th
Changes visible at https://github.com/lp-wan/ip-compression/compare/AUTH48_initial...AUTH48_back_to_RFC_Editor

## Slide 21: Conclusions, next steps
Expecting feedback from RFC Editors anytime
  Another round of validation by co-authors?
RFC8724 officially published in a few days/weeks?

## Slide 22: Questions addressed

## Slide 23: Question 2: keywords
For use on https://www.rfc-editor.org/search

## Slide 24: Question 2: proposed keywords
<keyword>header compression</keyword>
<keyword>compression</keyword>
<keyword>fragmentation</keyword>
<keyword>static context</keyword>
<keyword>rule-based</keyword>
<keyword>LPWAN</keyword>
<keyword>LPWANs</keyword>
<keyword>low power</keyword>
<keyword>low-power</keyword>
<keyword>LoWPAN</keyword>
<keyword>LoWPANs</keyword>
<keyword>LLN</keyword>
<keyword>LLNs</keyword>
<keyword>IoT</keyword>
<keyword>Internet of Things</keyword>
<keyword>adaptation layer</keyword>
<keyword>WSN</keyword>
<keyword>sensor network</keyword>
<keyword>wireless sensor network</keyword>
<keyword>802.15.4</keyword>
<keyword>constrained network</keyword>
<keyword>constrained node</keyword>
<keyword>constrained-node network</keyword>

## Slide 25: Question 5: artwork on 72 characters
Separate branch in the repo, see https://github.com/lp-wan/ip-compression/compare/work_AUTH48...reduced_drawing_width
Comments?
Strong motivation for “RuleID” spelling over “Rule ID”

## Slide 26: Questions 15.x (terminology)
15.g: “fixed-sized”, “variable-sized”  “fixed-size”, “variable-size”
  DONE
15.e: “Field Descriptor” (25%) vs. “Field Description” (75%)
  “Field Descriptor” currently in minority, but I prefer it
  Question to co-authors
15.c: LPWAN Application Server (App)
  Still to be done

## Slide 27: Questions 15.x (terminology)
15.d: terms in Terminology section redefined in Section 7.1 (compression).
  Propose to remove as much as possible from Terminology section
  Up, Dwn, Bi,
  Still to be done

## Slide 28: Questions 15.x (terminology)
15.a: use abbreviation after it has been introduced
  Still to be done
  Nearly open-ended
15.b: “SCHC compression”, “LPWAN network”
  DONE for LPWAN network.
  To be done for “SCHC compression”
  See discussion on meaning of SCHC next.

## Slide 29: Questions 15.x (terminology)
15.f: consistent use of terms
  Network Infrastructure vs. Network infrastructure side
    DONE: “Network Infrastructure side”
  Rule ID vs. RuleID (no space in the latter)
    Currently 102 vs 15, yet I propose RuleID (artwork on 72 characters, openSCHC code)
  SCHC Compressor vs. SCHC compressor (& compressor vs. Compressor generally)
  Decompressor vs. decompressor
    Either “compressor” or “SCHC C/D”
  Compression Rule vs. compression Rule
    “compression Rule”
  Fragmentation/Reassembly vs. fragmentation/reassembly
  SCHC reassembler vs. SCHC Reassembler (and SCHC Reassmbly)
    Either “fragmentation/reassembly” or “SCHC F/R”
  WINDOW_SIZE vs. window size
    Still to be investigated

## Slide 30: nature/meaning of SCHC
Majority vote?
SCHC is an acronym for “Static Context Header Compression and fragmentation”

## Slide 31: Question 1: title of RFC
Before
  Static Context Header Compression (SCHC) and fragmentation for LPWAN, application to UDP/IPv6
After?

## Slide 32: Question 1: title of RFC
It seems LPWAN is out
  (B2+B4+B6)=3
Spelling out the acronym?
  (B3+B4)=6
Complementing the acronym?
  (B1+B1rev)=5;
Title will be capitalized in any case
“Generic Framework for Static Context Header Compression and Fragmentation (SCHC)”?

## Slide 33: ACK-on-Error, last tile
Made it explicit in RFC8724 that Profile can allow last tile to be sent as part of the All-1Fragment or a Regular Fragment, with the selection happening at runtime.
Schc-over-foo will assess if the benefit of dynamic selection is worth the computation cost, based on various parameters (header alignment, padding, out-of-order delivery, etc.). RFC8724 can’t reasonably list all potential cases and provide a mandate for each.
Added two MUSTs in RFC8724 so that, even if the Profile allows dynamic selection, the sender will ensure that the last tile is never received both as part of an All-1 Fragment and as part of a Regular Fragment, which would be an straightforward cause for abort.

## Slide 34: Thank you!

## Slide 35
AOB ?