## Slide 1: Encapsulation For MPLS Performance Measurement with Alternate Marking Method draft-cheng-mpls-inband-pm-encapsulation-03
Weiqiang Cheng chengweiqiang@chinamobile.com
Xiao Min xiao.min2@zte.com.cn
Tianran Zhou zhoutianran@huawei.com
Ximing Dong dxm@fiberhome.com
Yoav Peleg yoav.peleg@broadcom.com

## Slide 2: Summary of the -03 revision
Major changes are made as comment resolution:
  Change from Base Special Purpose Label to Extended Special Purpose Label
  Change the definition of Flow-ID Label’s TC and TTL, to make them compliant with RFC 3032
  Add text on comparison with MPLS In-situ OAM
  Add text on security consideration

## Slide 3: Flow-based PM Encapsulation
Composite Special Purpose Label (Extension Label 15 + Flow-ID Label Indicator) followed by a Flow-ID Label
Flow-ID Label is used as MPLS Flow Identification
TC and TTL of Flow-ID Label (Indicator) imitates that of Entropy Label (Indicator) [RFC 6790], except that TC of Flow-ID Label is recommended as color-marking field

## Slide 4: Measurement Objects
MPLS Performance Measurement Objects can be LSP, VPN or in-parallel LSP and VPN
LSP
VPN
LSP and VPN

## Slide 5: Comparison with In-situ OAM
Major differences between MPLS In-band PM and MPLS In-situ OAM:
  MPLS In-band PM doesn’t introduce any new header, whereas MPLS In-situ OAM needs new header, which means additional ASIC requirements
  MPLS In-band PM allows the network nodes to report the refined data (e.g. calculated performance metrics) associated with a specified flow, whereas MPLS In-situ OAM requests the network nodes to report the data (e.g. ingress interface and egress interface) associated with a specified packet

## Slide 6: Security Consideration
Major points on security consideration:
  The Flow-ID Label Indicator and Flow- ID Label MUST NOT be signaled and distributed outside one performance measurement domain
  To prevent packets carrying Flow-ID Label from leaking from one domain to another, the domain boundary nodes SHOULD deploy some policies (e.g., ACL) to filter out the packets

## Slide 7: Next steps
Ask for WG adoption