## Slide 1: draft-kompella-mpls-larp-07
Kireeti Kompella, Balaji Rajagopalan,
Reji Thomas
IETF Interim 2020 MPLS 01

## Slide 2: Use Cases for L-ARP
MPLS in the data center
L-ARP client is a compute server participating in an MPLS underlay
L-ARP server is a Top-of-Rack switch
MPLS in the access
L-ARP client is a D-SLAM/OLT/… with a label per subscriber
L-ARP server is a BNG device

## Slide 3: What’s Changed?
This work was done 5-6 years ago
  At the time, there was some interest from some niche corners for an MPLS underlay in data centers
  But most data centers and caching PoPs were using an MPLS overlay over an IP (GRE or UDP) underlay
Lately, there’s a resurgence of interest in an MPLS underlay in DCs, from the server, possibly using SPRING
While it’s common to run BGP or some form of an overlay SDN controller to the server, it’s not usual to run an IGP or LDP on the server
  So, what will the control plane for the MPLS underlay be?

## Slide 4: Recap on How L-ARP Works
Similar to “regular” ARP:
ARP client asks ARP server for a MAC address (hw type Ethernet) to reach an IPv4 address (protocol type IPv4)
L-ARP client X asks L-ARP server T1 for a label (hw type MPLS) to reach an IPv4 address Y (protocol type IPv4)
L-ARP server T replies with a label L1
L-ARP server advertises L-ARP client’s IP address to rest of MPLS network

## Slide 5: How L-ARP Works
X
T1
Y
T3
T2
Z
1
X asks T1 for a label to Y
T1 checks LFIB for entry to Y, say it gets label L2
T1 allocates label L1, inserts LFIB entry L1  L2
T1 sends an L-ARP reply of L1 to X
(*) T1 advertises [X, L3] to rest of MPLS network
4

## Slide 6: How L-ARP Works: notes
X asks T1 for a label to Y
T1 checks LFIB for entry to Y, say it gets label L2
T1 allocates label L1, inserts LFIB entry L1  L2
T1 sends an L-ARP reply of L1 to X
(*) T1 advertises [X, L3] to rest of MPLS network
Why does X ask for a label to Y?
Use case: X and Y have VMs or containers in the same VRF. X gets a BGP advert with next hop Y and wants an MPLS tunnel to Y
What if the entry L2 is a label stack (a la SPRING)?
T1 effectively creates a “binding SID” L1 for Y and sends this to X
How does T1 advertise [X, L3]?
This is a “proxy” advertisement on behalf of X; how it’s done depends on the protocol used
Note that X and Y don’t have to be in the same subnet. T1 is effectively implementing proxy ARP on behalf of Y

## Slide 7: Bidirectional MPLS Connectivity
X wants MPLS connectivity to Y
  X uses L-ARP to learn the label to use (L1) for sending to Y
  But with what label should X expect to receive packets?
T1 needs to allocate a label for X
  T1 advertised [X, L3] to the rest of the network; what should it swap L3 with to reach X?
  The label that X receives may be NULL (PHP) or not (UHP)
  If PHP, X doesn’t need to know; if UHP, maybe labeled DHCP?
X
Y
…
L1
?
L2
L3
T1

## Slide 8: Next Steps
Quite a bit of work was done on this, but quite a while ago
  This included a prototype implementation on Linux and on a ToR running Junos
Need to refresh much of that work
  Linux MPLS code has changed significantly
Some protocol details need to be ironed out
  Format: label(s), metric, ELC, …
  Multihomed servers (L-ARP clients)
  L-ARP in SPRING networks
  Restart and persistence of label allocation