## Slide 1: P2MP Transport Using Chain Replication in Segment Routing draft-shen-spring-p2mp-transport-chain-02
Yimin Shen, Jeffrey Zhang - Juniper Networks
Rishabh Parekh - Cisco Systems
Hooman Bidgoli - Nokia
Yuji Kamite - NTT Communications
MPLS WG Virtual Interim Meeting, May 2020

## Slide 2: Motivation – P2MP Transport
Single-point provisioning at root
Stateless core
P2P tunnels, one per leaf
No traffic optimization
P2MP tree
Max traffic optimization
Multi-point provisioning at root and branch nodes
Stateful core, with replication SIDs on branch nodes
P2MP chains
Certain level of traffic optimization
Single-point provisioning at root
Stateless core
ingress replication
controller-driven P2MP tree
chain replication

## Slide 3: P2MP Transport Using P2MP Chains
A P2MP chain is a tunnel that reaches multiple leaf nodes along the path.
Root node sends packets over a small set of P2MP chains.
Applies to all topologies. Benefits the most for certain topologies.
  Ring topology: One P2MP chain per multicast stream. Max optimization.
  Linear topology: Reduced number of tunnels across domains.
root
leaf 1
leaf 2
leaf 3
root
leaf 1
leaf 2
leaf 3
leaf 4

## Slide 4
P2MP Chain and Bud Segment
R
L2
T1
L1
T2
forwarding
local processing
local processing
transit leaf
tail-end leaf
replicate P → P1
forward P along a chain
process P1 locally
One tail-end leaf node, as a normal receiver.
One or more transit leaf nodes, each acting as a bud node, i.e. both transit and receiver.
Each transit leaf node is modeled as a bud segment, with a bud-SID.
A P2MP chain comprises a list of SIDs with transit leaf nodes represented by bud-SIDs.
bud segment :
forwarding
forwarding
forwarding
chain replication

## Slide 5: Example 1
R
R1
R2
R3
R4
R5
R6
R7
R8
L1
L2
L3
L4
A multicast stream to L1 ~ L4, using two chains:
  Red Chain to L1 and L2 takes the shortest path from R to L1, and from L1 to L2.
    SID list = {B1, N2}.
  Green Chain to L3 and L4 takes an explicit path from R to L3, and from L3 to L4.
    SID list = {A1, A2, A3, A4, A5, B3, A6, A7}
A1
A2
A3
A4
A5
A6
A7
bud-SID B1
node-SID N2
bud-SID B3
node-SID N4
A1 – A7: adj-SIDs

## Slide 6: Example 2
R
R1
R2
R3
R4
R5
R6
R7
R8
L2
L3
L4
Green multicast stream - green chain to L2, L3 and L4
  Explicit path from R to L2, and the shortest paths from L2 to L3, and from L3 to L4.
  P2MP chain SID list = {A1, A2, A3, B2, B3, N4}
Red multicast stream - red chain to L2 and L4, but not L3
  Explicit path from R to L2, and the shortest path from L2 to L4 (L3 is a pure transit router).
  P2MP chain SID list = {A1, A2, A3, B2, N4}
A1
A2
A3
A4
A5
A6
A7
bud-SID B2
bud-SID B3
node-SID N4
A1 – A7: adj-SIDs

## Slide 7: Example 3
Green multicast stream
  root = A, leaves = {B, D, F, H}
  SID list = {bud-SID-B, bud-SID-D, bud-SID-F, node-SID-H}
Red multicast stream
  root = B, leaves = {C, F, G}
  SID list = {bud-SID-C, bud-SID-F, node-SID-G}
F is a leaf node of both streams.
  bud-SID-F appears in both P2MP chains.
A
B
C
D
E
F
G
H

## Slide 8: Bud Segments
Nodal segments
  Two per node: one for SR-MPLS, and one for SRv6
Global segments
  Bud-SIDs are allocated from SRGB
Routable segments, via shortest paths
  Can also be used with adj-SIDs to construct explicit paths
Sharable by all multicast streams
Other use cases, e.g. traffic mirroring, traffic monitoring, etc.

## Slide 9: General Forwarding Flow of Bud Segment
Replicate P → P1
Perform Next on bud-SID;
Forward P based on next SID
Perform a sequence of Next on all P2MP chain SIDs;
Process P1 locally
P
P1
Packet P
Active SID == bud-SID

## Slide 10
To process P1 locally, must pop all P2MP chain labels.
If there is a service label, root inserts an “End-of-Chain” label between service label and P2MP chain labels.
EoC is a new Extended Special-Purpose Label, as <XL = 15, EoC>.
Replicate P → P1
Pop bud-SID label;
Forward P based on lookup of next label
Pop until EoC or all labels are popped;
Process P1 locally
P
P1
Packet P
Top label == bud-SID label
service label
EoC
XL (15)
SID label Y
SID label X
bud-SID label
SID label Y
SID label X
bud-SID label
payload
payload
pop
pop
Bud Segment Forwarding Flow in SR-MPLS

## Slide 11: Example of EoC Label
R
R1
R2
R3
R4
R5
R6
R7
R8
L1
L2
L3
L4
Green chain’s SID list: {A1, A2, A3, A4, A5, B3, N4} . Service label is X.
  Sub-path from R to L3 is not the shortest path, hence using adj-SIDs followed by L3’s bud-SID.
  Sub-path from L3 to L4 is taking the shortest path, hence using L4’s node-SID.
R sends a service packet P with {A2, A3, A4, A5, B3, N4, XL, EoC, X}.
L3:
  Receives P with {B3, N4, XL, EoC, X}, and replicates it to generate P1.
  For P, pops B3, and forwards the packet based on N4, with outgoing {N4, XL, EoC, X}.
  For P1, pops B3, N4, XL, and EoC, and processes the packet with {X} locally.
L4 receives P with {N4, XL, EoC, X}, pops N4, XL, and EoC, and processes it.
A1
A2
A3
A4
A5
A6
A7
bud-SID B1
node-SID N2
bud-SID B3
node-SID N4
A1 – A7: adj-SID labels
X: service label

## Slide 12: Bud Segment Forwarding Flow in SRv6
Packet: IPv6 header + SRH (P2MP chain SIDs) + IP/L2 header + …
Replicate P → P1
Adjust SRH;
Forward P based on next SID
Remove outer IPv6 header and SRH;
Process P1 locally
P
P1
Packet P
DA == bud-SID

## Slide 13: Path Computation for P2MP Chain
P2P path computation can be extended to serve P2MP chain computation.
  Max hop count per chain
    Maximum delay allowed for a packet to accumulate before reaching a tail-end leaf node.
  Max length of SID list
    Max number of SIDs that a root node may apply to a packet.
    Typically a limit of forwarding hardware.
  Max number of leaf nodes per chain
  Max number of hops between consecutive leaf nodes
  Max number of times a link or node can be traversed per chain
Leaf groups
  A leaf group is an ordered list of loose hops.
  Each chain covers the leaf nodes of a given group.

## Slide 14: Provisioning and Distribution
Static configuration
Protocol extensions for advertisement – Similar to node segments
  ISIS
  OSPF
  BGP-LS

## Slide 15: Next Steps
Ask for review and comments in both SPRING WG and MPLS WG.
Request an early allocation of End-of-Chain Label from the Extended Special Purpose Label Registry by IANA.

## Slide 16: Thank You