## Slide 1: YANG and Netconf usage in 3GPP
Balázs Lengyel
2020-04-01
Balázs Lengyel
BDGS
2020-04-01

## Slide 2: 3GPP way of working
Stage 1 specifications – High level requirements
Stage 2 Information Models
  Defines functionality
  Not detailed or precise enough as interface definition
Stage 3 Solution Sets
  Just a mapping of Stage 2, strictly adhere to Stage 2
  Precise all details
  YANG/Netconf
  JsonSchema/OpenApi
  XMLSchema

## Slide 3: 3GPP Models
UML model in MS Word documents
  Objects & Attributes
  Containment/Inheritances as figures
  Attribute properties as plain English

## Slide 4: Mapping an Object Oriented Model to YANG
Multiple ways to do it
3GPP TS 32.160 defines mapping
Object -> grouping used inside a list
Attribute -> leaf, leaf-list or lists
  structured attribute may have many levels inside -> list
Attributes are collected under a YANG container to differentiate from child objects
Inheritance-> ClassBGrouping uses ClassAGrouping
  Inherits attributes
  Does not inherit containment,
    Somewhat rare
    handled case-by-case

## Slide 5: Example
module _3gpp-common-managed-element {
grouping Abstract_Class_Grp {
leaf dnPrefix {...}
leaf locationName { type string; }
}
grouping ManagedElementGrp {
uses Abstract_Class _Grp;
leaf swVersion {...}
}
list ManagedElement {
key id;
uses top3gpp:Top_Grp;
container attributes {
uses ManagedElementGrp;
} }
//contained class
list MeasurementControl {...}
}
ManagedElement class inherits from Abstract_Class
ManagedElement class contains MeasurementControl class

## Slide 6: Containment Issues
Simple case: ObjectA contains ObjectB is simple list in list
Recursive containment mapped to a list of references like in ietf-interface
Containment via inheritance – a nasty issue
  Handled case-by-case

## Slide 7: Addressing
Addressing via Distinguished Names
  DNs are embedded in many existing management systems
  DNs are included in a Network level hierarchy
  DNs can interwork with solutions in JsonSchema or Xsd solution set
  Does not include namespace
  Allows single key only
  Cannot be used for IETF models
  DNs are long – leafref are short, instance-identifiers are longer
  DNs don’t enforce referential integrity (require-instance)
  DNs address only an object instance not an attribute
/ex:system[ex:id=’1’]/ex:user[ex:id=’fred’]
DN: system=1, user=fred

## Slide 8: Modeling differences
3GPP Default means initial value
  Only affects data when the containing Object is created/Replaced
3GPP Invariant attributes
  Attribute can only be changed/set when the containing Object is created/Replaced
Write-Only data
System-Created Objects
  The list entry itself is read-only but attributes, contained objects below are configurable
Handled as YANG extensions
We don’t have these in YANG, we might not like them, but never forget -> 3GPP and mobile networks do work

## Slide 9: Modeling work
3GPP TS 28.623
  https://portal.3gpp.org/desktopmodules/Specifications/SpecificationDetails.aspx?specificationId=1542
  10 Common YANG modules
  top, managed-element, common-types, yang-extensions, etc.
3GPP TS 28.541
  https://portal.3gpp.org/desktopmodules/Specifications/SpecificationDetails.aspx?specificationId=3400
  58 YANG modules
  5G Core Network, 5G RAN NRM

## Slide 10: Methodology
YANG Modules stored in MS Word
  Lot of problems
  Can’t validate them
  Copy-Paste errors
  We have a GitLab copy, but that’s unofficial
  Trying to make GitLab the authoritative source – slow process
Full set of modules released every 3-6 months,
  major release every 18 months
Backwards compatibility is not considered as important

## Slide 11: Protocol
3GPP TS 28.532 specifies Netconf as protocol to use
YangPush may be used for data change notifications,
  but we are late big problem