## Slide 1
Updated YANG Schema Selection
draft-ietf-netmod-yang-ver-selection
NETMOD WG
April 2020
Presentation Authors: Jason Sterne & Joe Clarke
Presenting: Jason Sterne

## Slide 2: Scope of this presentation
This draft is presented in both NETMOD and NETCONF
The full set of versioning drafts are presented in NETMOD
Issues, questions, and discussion related to all other drafts should occur in NETMOD

## Slide 3: Recap: YANG Schema Selection draft-ietf-netmod-yang-ver-selection
Optional functionality (primarily on the server, minimal for the client):
  Servers can support and advertise multiple schema versions (‘schema-set’), e.g.
    vendor-modules@6.0.1
    vendor-modules@5.2.3
  clients can select which schema-set to use
Default schema-set is used if client doesn’t request anything
Schema-sets are comprised of YANG packages

## Slide 4: Changes since -01 draft (IETF 106)

## Slide 5: Changes since -01 draft (IETF 106)
1. Design simplified by removing the select-schema-sets RPC:
  NETCONF clients disconnect and reconnect to use a new schema-set
  RESTCONF clients use the schema-set name in each request URI
2. added another use case to the abstract:
  It can also be used to allow clients to select between YANG schema defined by different organizations

## Slide 6: Changes cont.
3. Clarified the basic unit of selection called ‘schema-set’:
schema-set: a named set of datastore schemas for supported datastores, where every datastore schema is specified as a union of compatible YANG packages.
Each schema-set has a unique name that identifies the schema-set during schema selection protocol operations, e.g., it is used in both the NETCONF capabilities exchange and the RESTCONF path.
schema-set: my-example@2.0.0
datastore: running
datastore: candidate
datastore: dynamic-12
datastore: operational
package: vendor-cfg 3.1.2
package: vendor-cfg 2.5.2
package: vendor-cfg 3.1.2
package: vendor-cfg 2.5.2
package: vendor-cfg 3.1.2
package: vendor-cfg 2.5.2
package: vendor-custom-dynamic-stuff 1.3.0
package: vendor-other-state 3.0.1
package: vendor-dynamic-state 1.3.0

## Slide 7: Changes cont.
schema-sets :
schema-sets supported by the server are available in the operational state datastore (DS) at:
  /schema- set-selection/schema-set
schema-sets that are selectable by a client are available in the operational state DS at:
  /schema- set-selection/selectable
module: ietf-schema-selection
rw schema-set-selection!
+--rw selectable* -> /schema-set-selection/schema-set/name
+--rw default -> /schema-set-selection/selectable
…
+--ro schema-set* [name]
+--ro name string
…
| +--ro package* [name version]
| +--ro name -> /pkgs:packages/package/name
| +--ro version leafref
Server optionally populates the ‘selectable’ list in the oper state DS with some schema-sets
Configurable 'selectable' leaf-list defines which schema-sets may be selected by clients (replaces the server populated list)
Configurable 'default' leaf defines the schema-set used by clients that do not select a schema-set
Server populates the schema-set list with all supported schema-sets

## Slide 8: Changes cont.
4. Removed the configuration of separate RESTCONF protocol instances
For RESTCONF, schema-sets are chosen via use of their name in the request URI. Clients select the desired schema-set by choosing the corresponding RESTCONF root resource. This is done by appending the schema-set name to the RESTCONF API root [RFC8040]. NMDA example:
  /restconf/schema/vendor-schema@X.Y.Z/ds/ietf-datastores:running
  refers to the Running configuration datastore

## Slide 9: Changes cont.
5. Objective added: “To allow considerable freedom for server implementations to decide how to implement schema selection, and choose the schema selection capabilities they support.”
6. Clarification: “The selection of a schema-set by a client MUST NOT change the behaviour of the server experienced by other clients. For example, the get-data response to one client MUST be the same before and after another client selects a schema-set.”

## Slide 10: Discussion Topics

## Slide 11: Discussion Topics cont.
GitHub Issue #40: Decide whether to specify exactly when a session is closed if a schema-set is removed from the selectable list
  any NETCONF sessions that were using that schema-set are disconnected, or
  any NETCONF sessions that were using that schema-set remain connected, but no new NETCONF sessions can use the schema-set that was removed from the 'selectable' leaf-list. If the server can only support a limited number of schema-sets in parallel, and the maximum number of schema-sets are currently in use, and a new NETCONF session attempts to use a new valid schema-set (exceeding the maximum number of parallel schema-sets), then TBD (disconnect those old NETCONF sessions that are using a schema-set that was removed from 'selectable', or block the new NETCONF session?)
  Reject the new config if there are active client sessions
To keep things simpler, DT prefers option 1. See proposed new text on backup slide.
Option 3 means blocking config because of state, and stops an admin from being able to remove a schema-set. Not preferred.

## Slide 12: Discussion Topics cont.
GitHub Issue #41: Should the version number be embedded in the schema-set name?
Pros of having a separate version:
  Clean split between name and version
  Matches packages
Cons of having a separate version:
  For custom schema, it forces clients to also specify a version, even when it might not be meaningful
  It makes the selectable list and the default reference to schema-sets a bit more awkward rather than a simple leaf-list and leaf
  It potentially forces a more awkward encoding (e.g. %40) for the schema name in RESTCONF paths, since ‘@’ would always be there and not removable (e.g. by a custom schema-set definition) – does this matter?
  If the schema selection is between different schema families (e.g. native vs ietf vs open-config) then a name may be sufficient, depending on whether the schema-sets are published as offline definitions or not

## Slide 13: Discussion Topics cont.
Where does this document live?
Version selection defines updates to NETCONF (capabilities exchange flow) and RESTCONF (path composition). Should this document (or part of it) move to the NETCONF WG?
Should the document split to cover:
  protocol changes (two documents: NETCONF and RESTCONF) and
  model updates (another document, perhaps back in NETMOD)?
DT proposes this to remain as one document in Netconf

## Slide 14: Discussion Topics
GitHub Issue #36: The schema-sets selectable by a client are available in the ‘selectable’ list in the oper. state datastore (DS). How do explicitly configured ‘selectable’ schema-sets interact with system populated schema-sets ?
  The list of configured selectable schema-sets, if not empty, replaces the list of system populated schema-sets in the ‘selectable’ list in the oper. state DS
  The list of configured selectable schema-sets is merged with the list of system populated schema-sets in the ‘selectable’ list in the oper. state DS
Configured custom schema-sets are automatically placed in the schema-set ro list, but must be manually added to the ‘selectable’ list
DT recommendation is option 1 (i.e., the client-configured schema-sets replace the system populated ones)
An operator needs to be able to remove default system populated items from the available ‘selectable’ list

## Slide 15: Discussion Topics cont.
Issue raised during adoption call: This solution is complex and may be impossible to implement in certain scenarios
  Useful to allow for a server to support multiple schema with minimal impact on clients (i.e., clients do not need to immediately update)
  Part of complete solution, but optional for servers
  Lots of flexibility in the draft for different server capabilities
Example use cases:
An NBC change needs to occur (e.g. bug fix, or extending functionality) that causes a leaf to change type but there is a strong desire to keep the same name (e.g. something basic like "interface" or "address"). We can't use a "status deprecated" approach to support the old functionality in this case.
The ability for a client to specify (and a server to advertise & limit) which data models (3rd party vs proprietary) it wants to use for interactions with the server.

## Slide 16: Backup

## Slide 17: Changes cont.
7. Repartitioned the YANG model functionality.
module: ietf-schema-selection
rw schema-set-selection!
+--rw selectable* -> /schema-set-selection/schema-set/name
+--rw default -> /schema-set-selection/selectable
+--rw custom* [name] {custom-schema-set}?
| +--rw name string
| +--rw description? string
| +--rw included-schema*
| -> /schema-set-selection/schema-set/name
+--ro schema-set* [name]
+--ro name string
+--ro partial? empty
+--ro datastore* [name]
| +--ro name ds:datastore-ref
| +--ro read-only? empty
| +--ro package* [name version]
| +--ro name -> /pkgs:packages/package/name
| +--ro version leafref
| +--ro checksum? leafref
+--ro selectable-with*
| -> /schema-set-selection/schema-set/name
+--ro custom-selectable! {custom-schema-set}?
+--ro combinable-with*
-> /schema-set-selection/schema-set/name
Control which subset of the server supported schema-sets are advertised and allowed for selection
Optionally add custom schema-sets (by renaming or combining other supported schema-sets)
Indicate a schema isn't complete on its own (e.g. igp) and would generally be bundled into a custom schema-set
For datastores that are normally writable, indicates that the datastore cannot be written using this schema-set. E.g., if <running> was a supported datastore then it could be read, but not written.
Leafref to package module instead of yang library
Checksum added per package
Indications of which other packages this can be selected with and/or combined with

## Slide 18: Discussion Topics cont.
GitHub Issue #40 cont.
Proposed new text for option 1:
  If a server supports multiple schema-sets in parallel, but a client removes a schema-set that is in use on a NETCONF session from the 'selectable' leaf-list, then any NETCONF sessions that were using the removed schema-set are disconnected.
  If the server can only support a limited number of schema-sets in parallel, and the maximum number of schema-sets are currently in use by active NETCONF sessions (or RESTCONF requests), and a new NETCONF session attempts to connect and use a new valid schema-set (exceeding the maximum number of parallel schema-sets), then the new NETCONF session is disconnected.
  If the server can only support a limited number of schema-sets in parallel, and the maximum number of schema-sets are currently in use by active NETCONF sessions (or RESTCONF requests), and a new RESTCONF request attempts use a new valid schema-set (exceeding the maximum number of parallel schema-sets), then the RESTCONF request fails and the server returns an error.
  Servers SHOULD avoid a situation whereby a new NETCONF session is unable to connect without specifying a schema-set (i.e. connecting and using the default schema-set SHOULD always be possible).
  Servers SHOULD avoid a situation whereby a RESTCONF request that doesn’t specify a schema-set fails due to the lack of availability of a default schema-set.