## Slide 1: Transport Slice Intent <draft-contreras-nmrg-transport-slice-intent-00>
L.M. Contreras (Ed.) (Telefónica)
P. Demestichas (Ed.), K. Tsagkaris, K. Trichias, V. Foteinos, T. Gkiolias (WINGS)
NMRG interim meeting, April 2020
This work has been (partially) funded by the EU H2020 5G-EVE Project (grant no. 815074)

## Slide 2: Background
Existing work on the application of Intent-Based mechanisms for Network Slicing
  See presentation “IBN for network slicing in 5G-EVE project” at IETF#106 Singapore meeting
Extension of the work to the particular case of the transport Network
  Influenced by the work in TEAS NS DT on transport slicing
  Narrow down focus to IETF scope

## Slide 3: Transport slices
On-going work in TEAS WG NS DT
  [1] draft-nsdt-teas-transport-slice-definition-01
  [2] draft-nsdt-teas-ns-framework-02
From [1]: “A transport slice is built based on a request from a higher operations system. The interface to higher operations systems should express the needed connectivity in a technology-agnostic way, and slice customers do not need to recognize concrete configurations based on the technologies (e.g being more declarative than imperative). The request to instantiate a transport slice is represented with some indicators such as SLO, and technologies are selected and managed accordingly.”
IB approach seems adequate for the provision of transport network slices with appropriate level of abstraction towards the transport network control and management artifacts

## Slide 4: E2E slice nanagement and control

## Slide 5: Transport Slice Intent
draft-irtf-nmrg-ibn-concepts-definitions-01: “Intent is a higher-level declarative goal that operates at the level of a network and services it provides, not individual devices. It is used to define outcomes and high-level operational goals, without the need to enumerate specific events, conditions, and actions”
Foundation for transport slice intents → GSMA Generic Slice Template
  NG.116 (Generic network Slice Template (GST): Version 2 Released on October 2019.
  The purpose of NG.116 is to assist network slice provides to map the use cases of network slice customers into generic attributes.
  New attributes are still being defined and added.

## Slide 6: Transport Slice Intents Intent lifecycle according to draft-irtf-nmrg-ibn-concepts-definitions-01
[3] draft-contreras-teas-slice-nbi-01
Processing of Generic Slice Template
(transport concerns)
Request to the Transport Slice Controller
GST-like
attributes
TSC NBI
[3]

## Slide 7: Mechanisms for translating transport slice intents
A well defined set of context aware attributes should be agreed upon
  This will allow unambiguous instantiation of Intent driven transport slice
A combination of a structured set of attributes (communicated between an IBN and an upper layer system) together with user input would allow an IBN to have intent modeled and reason about its completeness/validity.
Translation approaches and interaction with the upper systems might benefit from Natural Language Processing (NLP) technics
  NPL technics can enable high level expression of requirements found missing
  Translation approaches and interaction with higher layers can benefit from AI/ML mechanisms

## Slide 8: Next steps
Keep developing IB capabilities for transport slices
Keep analysing GST attributes and their impact in transport
Align with progress in TEAS NS DT
Request comments and inputs for new versions
Prepare new version for Madrid meeting (IETF#108)
  J. Tantsura joined as co-author

## Slide 9: Backup - Generic Slice Template Attributes (examples)
Maximum Supported Packet size
Downlink Throughput per user
Uplink Throughput per user
Downlink Throughput per slice
Uplink Throughput per slice
Reliability
Device velocity
Radio spectrum
Delay Tolerance
Synchronicity
Positioning support
Supported Access technologies
Multicast
Support for non-IP traffic
Deterministic communication
Terminal number and density
Performance Monitoring
Real-time Charging/Billing
User Management openness
Performance prediction
Location based message delivery
Security Model
Isolation
Custom user plane termination
Session and Service Continuity
Root cause Investigation
Coverage